Culverts v9.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

Data	3

Data	3

Results	4

Regular check	4

Maximum velocity check	5

Maximum capacity check	6

Data	7

Data	7

Results	8

Regular check	8

Maximum velocity check	10

Maximum capacity check	11

# Project information

# Data

| Friction type | Manning |
| --- | --- |

## Data

| Name | Circular |
| --- | --- |
| Location | SR2 at Station 2+507 |
| Culvert type | Circular |
| Material | Aluminum |
| Diameter (m) | 0.800 |
| Number of culverts | 1 |
| Friction factor | 0.0160 |
| Flow rate (m³/s) | 0.600 |
| Entrance | Groove end projecting |
| Maximum allowable headwater (m) | 0.000 |
| Local entrance losses | 0.500 |
| Culvert Profile |

| Maximum elevation (m) | 6.100 |
| --- | --- |
| Left slope | 0.00000 |
| Right slope | 0.00000 |
| Station 1 (m) | 0.000 |
| Inlet elevation 1 (m) | 4.600 |
| Station 2 (m) | 21.500 |
| Outlet elevation 2 (m) | 4.300 |

# Results

## Regular check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 5.365 |
| Inlet control HW elevation (m) | 5.270 |
| Outlet control HW elevation (m) | 5.365 |
| Headwater depth / height (m/m) | 0.957 |
| Discharge (m³/s) | 0.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 4.600 |
| Downstream invert (m) | 4.300 |
| Length (m) | 21.500 |
| Constructed slope (m/m) | 0.01395 |
| HYDRAULIC PROFILE |
| Froude number | 1.4477 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.387 |
| Depth downstream (m) | 0.470 |
| Critical depth (m) | 0.470 |
| Velocity (m/s) | 2.49 |
| Wet area (m²) | 0.2410 |
| Wet perimeter (m) | 1.231 |
| Linear losses (m) | 0.292 |
| Energy losses (m) | 0.765 |
| Submerged inlet | No |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0078 |
| M | 2.0000 |
| C | 0.0379 |
| Y | 0.6900 |
| Total area (m²) | 0.5027 |
| Flow depth at inlet (m) | 0.670 |
| Inlet control HW elevation (m) | 5.270 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 6.100 |
| Overflow occurs | No |

## Maximum velocity check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 5.772 |
| Inlet control HW elevation (m) | 5.270 |
| Outlet control HW elevation (m) | 5.772 |
| Headwater depth / height (m/m) | 1.465 |
| Discharge (m³/s) | 0.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 4.600 |
| Downstream invert (m) | 4.300 |
| Length (m) | 21.500 |
| Constructed slope (m/m) | 0.01395 |
| HYDRAULIC PROFILE |
| Froude number | 1.9777 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.329 |
| Depth downstream (m) | 0.470 |
| Critical depth (m) | 0.470 |
| Velocity (m/s) | 3.08 |
| Wet area (m²) | 0.1948 |
| Wet perimeter (m) | 1.114 |
| Linear losses (m) | 0.447 |
| Energy losses (m) | 1.172 |
| Submerged inlet | No |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0078 |
| M | 2.0000 |
| C | 0.0379 |
| Y | 0.6900 |
| Total area (m²) | 0.5027 |
| Flow depth at inlet (m) | 0.670 |
| Inlet control HW elevation (m) | 5.270 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 6.100 |
| Overflow occurs | No |

## Maximum capacity check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 5.270 |
| Inlet control HW elevation (m) | 5.270 |
| Outlet control HW elevation (m) | 5.242 |
| Headwater depth / height (m/m) | 0.838 |
| Discharge (m³/s) | 0.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 4.600 |
| Downstream invert (m) | 4.300 |
| Length (m) | 21.500 |
| Constructed slope (m/m) | 0.01395 |
| HYDRAULIC PROFILE |
| Froude number | 1.2685 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.415 |
| Depth downstream (m) | 0.470 |
| Critical depth (m) | 0.470 |
| Velocity (m/s) | 2.28 |
| Wet area (m²) | 0.2632 |
| Wet perimeter (m) | 1.286 |
| Linear losses (m) | 0.245 |
| Energy losses (m) | 0.642 |
| Submerged inlet | No |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0078 |
| M | 2.0000 |
| C | 0.0379 |
| Y | 0.6900 |
| Total area (m²) | 0.5027 |
| Flow depth at inlet (m) | 0.670 |
| Inlet control HW elevation (m) | 5.270 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 6.100 |
| Overflow occurs | No |

# Data

| Friction type | Manning |
| --- | --- |

## Data

| Name | Arch |
| --- | --- |
| Location | Station 0+096.43 |
| Culvert type | Arch |
| Material | Concrete |
| Span (m) | 6.000 |
| Rise (m) | 3.000 |
| Number of culverts | 1 |
| Friction factor | 0.0160 |
| Flow rate (m³/s) | 8.600 |
| Entrance | Groove end projecting |
| Maximum allowable headwater (m) | 0.000 |
| Local entrance losses | 0.200 |
| Culvert Profile |

| Maximum elevation (m) | 42.150 |
| --- | --- |
| Left slope | 0.00000 |
| Right slope | 0.00000 |
| Station 1 (m) | 0.000 |
| Inlet elevation 1 (m) | 28.200 |
| Station 2 (m) | 54.000 |
| Outlet elevation 2 (m) | 26.900 |

# Results

## Regular check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 1.#INF |
| Inlet control HW elevation (m) | 30.234 |
| Outlet control HW elevation (m) | 1.#INF |
| Headwater depth / height (m/m) | 1.#INF |
| Discharge (m³/s) | 8.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 28.200 |
| Downstream invert (m) | 26.900 |
| Length (m) | 54.000 |
| Constructed slope (m/m) | 0.02407 |
| HYDRAULIC PROFILE |
| Froude number | 2.3935 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.332 |
| Depth downstream (m) | 0.594 |
| Critical depth (m) | 0.594 |
| Velocity (m/s) | 4.33 |
| Wet area (m²) | 1.9872 |
| Wet perimeter (m) | 6.665 |
| Linear losses (m) | 1.#INF |
| Energy losses (m) | 1.#INF |
| Submerged inlet | Yes |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0045 |
| M | 0.7500 |
| C | 0.0317 |
| Y | 0.6900 |
| Total area (m²) | 0.0000 |
| Flow depth at inlet (m) | 2.034 |
| Inlet control HW elevation (m) | 30.234 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 42.150 |
| Overflow occurs | No |

## Maximum velocity check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 1.#INF |
| Inlet control HW elevation (m) | 30.234 |
| Outlet control HW elevation (m) | 1.#INF |
| Headwater depth / height (m/m) | 1.#INF |
| Discharge (m³/s) | 8.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 28.200 |
| Downstream invert (m) | 26.900 |
| Length (m) | 54.000 |
| Constructed slope (m/m) | 0.02407 |
| HYDRAULIC PROFILE |
| Froude number | 3.1352 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.277 |
| Depth downstream (m) | 0.594 |
| Critical depth (m) | 0.594 |
| Velocity (m/s) | 5.18 |
| Wet area (m²) | 1.6610 |
| Wet perimeter (m) | 6.555 |
| Linear losses (m) | 1.#INF |
| Energy losses (m) | 1.#INF |
| Submerged inlet | Yes |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0045 |
| M | 0.7500 |
| C | 0.0317 |
| Y | 0.6900 |
| Total area (m²) | 0.0000 |
| Flow depth at inlet (m) | 2.034 |
| Inlet control HW elevation (m) | 30.234 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 42.150 |
| Overflow occurs | No |

## Maximum capacity check

| SUMMARY |
| --- |
| Allowable HW elevation (m) | 0.000 |
| Computed headwater elevation (m) | 1.#INF |
| Inlet control HW elevation (m) | 30.234 |
| Outlet control HW elevation (m) | 1.#INF |
| Headwater depth / height (m/m) | 1.#INF |
| Discharge (m³/s) | 8.600 |
| Tailwater elevation (m) | 0.300 |
| Control type | Inlet |
| GRADES |
| Upstream invert (m) | 28.200 |
| Downstream invert (m) | 26.900 |
| Length (m) | 54.000 |
| Constructed slope (m/m) | 0.02407 |
| HYDRAULIC PROFILE |
| Froude number | 2.1420 |
| Flow regime | Supercritical |
| Normal depth (m) | 0.357 |
| Depth downstream (m) | 0.594 |
| Critical depth (m) | 0.594 |
| Velocity (m/s) | 4.02 |
| Wet area (m²) | 2.1392 |
| Wet perimeter (m) | 6.716 |
| Linear losses (m) | 1.#INF |
| Energy losses (m) | 1.#INF |
| Submerged inlet | Yes |
| Submerged outlet | No |
| INLET CONTROL |
| K | 0.0045 |
| M | 0.7500 |
| C | 0.0317 |
| Y | 0.6900 |
| Total area (m²) | 0.0000 |
| Flow depth at inlet (m) | 2.034 |
| Inlet control HW elevation (m) | 30.234 |
| OVERFLOW |
| Maximum allowable HW elevation (m) | 0.000 |
| Maximum geometric height (m) | 42.150 |
| Overflow occurs | No |