River Flow v9.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Project information	4

General data	4

Model preferences	4

Time Steps	4

Design	4

Sections	4

J 1	4

J 2	4

J 3	4

J 4	4

J 5	5

J 6	5

J 7	5

J 8	5

J 9	5

J 10	5

J 11	5

J 12	6

J 13	6

J 14	6

J 15	6

Conduits	6

C1	6

C2	6

C3	6

C4	7

C5	7

C6	7

C7	7

C8	7

C9	7

C10	7

C11	7

C12	8

C13	8

C14	8

Inflows: Direct	8

Section: J 1	8

Time Patterns	8

TP1	8

TP 2	9

Results	9

Node results	9

00:15 28/07/2010	9

00:30 28/07/2010	10

00:45 28/07/2010	10

01:00 28/07/2010	11

Link results	11

00:15 28/07/2010	11

00:30 28/07/2010	12

00:45 28/07/2010	12

01:00 28/07/2010	12

System results	13

# Project information

# General data

## Model preferences

| Flow units | m³/s |
| --- | --- |
| Routing method | Steady flow |

## Time Steps

| Routing step (sec) | 00:00:05 |
| --- | --- |

## Design

| Kinematic viscosity (m²/s) | 0.00000131 |
| --- | --- |
| Density (kg/m³) | 999.75 |

# Sections

## J 1

| X-Coordinate | 491245.16 |
| --- | --- |
| Y-Coordinate | 4523630.98 |
| Constituent | Flow |
| Inflow (m³/s) | 15 |
| Offset elevation (m) | 0.000 |

## J 2

| X-Coordinate | 491230.68 |
| --- | --- |
| Y-Coordinate | 4523634.91 |
| Offset elevation (m) | 0.000 |

## J 3

| X-Coordinate | 491216.2 |
| --- | --- |
| Y-Coordinate | 4523638.83 |
| Offset elevation (m) | 0.000 |

## J 4

| X-Coordinate | 491201.32 |
| --- | --- |
| Y-Coordinate | 4523642.86 |
| Offset elevation (m) | 0.000 |

## J 5

| X-Coordinate | 491186.53 |
| --- | --- |
| Y-Coordinate | 4523645.34 |
| Offset elevation (m) | 0.000 |

## J 6

| X-Coordinate | 491171.73 |
| --- | --- |
| Y-Coordinate | 4523647.82 |
| Offset elevation (m) | 0.000 |

## J 7

| X-Coordinate | 491156.94 |
| --- | --- |
| Y-Coordinate | 4523650.3 |
| Offset elevation (m) | 0.000 |

## J 8

| X-Coordinate | 491142.15 |
| --- | --- |
| Y-Coordinate | 4523652.78 |
| Offset elevation (m) | 0.000 |

## J 9

| X-Coordinate | 491122.26 |
| --- | --- |
| Y-Coordinate | 4523656.11 |
| Offset elevation (m) | 0.000 |

## J 10

| X-Coordinate | 491107.61 |
| --- | --- |
| Y-Coordinate | 4523652.89 |
| Offset elevation (m) | 0.000 |

## J 11

| X-Coordinate | 491092.96 |
| --- | --- |
| Y-Coordinate | 4523649.66 |
| Offset elevation (m) | 0.000 |

## J 12

| X-Coordinate | 491078.31 |
| --- | --- |
| Y-Coordinate | 4523646.44 |
| Offset elevation (m) | 0.000 |

## J 13

| X-Coordinate | 491063.67 |
| --- | --- |
| Y-Coordinate | 4523643.21 |
| Offset elevation (m) | 0.000 |

## J 14

| X-Coordinate | 491043.75 |
| --- | --- |
| Y-Coordinate | 4523638.83 |
| Offset elevation (m) | 0.000 |

## J 15

| X-Coordinate | 491028.83 |
| --- | --- |
| Y-Coordinate | 4523640.44 |
| Offset elevation (m) | 0.000 |

# Conduits

## C1

| Start node | J 1 |
| --- | --- |
| End node | J 2 |
| Slope | 0.13597 |

## C2

| Start node | J 2 |
| --- | --- |
| End node | J 3 |
| Slope | 0.00600 |

## C3

| Start node | J 3 |
| --- | --- |
| End node | J 4 |
| Slope | 0.00259 |

## C4

| Start node | J 4 |
| --- | --- |
| End node | J 5 |
| Slope | 0.03001 |

## C5

| Start node | J 5 |
| --- | --- |
| End node | J 6 |
| Slope | 0.01266 |

## C6

| Start node | J 6 |
| --- | --- |
| End node | J 7 |
| Slope | 0.01334 |

## C7

| Start node | J 7 |
| --- | --- |
| End node | J 8 |
| Slope | 0.02934 |

## C8

| Start node | J 8 |
| --- | --- |
| End node | J 9 |
| Slope | 0.02529 |

## C9

| Start node | J 9 |
| --- | --- |
| End node | J 10 |
| Slope | 0.01800 |

## C10

| Start node | J 10 |
| --- | --- |
| End node | J 11 |
| Slope | 0.01733 |

## C11

| Start node | J 11 |
| --- | --- |
| End node | J 12 |
| Slope | 0.01600 |

## C12

| Start node | J 12 |
| --- | --- |
| End node | J 13 |
| Slope | 0.00934 |

## C13

| Start node | J 13 |
| --- | --- |
| End node | J 14 |
| Slope | 0.03677 |

## C14

| Start node | J 14 |
| --- | --- |
| End node | J 15 |
| Slope | 0.02466 |

# Inflows: Direct

## Section: J 1

| Constituent | Flow |
| --- | --- |
| Inflow (m³/s) | 15 |

# Time Patterns

## TP1

| Pattern type | Monthly |
| --- | --- |
| January | 0 |
| February | 0 |
| March | 0 |
| April | 0 |
| May | 0 |
| June | 0 |
| July | 0 |
| August | 0 |
| September | 0 |
| October | 0 |
| November | 0 |
| December | 0 |

## TP 2

| Pattern type | Monthly |
| --- | --- |
| January | 0.9 |
| February | 0.8 |
| March | 1 |
| April | 1 |
| May | 1.1 |
| June | 1.2 |
| July | 1 |
| August | 1.1 |
| September | 0.9 |
| October | 1 |
| November | 0.9 |
| December | 1.1 |

# Results

# Node results

## 00:15 28/07/2010

| Node | Depth (m) | Head (m) | Volume (m³) | Lateral inflow (m³/s) | Total inflow (m³/s) | Flooding (m³/s) |
| --- | --- | --- | --- | --- | --- | --- |
| J 1 | 0.352 | 108.282 | 0.000 | 15.000 | 15.000 | 0.000 |
| J 2 | 1.146 | 107.036 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 3 | 1.249 | 107.049 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 4 | 1.249 | 107.009 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 5 | 0.915 | 106.225 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 6 | 0.915 | 106.035 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 7 | 0.769 | 105.689 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 8 | 0.610 | 105.090 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 9 | 0.610 | 104.580 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 10 | 0.700 | 104.400 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 11 | 0.712 | 104.152 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 12 | 0.803 | 104.003 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 13 | 0.803 | 103.863 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 14 | 0.649 | 102.959 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 15 | 0.649 | 102.589 | 0.000 | 0.000 | 15.000 | 0.000 |

## 00:30 28/07/2010

| Node | Depth (m) | Head (m) | Volume (m³) | Lateral inflow (m³/s) | Total inflow (m³/s) | Flooding (m³/s) |
| --- | --- | --- | --- | --- | --- | --- |
| J 1 | 0.352 | 108.282 | 0.000 | 15.000 | 15.000 | 0.000 |
| J 2 | 1.146 | 107.036 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 3 | 1.249 | 107.049 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 4 | 1.249 | 107.009 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 5 | 0.915 | 106.225 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 6 | 0.915 | 106.035 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 7 | 0.769 | 105.689 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 8 | 0.610 | 105.090 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 9 | 0.610 | 104.580 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 10 | 0.700 | 104.400 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 11 | 0.712 | 104.152 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 12 | 0.803 | 104.003 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 13 | 0.803 | 103.863 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 14 | 0.649 | 102.959 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 15 | 0.649 | 102.589 | 0.000 | 0.000 | 15.000 | 0.000 |

## 00:45 28/07/2010

| Node | Depth (m) | Head (m) | Volume (m³) | Lateral inflow (m³/s) | Total inflow (m³/s) | Flooding (m³/s) |
| --- | --- | --- | --- | --- | --- | --- |
| J 1 | 0.352 | 108.282 | 0.000 | 15.000 | 15.000 | 0.000 |
| J 2 | 1.146 | 107.036 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 3 | 1.249 | 107.049 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 4 | 1.249 | 107.009 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 5 | 0.915 | 106.225 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 6 | 0.915 | 106.035 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 7 | 0.769 | 105.689 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 8 | 0.610 | 105.090 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 9 | 0.610 | 104.580 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 10 | 0.700 | 104.400 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 11 | 0.712 | 104.152 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 12 | 0.803 | 104.003 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 13 | 0.803 | 103.863 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 14 | 0.649 | 102.959 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 15 | 0.649 | 102.589 | 0.000 | 0.000 | 15.000 | 0.000 |

## 01:00 28/07/2010

| Node | Depth (m) | Head (m) | Volume (m³) | Lateral inflow (m³/s) | Total inflow (m³/s) | Flooding (m³/s) |
| --- | --- | --- | --- | --- | --- | --- |
| J 1 | 0.352 | 108.282 | 0.000 | 15.000 | 15.000 | 0.000 |
| J 2 | 1.146 | 107.036 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 3 | 1.249 | 107.049 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 4 | 1.249 | 107.009 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 5 | 0.915 | 106.225 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 6 | 0.915 | 106.035 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 7 | 0.769 | 105.689 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 8 | 0.610 | 105.090 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 9 | 0.610 | 104.580 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 10 | 0.700 | 104.400 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 11 | 0.712 | 104.152 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 12 | 0.803 | 104.003 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 13 | 0.803 | 103.863 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 14 | 0.649 | 102.959 | 0.000 | 0.000 | 15.000 | 0.000 |
| J 15 | 0.649 | 102.589 | 0.000 | 0.000 | 15.000 | 0.000 |

# Link results

## 00:15 28/07/2010

| Link | Flow rate m³/s | Flow depth (m) | Velocity (m/s) | Froude | Capacity |
| --- | --- | --- | --- | --- | --- |
| C1 | 15.000 | 0.352 | 3.01 | 1.87 | 0.05 |
| C2 | 15.000 | 1.146 | 1.32 | 0.49 | 0.13 |
| C3 | 15.000 | 1.249 | 0.89 | 0.31 | 0.13 |
| C4 | 15.000 | 0.851 | 2.01 | 0.95 | 0.09 |
| C5 | 15.000 | 0.915 | 1.26 | 0.62 | 0.10 |
| C6 | 15.000 | 0.769 | 1.30 | 0.63 | 0.09 |
| C7 | 15.000 | 0.442 | 1.52 | 0.87 | 0.05 |
| C8 | 15.000 | 0.610 | 1.53 | 0.84 | 0.07 |
| C9 | 15.000 | 0.603 | 1.48 | 0.73 | 0.06 |
| C10 | 15.000 | 0.700 | 1.45 | 0.72 | 0.08 |
| C11 | 15.000 | 0.712 | 1.32 | 0.68 | 0.09 |
| C12 | 15.000 | 0.803 | 1.13 | 0.53 | 0.11 |
| C13 | 15.000 | 0.558 | 1.95 | 1.03 | 0.08 |
| C14 | 15.000 | 0.649 | 1.76 | 0.86 | 0.10 |

## 00:30 28/07/2010

| Link | Flow rate m³/s | Flow depth (m) | Velocity (m/s) | Froude | Capacity |
| --- | --- | --- | --- | --- | --- |
| C1 | 15.000 | 0.352 | 3.01 | 1.87 | 0.05 |
| C2 | 15.000 | 1.146 | 1.32 | 0.49 | 0.13 |
| C3 | 15.000 | 1.249 | 0.89 | 0.31 | 0.13 |
| C4 | 15.000 | 0.851 | 2.01 | 0.95 | 0.09 |
| C5 | 15.000 | 0.915 | 1.26 | 0.62 | 0.10 |
| C6 | 15.000 | 0.769 | 1.30 | 0.63 | 0.09 |
| C7 | 15.000 | 0.442 | 1.52 | 0.87 | 0.05 |
| C8 | 15.000 | 0.610 | 1.53 | 0.84 | 0.07 |
| C9 | 15.000 | 0.603 | 1.48 | 0.73 | 0.06 |
| C10 | 15.000 | 0.700 | 1.45 | 0.72 | 0.08 |
| C11 | 15.000 | 0.712 | 1.32 | 0.68 | 0.09 |
| C12 | 15.000 | 0.803 | 1.13 | 0.53 | 0.11 |
| C13 | 15.000 | 0.558 | 1.95 | 1.03 | 0.08 |
| C14 | 15.000 | 0.649 | 1.76 | 0.86 | 0.10 |

## 00:45 28/07/2010

| Link | Flow rate m³/s | Flow depth (m) | Velocity (m/s) | Froude | Capacity |
| --- | --- | --- | --- | --- | --- |
| C1 | 15.000 | 0.352 | 3.01 | 1.87 | 0.05 |
| C2 | 15.000 | 1.146 | 1.32 | 0.49 | 0.13 |
| C3 | 15.000 | 1.249 | 0.89 | 0.31 | 0.13 |
| C4 | 15.000 | 0.851 | 2.01 | 0.95 | 0.09 |
| C5 | 15.000 | 0.915 | 1.26 | 0.62 | 0.10 |
| C6 | 15.000 | 0.769 | 1.30 | 0.63 | 0.09 |
| C7 | 15.000 | 0.442 | 1.52 | 0.87 | 0.05 |
| C8 | 15.000 | 0.610 | 1.53 | 0.84 | 0.07 |
| C9 | 15.000 | 0.603 | 1.48 | 0.73 | 0.06 |
| C10 | 15.000 | 0.700 | 1.45 | 0.72 | 0.08 |
| C11 | 15.000 | 0.712 | 1.32 | 0.68 | 0.09 |
| C12 | 15.000 | 0.803 | 1.13 | 0.53 | 0.11 |
| C13 | 15.000 | 0.558 | 1.95 | 1.03 | 0.08 |
| C14 | 15.000 | 0.649 | 1.76 | 0.86 | 0.10 |

## 01:00 28/07/2010

| Link | Flow rate m³/s | Flow depth (m) | Velocity (m/s) | Froude | Capacity |
| --- | --- | --- | --- | --- | --- |
| C1 | 15.000 | 0.352 | 3.01 | 1.87 | 0.05 |
| C2 | 15.000 | 1.146 | 1.32 | 0.49 | 0.13 |
| C3 | 15.000 | 1.249 | 0.89 | 0.31 | 0.13 |
| C4 | 15.000 | 0.851 | 2.01 | 0.95 | 0.09 |
| C5 | 15.000 | 0.915 | 1.26 | 0.62 | 0.10 |
| C6 | 15.000 | 0.769 | 1.30 | 0.63 | 0.09 |
| C7 | 15.000 | 0.442 | 1.52 | 0.87 | 0.05 |
| C8 | 15.000 | 0.610 | 1.53 | 0.84 | 0.07 |
| C9 | 15.000 | 0.603 | 1.48 | 0.73 | 0.06 |
| C10 | 15.000 | 0.700 | 1.45 | 0.72 | 0.08 |
| C11 | 15.000 | 0.712 | 1.32 | 0.68 | 0.09 |
| C12 | 15.000 | 0.803 | 1.13 | 0.53 | 0.11 |
| C13 | 15.000 | 0.558 | 1.95 | 1.03 | 0.08 |
| C14 | 15.000 | 0.649 | 1.76 | 0.86 | 0.10 |

# System results

| Date | Temperature (°C) | Rainfall (mm/h) | Snow depth (mm) | Losses (mm/h) | Runoff (m³/s) |
| --- | --- | --- | --- | --- | --- |
| 00:15 28/07/2010 | 0.0 | 0.00 | 0.00 | 0.00 | 0.000 |
| 00:30 28/07/2010 | 0.0 | 0.00 | 0.00 | 0.00 | 0.000 |
| 00:45 28/07/2010 | 0.0 | 0.00 | 0.00 | 0.00 | 0.000 |
| 01:00 28/07/2010 | 0.0 | 0.00 | 0.00 | 0.00 | 0.000 |

| Date | Dry weather inflow (m³/s) | Groundwater inflow (m³/s) | RDII inflow (m³/s) | Direct inflow (m³/s) | Total inflow (m³/s) |
| --- | --- | --- | --- | --- | --- |
| 00:15 28/07/2010 | 0.000 | 0.000 | 0.000 | 15.000 | 15.000 |
| 00:30 28/07/2010 | 0.000 | 0.000 | 0.000 | 15.000 | 15.000 |
| 00:45 28/07/2010 | 0.000 | 0.000 | 0.000 | 15.000 | 15.000 |
| 01:00 28/07/2010 | 0.000 | 0.000 | 0.000 | 15.000 | 15.000 |

| Date | Flooding (m³/s) | Outfalls (m³/s) | Stored (m³) | Evaporation (mm/h) |
| --- | --- | --- | --- | --- |
| 00:15 28/07/2010 | 0.000 | 15.000 | 2265.394 | 0.00 |
| 00:30 28/07/2010 | 0.000 | 15.000 | 2265.394 | 0.00 |
| 00:45 28/07/2010 | 0.000 | 15.000 | 2265.394 | 0.00 |
| 01:00 28/07/2010 | 0.000 | 15.000 | 2265.394 | 0.00 |