Sewer Networks v9.0 - Calculations Report Copyright ©1996-2009 TechnoLogismiki www.technologismiki.com

Contents

Project information	4

General data	4

Model preferences	4

Dates	4

Time Steps	4

Design	4

Climatology	5

Temperature	5

Evaporation	5

Wind Speed	5

Snow Melt	5

Areal Depletion	6

Junctions	6

Α1	6

Α2	6

Α3	6

Α4	7

Α5	7

Α6	7

Α7	7

Α8	7

Α9	8

Α10	8

Α11	8

Α12	8

Α13	8

Α2-3	9

Α2-2	9

Conduits	9

Α1:Α2	9

Α2:Α3	9

Α3:Α4	10

Α4:Α5	10

Α5:Α6	10

Α6:Α7	10

Α7:Α8	11

Α8:Α9	11

Α9:Α10	11

Α10:Α11	12

Α11:Α12	12

Α12:Α13	12

Α2-3:Α2-2	12

Α2-2:Α2	13

Pipes Specifications	13

D   1	13

D   0.9	13

D   0.8	14

D   0.6	14

D   0.4	14

D   1.1	15

D   1.2	15

D   1.3	15

D   1.4	16

Inflows: Direct	16

Junction: Α1	16

Junction: Α3	16

Junction: Α5	16

Junction: Α6	17

Junction: Α10	17

Junction: Α2-3	17

Vertical Street Addresses	17

Other Junctions	17

Manhole Specifications	17

Trench Specifications	18

OLD / 1	18

OLD / 2	18

Runoff Areas	19

P1	19

P2	19

Sewer Flow (Area)	19

P1	19

P2	19

Results	20

Node results	20

01:00 30/10/2007	20

Link results	21

01:00 30/10/2007	21

System results	21

# Project information

# General data

## Model preferences

| Flow units | m³/s |
| --- | --- |
| Infiltration model | Horton |
| Routing method | Steady flow |
| Allow excess water ponding | No |
| Skip steady state periods | No |
| Minimum conduit slope (%) | No |
| Ignore rainfall/runoff | No |
| Ignore snow melt | No |
| Ignore ground water | No |
| Ignore flow routing | No |
| Ignore water quality | No |
| Minimum conduit slope (%) | 0 |
| Report input summary | No |
| Skip steady state periods | No |

## Dates

| Start analysis on | 00:00 30/10/2007 |
| --- | --- |
| Start reporting on | 00:00 30/10/2007 |
| End analysis on | 01:00 30/10/2007 |
| Start sweeping on | 01/01 |
| End sweeping on | 31/12 |
| Number of antecedent dry days | 0 |

## Time Steps

| Reporting time step (days, HH:MM:SS) | 1:00:00 |
| --- | --- |
| Dry weather runoff (days, HH:MM:SS) | 00:15:00 |
| Wet weather runoff (days, HH:MM:SS) | 01:00:00 |
| Routing (sec) | 00:00:30 |

## Design

| Conduit placement automation | Crown elevations |
| --- | --- |
| Cuts in excavations measured | From ground |
| Inlet bottoms measured | From sublayer |
| Kinematic viscosity (m²/s) | 0.00000139 |
| Density (kg/m³) | 999.88 |
| Maximum sewer peak flow factor (kg/m³) | 0 |

# Climatology

## Temperature

| Source | No data |
| --- | --- |

## Evaporation

| Source | Constant value (mm/day) |
| --- | --- |

## Wind Speed

| Source | Monthly averages |
| --- | --- |

| No | Month | Monthly averages (km/h) |
| --- | --- | --- |
| 1 | January | N/A |
| 2 | February | N/A |
| 3 | March | N/A |
| 4 | April | N/A |
| 5 | May | N/A |
| 6 | June | N/A |
| 7 | July | N/A |
| 8 | August | N/A |
| 9 | September | N/A |
| 10 | October | N/A |
| 11 | November | N/A |
| 12 | December | N/A |

## Snow Melt

| Dividing temperature between snow and rain (°C) | 1.1 |
| --- | --- |
| Antecedent temperature index weight (fraction) | 0.5000 |
| Negative melt ratio (fraction) | 0.6000 |
| Elevation above mean sea level (m) | 0.000 |
| Latitude (degrees) | 50.0000 |
| Longitude correction (+/- minutes) | 0.0000 |

## Areal Depletion

| Depth ratio | Impervious | Pervious |
| --- | --- | --- |
| 0.0 | 1.0000 | 1.0000 |
| 0.1 | 1.0000 | 1.0000 |
| 0.2 | 1.0000 | 1.0000 |
| 0.3 | 1.0000 | 1.0000 |
| 0.4 | 1.0000 | 1.0000 |
| 0.5 | 1.0000 | 1.0000 |
| 0.6 | 1.0000 | 1.0000 |
| 0.7 | 1.0000 | 1.0000 |
| 0.8 | 1.0000 | 1.0000 |
| 0.9 | 1.0000 | 1.0000 |

# Junctions

## Α1

| X-Coordinate | 485818.61 |
| --- | --- |
| Y-Coordinate | 4227054.63 |
| Constituent | Flow |
| Scale factor | 1 |
| P1 (ha) | 7.0000 |
| Ground elevation (m) | 301.220 |
| Invert elevation (m) | 299.220 |
| Ponded area (m²) | 0.0000 |

## Α2

| X-Coordinate | 485873.12 |
| --- | --- |
| Y-Coordinate | 4227106.57 |
| Ground elevation (m) | 302.090 |
| Invert elevation (m) | 298.501 |
| Ponded area (m²) | 0.0000 |

## Α3

| X-Coordinate | 485916.89 |
| --- | --- |
| Y-Coordinate | 4227084.91 |
| Constituent | Flow |
| Scale factor | 1 |
| P2 (ha) | 0.5000 |
| Ground elevation (m) | 300.590 |
| Invert elevation (m) | 298.100 |
| Ponded area (m²) | 0.0000 |

## Α4

| X-Coordinate | 485955.42 |
| --- | --- |
| Y-Coordinate | 4227063.76 |
| Ground elevation (m) | 299.250 |
| Invert elevation (m) | 297.250 |
| Ponded area (m²) | 0.0000 |

## Α5

| X-Coordinate | 486012.57 |
| --- | --- |
| Y-Coordinate | 4227045.44 |
| Constituent | Flow |
| Scale factor | 1 |
| P2 (ha) | 2.1000 |
| Ground elevation (m) | 297.680 |
| Invert elevation (m) | 295.680 |
| Ponded area (m²) | 0.0000 |

## Α6

| X-Coordinate | 486020.64 |
| --- | --- |
| Y-Coordinate | 4226982.32 |
| Constituent | Flow |
| Scale factor | 1 |
| P2 (ha) | 7.0000 |
| Ground elevation (m) | 295.870 |
| Invert elevation (m) | 293.870 |
| Ponded area (m²) | 0.0000 |

## Α7

| X-Coordinate | 486028.29 |
| --- | --- |
| Y-Coordinate | 4226922.04 |
| Ground elevation (m) | 294.900 |
| Invert elevation (m) | 292.900 |
| Ponded area (m²) | 0.0000 |

## Α8

| X-Coordinate | 486026.86 |
| --- | --- |
| Y-Coordinate | 4226868.46 |
| Ground elevation (m) | 294.900 |
| Invert elevation (m) | 292.264 |
| Ponded area (m²) | 0.0000 |

## Α9

| X-Coordinate | 486023.03 |
| --- | --- |
| Y-Coordinate | 4226812 |
| Ground elevation (m) | 295.490 |
| Invert elevation (m) | 291.698 |
| Ponded area (m²) | 0.0000 |

## Α10

| X-Coordinate | 486022.28 |
| --- | --- |
| Y-Coordinate | 4226760.78 |
| Constituent | Flow |
| Scale factor | 1 |
| P2 (ha) | 4.7000 |
| Ground elevation (m) | 295.560 |
| Invert elevation (m) | 291.186 |
| Ponded area (m²) | 0.0000 |

## Α11

| X-Coordinate | 486023.37 |
| --- | --- |
| Y-Coordinate | 4226704.9 |
| Ground elevation (m) | 294.020 |
| Invert elevation (m) | 290.527 |
| Ponded area (m²) | 0.0000 |

## Α12

| X-Coordinate | 486022.28 |
| --- | --- |
| Y-Coordinate | 4226639.98 |
| Ground elevation (m) | 291.160 |
| Invert elevation (m) | 288.500 |
| Ponded area (m²) | 0.0000 |

## Α13

| X-Coordinate | 486019.71 |
| --- | --- |
| Y-Coordinate | 4226583.72 |
| Ground elevation (m) | 288.270 |
| Invert elevation (m) | 286.670 |
| Ponded area (m²) | 0.0000 |

## Α2-3

| X-Coordinate | 485923.84 |
| --- | --- |
| Y-Coordinate | 4227174.1 |
| Constituent | Flow |
| Scale factor | 1 |
| P1 (ha) | 7.8000 |
| Ground elevation (m) | 303.850 |
| Invert elevation (m) | 302.350 |
| Ponded area (m²) | 0.0000 |

## Α2-2

| X-Coordinate | 485898.85 |
| --- | --- |
| Y-Coordinate | 4227137.43 |
| Ground elevation (m) | 302.840 |
| Invert elevation (m) | 300.340 |
| Ponded area (m²) | 0.0000 |

# Conduits

## Α1:Α2

| Start node | Α1 |
| --- | --- |
| End node | Α2 |
| Shape | D 1 |
| Inlet elevation (m) | 299.220 |
| Outlet elevation (m) | {298.601} |
| Slope | 0.00822 |
| Sum of upstream areas (ha) | 7.0000 |
| Total pipe length (m) | 75.293 |
| Total pipe length x diameter (m²) | 75.293000 |

## Α2:Α3

| Start node | Α2 |
| --- | --- |
| End node | Α3 |
| Shape | D 1.1 |
| Inlet elevation (m) | {298.501} |
| Outlet elevation (m) | 298.100 |
| Slope | 0.00822 |
| Sum of upstream areas (ha) | 15.0000 |
| Total pipe length (m) | 208.524 |
| Total pipe length x diameter (m²) | 213.407600 |

## Α3:Α4

| Start node | Α3 |
| --- | --- |
| End node | Α4 |
| Shape | D 1.1 |
| Inlet elevation (m) | 298.100 |
| Outlet elevation (m) | 297.250 |
| Slope | 0.01934 |
| Sum of upstream areas (ha) | 15.0000 |
| Total pipe length (m) | 252.477 |
| Total pipe length x diameter (m²) | 261.755900 |

## Α4:Α5

| Start node | Α4 |
| --- | --- |
| End node | Α5 |
| Shape | D 1.1 |
| Inlet elevation (m) | 297.250 |
| Outlet elevation (m) | 295.680 |
| Slope | 0.02616 |
| Sum of upstream areas (ha) | 15.0000 |
| Total pipe length (m) | 312.492 |
| Total pipe length x diameter (m²) | 327.772400 |

## Α5:Α6

| Start node | Α5 |
| --- | --- |
| End node | Α6 |
| Shape | D 1.1 |
| Inlet elevation (m) | 295.680 |
| Outlet elevation (m) | 293.870 |
| Slope | 0.02844 |
| Sum of upstream areas (ha) | 17.0000 |
| Total pipe length (m) | 376.126 |
| Total pipe length x diameter (m²) | 397.769800 |

## Α6:Α7

| Start node | Α6 |
| --- | --- |
| End node | Α7 |
| Shape | D 1.2 |
| Inlet elevation (m) | 293.870 |
| Outlet elevation (m) | 292.900 |
| Slope | 0.01596 |
| Sum of upstream areas (ha) | 24.0000 |
| Total pipe length (m) | 436.889 |
| Total pipe length x diameter (m²) | 470.685400 |

## Α7:Α8

| Start node | Α7 |
| --- | --- |
| End node | Α8 |
| Shape | D 1.2 |
| Inlet elevation (m) | 292.900 |
| Outlet elevation (m) | 292.264 |
| Slope | 0.01187 |
| Sum of upstream areas (ha) | 24.0000 |
| Total pipe length (m) | 490.488 |
| Total pipe length x diameter (m²) | 535.004200 |

## Α8:Α9

| Start node | Α8 |
| --- | --- |
| End node | Α9 |
| Shape | D 1.3 |
| Inlet elevation (m) | 292.264 |
| Outlet elevation (m) | 291.698 |
| Slope | 0.01000 |
| Sum of upstream areas (ha) | 24.0000 |
| Total pipe length (m) | 547.078 |
| Total pipe length x diameter (m²) | 608.571200 |

## Α9:Α10

| Start node | Α9 |
| --- | --- |
| End node | Α10 |
| Shape | D 1.3 |
| Inlet elevation (m) | 291.698 |
| Outlet elevation (m) | 291.186 |
| Slope | 0.01000 |
| Sum of upstream areas (ha) | 24.0000 |
| Total pipe length (m) | 598.303 |
| Total pipe length x diameter (m²) | 675.163700 |

## Α10:Α11

| Start node | Α10 |
| --- | --- |
| End node | Α11 |
| Shape | D 1.3 |
| Inlet elevation (m) | 291.186 |
| Outlet elevation (m) | 290.527 |
| Slope | 0.01179 |
| Sum of upstream areas (ha) | 29.0000 |
| Total pipe length (m) | 654.194 |
| Total pipe length x diameter (m²) | 747.822000 |

## Α11:Α12

| Start node | Α11 |
| --- | --- |
| End node | Α12 |
| Shape | D 1.3 |
| Inlet elevation (m) | 290.527 |
| Outlet elevation (m) | 288.500 |
| Slope | 0.03122 |
| Sum of upstream areas (ha) | 29.0000 |
| Total pipe length (m) | 719.123 |
| Total pipe length x diameter (m²) | 832.229700 |

## Α12:Α13

| Start node | Α12 |
| --- | --- |
| End node | Α13 |
| Shape | D 1.3 |
| Inlet elevation (m) | 288.500 |
| Outlet elevation (m) | 286.670 |
| Slope | 0.03249 |
| Sum of upstream areas (ha) | 29.0000 |
| Total pipe length (m) | 775.442 |
| Total pipe length x diameter (m²) | 905.444400 |

## Α2-3:Α2-2

| Start node | Α2-3 |
| --- | --- |
| End node | Α2-2 |
| Shape | D 1 |
| Inlet elevation (m) | 302.350 |
| Outlet elevation (m) | 300.340 |
| Slope | 0.04529 |
| Sum of upstream areas (ha) | 8.0000 |
| Total pipe length (m) | 44.376 |
| Total pipe length x diameter (m²) | 44.376000 |

## Α2-2:Α2

| Start node | Α2-2 |
| --- | --- |
| End node | Α2 |
| Shape | D 1 |
| Inlet elevation (m) | 300.340 |
| Outlet elevation (m) | 298.601 |
| Slope | 0.04345 |
| Sum of upstream areas (ha) | 8.0000 |
| Total pipe length (m) | 84.395 |
| Total pipe length x diameter (m²) | 84.395000 |

# Pipes Specifications

## D   1

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 1 |
| Material | Concrete |
| Thickness (m) | 0.120 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   0.9

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 0.9 |
| Material | Concrete |
| Thickness (m) | 0.105 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   0.8

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 0.8 |
| Material | Concrete |
| Thickness (m) | 0.090 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   0.6

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 0.6 |
| Material | Concrete |
| Thickness (m) | 0.065 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   0.4

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 0.4 |
| Material | Concrete |
| Thickness (m) | 0.040 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.50 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   1.1

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 1.1 |
| Material | Concrete |
| Thickness (m) | 0.150 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   1.2

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 1.2 |
| Material | Concrete |
| Thickness (m) | 0.150 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   1.3

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 1.3 |
| Material | Concrete |
| Thickness (m) | 0.150 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

## D   1.4

| Shape data |
| --- |
| Type | Circular |
| Diameter (m) | 1.4 |
| Material | Concrete |
| Thickness (m) | 0.150 |
| Hydraulic data |
| Manning coefficient | 0.0140 |
| Darcy-Weisbach coefficient | 0.0000 |
| Hazen-Williams coefficient | 0.0000 |
| Maximum capacity | 0.70 |
| Maximum velocity (m/s) | 6.00 |
| Construction |

# Inflows: Direct

## Junction: Α1

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P1 (ha) | 7.0000 |

## Junction: Α3

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P2 (ha) | 0.5000 |

## Junction: Α5

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P2 (ha) | 2.1000 |

## Junction: Α6

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P2 (ha) | 7.0000 |

## Junction: Α10

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P2 (ha) | 4.7000 |

## Junction: Α2-3

| Constituent | Flow |
| --- | --- |
| Scale factor | 1 |
| P1 (ha) | 7.8000 |

# Vertical Street Addresses

| No | Vertical street address | Distance from start (m) | Profile |
| --- | --- | --- | --- |
| 1 | ΑΓ.ΑΘΑΝΑΣΙΟΥ | 75.293 | ΣΥΛΛΕΚΤΗΡΑΣ |

# Other Junctions

| No | Inlet type | Distance from start (m) | Bottom elevation (m) | Comments | Place |
| --- | --- | --- | --- | --- | --- |
| 1 | D 1 | 0.000 | 0.000 |  | - |
| 2 | D 1 | 84.400 | 297.262 |  | - |
| 3 | D 1 | 75.290 | 298.999 |  | - |

# Manhole Specifications

| No |
| --- |
| Inlet geometry | Circular |
| Diameter (m) | 1.500 |
| Inlet height (m) | 3.000 |
| Inlet has neck | No |
| Use sublayer | No |
| Thickness |
| Upper slab thickness (m) | 0.000 |
| Bottom slab thickness (m) | 0.000 |
| Wall thickness (m) | 0.000 |
| Neck's wall thickness (m) | 0.000 |
| Materials |
| Inlet is made of | N/A |
| Bottom layout in inlet is made of | N/A |
| Sublayer is made of | N/A |
| Calculate wood forms | No |
| Calculate asphalt | No |

# Trench Specifications

## OLD / 1

| Trench data |
| --- |
| Type | V |
| Pipe foundation height (m) | 0.25 |
| Backfilling height (m) | 0 |
| Sublayer (Layer 1) material (m) | C8/10 |
| Layer 2 backfilling material (m) | C8/10 |
| Layer 3 backfilling material (m) | C8/10 |
| Layer 4 backfilling material (m) | C8/10 |
| Trench profile |
| Number of layers | 0 |
| Number of ground layers | 0 |
| Miscellaneous |
| Use marking grid | No |
| Ground is | Plain |
| Extra surface width for construction (m) | 0.000 |
| Foundation concrete type | C8/10 |
| Confinement concrete type | C8/10 |
| Conduit concrete type | C8/10 |

## OLD / 2

| Trench data |
| --- |
| Type | V |
| Pipe foundation height (m) | 0.3 |
| Backfilling height (m) | 0 |
| Sublayer (Layer 1) material (m) | C8/10 |
| Layer 2 backfilling material (m) | C8/10 |
| Layer 3 backfilling material (m) | C8/10 |
| Layer 4 backfilling material (m) | C8/10 |
| Trench profile |
| Number of layers | 0 |
| Number of ground layers | 0 |
| Miscellaneous |
| Use marking grid | No |
| Ground is | Plain |
| Extra surface width for construction (m) | 0.000 |
| Foundation concrete type | C8/10 |
| Confinement concrete type | C8/10 |
| Conduit concrete type | C8/10 |

# Runoff Areas

## P1

| Runoff coefficient | 0.5000 |
| --- | --- |

## P2

| Runoff coefficient | 0.6000 |
| --- | --- |

# Sewer Flow (Area)

## P1

| Mean daily water consumption Qy (m³/day/person) | 0.00 |
| --- | --- |
| Mean daily water consumption Qy (m³/day/person) | 0.00 |
| Fraction of water consumption to the sewer (%) | 0.00 |
| Mean daily sewer flow Qd (m³/day/person) | 0.00 |
| Daily peak factor | 0.0000 |
| Max daily sewer flow Ql' (m³/day/person) | 0.00 |
| Augmentation factor (%) | 0.0000 |
| Max daily sewer flow Ql (m³/day/person) | 0.00 |
| Total population (person) | 0 |
| Total area (ha) | 0.0000 |
| Mean daily water consumption Qy (m³/s/ha) | 0.0000 |
| Mean daily sewer flow Qd (m³/s/ha) | 0.0000 |
| Max daily sewer flow Ql (m³/s/ha) | 0.0000 |

## P2

| Mean daily water consumption Qy (m³/day/person) | 0.00 |
| --- | --- |
| Mean daily water consumption Qy (m³/day/person) | 0.00 |
| Fraction of water consumption to the sewer (%) | 0.00 |
| Mean daily sewer flow Qd (m³/day/person) | 0.00 |
| Daily peak factor | 0.0000 |
| Max daily sewer flow Ql' (m³/day/person) | 0.00 |
| Augmentation factor (%) | 0.0000 |
| Max daily sewer flow Ql (m³/day/person) | 0.00 |
| Total population (person) | 0 |
| Total area (ha) | 0.0000 |
| Mean daily water consumption Qy (m³/s/ha) | 0.0000 |
| Mean daily sewer flow Qd (m³/s/ha) | 0.0000 |
| Max daily sewer flow Ql (m³/s/ha) | 0.0000 |

# Results

# Node results

## 01:00 30/10/2007

| Node | Depth (m) | Head (m) | Volume (m³) | Lateral inflow (m³/s) | Total inflow (m³/s) | Flooding (m³/s) |
| --- | --- | --- | --- | --- | --- | --- |
| Α1 | 0.476 | 299.696 | 0.000 | 0.927 | 0.927 | 0.000 |
| Α2 | 0.713 | 299.214 | 0.000 | 0.000 | 1.961 | 0.000 |
| Α3 | 0.713 | 298.813 | 0.000 | 0.079 | 2.040 | 0.000 |
| Α4 | 0.557 | 297.807 | 0.000 | 0.000 | 2.040 | 0.000 |
| Α5 | 0.544 | 296.224 | 0.000 | 0.334 | 2.374 | 0.000 |
| Α6 | 0.784 | 294.654 | 0.000 | 1.113 | 3.487 | 0.000 |
| Α7 | 0.877 | 293.777 | 0.000 | 0.000 | 3.487 | 0.000 |
| Α8 | 0.877 | 293.141 | 0.000 | 0.000 | 3.487 | 0.000 |
| Α9 | 0.862 | 292.560 | 0.000 | 0.000 | 3.487 | 0.000 |
| Α10 | 0.938 | 292.124 | 0.000 | 0.747 | 4.234 | 0.000 |
| Α11 | 0.938 | 291.465 | 0.000 | 0.000 | 4.234 | 0.000 |
| Α12 | 0.676 | 289.176 | 0.000 | 0.000 | 4.234 | 0.000 |
| Α13 | 1.600 | 288.270 | 0.000 | 0.000 | 4.234 | 0.000 |
| Α2-3 | 0.317 | 302.667 | 0.000 | 1.033 | 1.033 | 0.000 |
| Α2-2 | 0.321 | 300.661 | 0.000 | 0.000 | 1.033 | 0.000 |

# Link results

## 01:00 30/10/2007

| Link | Flow rate m³/s | Flow depth (m) | Velocity (m/s) | Froude | Capacity |
| --- | --- | --- | --- | --- | --- |
| Α1:Α2 | 0.927 | 0.476 | 2.52 | 1.32 | 0.48 |
| Α2:Α3 | 1.961 | 0.713 | 3.01 | 1.22 | 0.65 |
| Α3:Α4 | 2.040 | 0.557 | 4.22 | 2.03 | 0.51 |
| Α4:Α5 | 2.040 | 0.510 | 4.73 | 2.41 | 0.46 |
| Α5:Α6 | 2.374 | 0.544 | 5.07 | 2.48 | 0.49 |
| Α6:Α7 | 3.487 | 0.784 | 4.45 | 1.72 | 0.65 |
| Α7:Α8 | 3.487 | 0.877 | 3.93 | 1.38 | 0.73 |
| Α8:Α9 | 3.487 | 0.862 | 3.73 | 1.37 | 0.66 |
| Α9:Α10 | 3.487 | 0.862 | 3.73 | 1.37 | 0.66 |
| Α10:Α11 | 4.234 | 0.938 | 4.13 | 1.40 | 0.72 |
| Α11:Α12 | 4.234 | 0.676 | 6.06 | 2.64 | 0.52 |
| Α12:Α13 | 4.234 | 0.668 | 6.16 | 2.70 | 0.51 |
| Α2-3:Α2-2 | 1.033 | 0.317 | 4.83 | 3.21 | 0.32 |
| Α2-2:Α2 | 1.033 | 0.321 | 4.76 | 3.15 | 0.32 |

# System results

| Date | Temperature (°C) | Rainfall (mm/h) | Snow depth (mm) | Losses (mm/h) | Runoff (m³/s) |
| --- | --- | --- | --- | --- | --- |
| 01:00 30/10/2007 | 0.0 | 0.00 | 0.00 | 0.00 | 0.000 |

| Date | Dry weather inflow (m³/s) | Groundwater inflow (m³/s) | RDII inflow (m³/s) | Direct inflow (m³/s) | Total inflow (m³/s) |
| --- | --- | --- | --- | --- | --- |
| 01:00 30/10/2007 | 0.000 | 0.000 | 0.000 | 4.234 | 4.234 |

| Date | Flooding (m³/s) | Outfalls (m³/s) | Stored (m³) | Evaporation (mm/h) |
| --- | --- | --- | --- | --- |
| 01:00 30/10/2007 | 0.000 | 4.234 | 491.879 | 0.00 |