Biaxial Bending v2.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

Data	3

Units	3

General data	3

Section	3

General	3

Image	4

Polygon 1	4

Polygon 2	5

Polygon 3	5

Polygon 4	5

Polygon 5	6

Polygon 6	6

Polygon 7	6

Polygon 8	6

Polygon 9	7

Polygon 10	7

Polygon 11	7

Polygon 12	7

Polygon 13	7

Polygon 14	8

Polygon 15	8

Polygon 16	8

Polygon 17	8

Polygon 18	9

Materials	9

S460, 1.15 (MPa)	9

C30, 0.85, 1.5 (MPa)	10

S355, 1.1 (MPa)	10

Results	11

Final values (X'Y'Z')	11

Final values (XYZ)	11

Image	12

Detailed results	12

# Project information

|  | Παράδειγμα Chen |
| --- | --- |
|  | Αριστοτέλης Χαραλαμπάκης |
|  | Το παράδειγμα αυτό μελετήθηκε από τους Chen et al. |
|  | C:\Program Files\TechnoLogismiki\tlw2011\Samples\BiaxialBending\Sample1.m125 |
| Date and time: | 01/12/2010 13:54 |

# Data

## Units

| Length units | mm |
| --- | --- |
| Force units | KN |
| Bending moment units | KNm |

## General data

| Rotation angle (C.C.W. deg) | 0 |
| --- | --- |
| Axial load (KN) | 0 |
| Initial curvature step | Detailed |
| Maximum axial load error (KN) | 1 |
| Usage of point C | No |

## Section

### General

| Curvilinear polygons | 18 |
| --- | --- |

### Image

### Polygon 1

| Name | H-shape |
| --- | --- |
| Foreground material | S355, 1.1 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Corner point | 12 |
| Corner points 1 X-coordinate | -71.481 |
| Corner points 1 Y-coordinata | 59.4536 |
| Corner points 2 X-coordinate | -71.481 |
| Corner points 2 Y-coordinata | -165.9464 |
| Corner points 3 X-coordinate | -194.231 |
| Corner points 3 Y-coordinata | -165.9464 |
| Corner points 4 X-coordinate | -194.231 |
| Corner points 4 Y-coordinata | -183.2464 |
| Corner points 5 X-coordinate | 61.769 |
| Corner points 5 Y-coordinata | -183.2464 |
| Corner points 6 X-coordinate | 61.769 |
| Corner points 6 Y-coordinata | -165.9464 |
| Corner points 7 X-coordinate | -60.981 |
| Corner points 7 Y-coordinata | -165.9464 |
| Corner points 8 X-coordinate | -60.981 |
| Corner points 8 Y-coordinata | 59.4536 |
| Corner points 9 X-coordinate | 61.769 |
| Corner points 9 Y-coordinata | 59.4536 |
| Corner points 10 X-coordinate | 61.769 |
| Corner points 10 Y-coordinata | 76.7536 |
| Corner points 11 X-coordinate | -194.231 |
| Corner points 11 Y-coordinata | 76.7536 |
| Corner points 12 X-coordinate | -194.231 |
| Corner points 12 Y-coordinata | 59.4536 |

### Polygon 2

| Name | Concrete core |
| --- | --- |
| Foreground material | C30, 0.85, 1.5 (MPa) |
| Background material | None |
| Corner point | 5 |
| Corner points 1 X-coordinate | -294.231 |
| Corner points 1 Y-coordinata | 416.7536 |
| Corner points 2 X-coordinate | -294.231 |
| Corner points 2 Y-coordinata | -283.2464 |
| Corner points 3 X-coordinate | 405.769 |
| Corner points 3 Y-coordinata | -283.2464 |
| Corner points 4 X-coordinate | 405.769 |
| Corner points 4 Y-coordinata | 16.7536 |
| Corner points 5 X-coordinate | 105.769 |
| Corner points 5 Y-coordinata | 416.7536 |

### Polygon 3

| Name | D200 hole |
| --- | --- |
| Foreground material | None |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -68.2644 |
| Y-coordinate of center | 226.7536 |
| Radius | 100 |

### Polygon 4

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -244.231 |
| Y-coordinate of center | 366.7536 |
| Radius | 9 |

### Polygon 5

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -94.231 |
| Y-coordinate of center | 366.7536 |
| Radius | 9 |

### Polygon 6

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 55.769 |
| Y-coordinate of center | 366.7536 |
| Radius | 9 |

### Polygon 7

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 159.0164 |
| Y-coordinate of center | 240.1923 |
| Radius | 9 |

### Polygon 8

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -244.231 |
| Y-coordinate of center | 216.7536 |
| Radius | 9 |

### Polygon 9

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -244.231 |
| Y-coordinate of center | 66.7536 |
| Radius | 9 |

### Polygon 10

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 257.3927 |
| Y-coordinate of center | 120.1396 |
| Radius | 9 |

### Polygon 11

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 355.769 |
| Y-coordinate of center | 0.0869 |
| Radius | 9 |

### Polygon 12

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 355.769 |
| Y-coordinate of center | -116.5798 |
| Radius | 9 |

### Polygon 13

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 355.769 |
| Y-coordinate of center | -233.2464 |
| Radius | 9 |

### Polygon 14

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 205.769 |
| Y-coordinate of center | -233.2464 |
| Radius | 9 |

### Polygon 15

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | 55.769 |
| Y-coordinate of center | -233.2464 |
| Radius | 9 |

### Polygon 16

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -94.231 |
| Y-coordinate of center | -233.2464 |
| Radius | 9 |

### Polygon 17

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -244.231 |
| Y-coordinate of center | -233.2464 |
| Radius | 9 |

### Polygon 18

| Name | D18 |
| --- | --- |
| Foreground material | S460, 1.15 (MPa) |
| Background material | C30, 0.85, 1.5 (MPa) |
| Circle | Yes |
| X-coordinate of center | -244.231 |
| Y-coordinate of center | -83.2464 |
| Radius | 9 |

## Materials

### S460, 1.15 (MPa)

| Stress units | MPa |
| --- | --- |
| Safety factor | 1 |
| Young's modulus | 200000 |
| Yield stress | 400 |
| Max negative strain | -.01 |
| Max neg. strain failure | Yes |
| Max positive strain | .01 |
| Max pos. strain failure | Yes |

| # | Strain (X) | Stress (Υ) | Code |
| --- | --- | --- | --- |
| 1 | -.01 | -400 | 1 |
| 2 | -.002 | -400 | 1 |
| 3 | 0 | 0 | 1 |
| 4 | .002 | 400 | 1 |
| 5 | .01 | 400 |  |

### C30, 0.85, 1.5 (MPa)

| Stress units | MPa |
| --- | --- |
| Safety factor | 1 |
| Young's modulus | 32000 |
| Yield stress | 17 |
| Max negative strain | -.0035 |
| Max neg. strain failure | Yes |
| Max positive strain | 0 |
| Max pos. strain failure | No |

| # | Strain (X) | Stress (Υ) | Code |
| --- | --- | --- | --- |
| 1 | -.0035 | -17 | 1 |
| 2 | -.002 | -17 | 21 |
| 3 | -.0013 | -14.9175 | 22 |
| 4 | 0 | 0 |  |

### S355, 1.1 (MPa)

| Stress units | MPa |
| --- | --- |
| Safety factor | 1 |
| Young's modulus | 200000 |
| Yield stress | 322.7273 |
| Max negative strain | -.01 |
| Max neg. strain failure | Yes |
| Max positive strain | .01 |
| Max pos. strain failure | Yes |

| # | Strain (X) | Stress (Υ) | Code |
| --- | --- | --- | --- |
| 1 | -.01 | -322.7273 | 1 |
| 2 | -.001613636 | -322.7273 | 1 |
| 3 | 0 | 0 | 1 |
| 4 | .001613636 | 322.7273 | 1 |
| 5 | .01 | 322.7273 |  |

# Results

## Final values (X'Y'Z')

| Main moment Y'Y' (KNm) | 843.4246 |
| --- | --- |
| Secondary moment Z'Z' (KNm) | 188.5107 |
| Curvature (1/mm) | 1.992285E-05 |
| Strain at origin | 2.513917E-03 |

## Final values (XYZ)

| Main moment YY (KNm) | 843.4246 |
| --- | --- |
| Secondary moment ZZ (KNm) | 188.5107 |

## Image

## Detailed results

| # | E0 | K | Fx | My'y' | Mz'z' |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0 | 0 | 0 | 0 |
| 2 | 1.46743397345909E-04 | 1.52587890625E-06 | -0.3963 | 165.5734 | 38.7787 |
| 3 | 2.87569452211401E-04 | 3.0517578125E-06 | -0.1541 | 326.7825 | 75.7478 |
| 4 | 4.25157596062965E-04 | 4.57763671875E-06 | 0.0148 | 476.1107 | 109.3284 |
| 5 | 5.76583775931391E-04 | .000006103515625 | -0.0011 | 578.2769 | 133.1686 |
| 6 | 7.31882772779379E-04 | 7.62939453125E-06 | -0.0006 | 662.2086 | 154.6071 |
| 7 | 8.81887878841119E-04 | 9.1552734375E-06 | -0.0106 | 740.6159 | 173.1907 |
| 8 | 1.0726401744716E-03 | 1.068115234375E-05 | 0.0202 | 784.5351 | 185.4268 |
| 9 | 1.30012533365568E-03 | .00001220703125 | 0.0214 | 802.5469 | 188.8038 |
| 10 | 1.53531216326302E-03 | 1.373291015625E-05 | 0.0166 | 814.9908 | 188.4038 |
| 11 | 1.77373558686156E-03 | 1.52587890625E-05 | 0.1624 | 825.3756 | 187.2654 |
| 12 | 2.01519717094973E-03 | 1.678466796875E-05 | -0.4181 | 834.1274 | 186.3099 |
| 13 | 2.25954651513023E-03 | .000018310546875 | 0.3338 | 839.538 | 187.7025 |
| 14 | 2.49971482307692E-03 | 1.983642578125E-05 | -0.4098 | 843.4382 | 188.4706 |
| 15 | 2.50729026976365E-03 | 1.98841094970703E-05 | -0.2049 | 843.5051 | 188.4845 |
| 16 | 2.51112151814917E-03 | 1.99079513549805E-05 | -0.0222 | 843.5257 | 188.4927 |
| 17 | 2.51299741710875E-03 | 1.99198722839356E-05 | -0.0027 | 843.5471 | 188.4954 |
| 18 | 2.51391711679052E-03 | 1.99228525161743E-05 | 0.8194 | 843.4246 | 188.5107 |