Landfill Gas v5.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

Data	3

Landfill Characteristics	3

Model Parameters	3

Gases And Pollutants	3

Waste Acceptance Rates	3

Results	4

Wastes	4

Gases	5

# Project information

| Title: | Sample Project |
| --- | --- |
| Engineer: | TechnoLogismiki |

# Data

## Landfill Characteristics

| Landfill open year | 1970 |
| --- | --- |
| Landfill closure year | 2030 |
| Current year | 1980 |
| Calculations end year | 2110 |

## Model Parameters

| Methane generation rate (1/year) | CAA conventional - 0.05 |
| --- | --- |
| Potential methane generation capacity (m³/Mg) | CAA conventional - 170 |
| NMOC concentration (ppmv as hexane) | CAA - 4000 |
| Methane content (% by volume) | CAA - 50% |

## Gases And Pollutants

| No | Name | Concentration (ppmv) | Molecular Weight | A | B | C |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Total landfill gas | N/A | 30.02 | - | - | - |
| 2 | Methane | N/A | 16.04 | - | - | - |
| 3 | Carbon dioxide | N/A | 44.01 | - | - | - |
| 4 | NMOC | 4000.000 | 86.18 | - | - | - |
| 5 | 1,2-Dichloroethane (ethylene dichloride) | 0.410 | 98.96 | Y | Y | - |

## Waste Acceptance Rates

| Year | Wastes (ton/year) |
| --- | --- |
| 1970 | 15.000 |
| 1971 | 20.000 |
| 1972 | 77.000 |
| 1973 | - |
| 1974 | - |
| 1975 | - |
| 1976 | - |
| 1977 | - |
| 1978 | - |
| 1979 | - |
| 1980 | - |

# Results

## Wastes

| Year | User input | User waste in place | Waste acceptance | Waste in place |
| --- | --- | --- | --- | --- |
| 1970 | 15.000 | 0.000 | 15.000 | 0.000 |
| 1971 | 20.000 | 15.000 | 20.000 | 15.000 |
| 1972 | 77.000 | 35.000 | 77.000 | 35.000 |
| 1973 | 0.000 | 112.000 | 77.000 | 112.000 |
| 1974 | 0.000 | 112.000 | 77.000 | 189.000 |
| 1975 | 0.000 | 112.000 | 77.000 | 266.000 |
| 1976 | 0.000 | 112.000 | 77.000 | 343.000 |
| 1977 | 0.000 | 112.000 | 77.000 | 420.000 |
| 1978 | 0.000 | 112.000 | 77.000 | 497.000 |
| 1979 | 0.000 | 112.000 | 77.000 | 574.000 |
| 1980 | 0.000 | 112.000 | 77.000 | 651.000 |
| 1981 | 0.000 | 112.000 | 77.000 | 728.000 |
| 1982 | 0.000 | 112.000 | 77.000 | 805.000 |
| 1983 | 0.000 | 112.000 | 77.000 | 882.000 |
| 1984 | 0.000 | 112.000 | 77.000 | 959.000 |
| 1985 | 0.000 | 112.000 | 77.000 | 1036.000 |
| 1986 | 0.000 | 112.000 | 77.000 | 1113.000 |
| 1987 | 0.000 | 112.000 | 77.000 | 1190.000 |
| 1988 | 0.000 | 112.000 | 77.000 | 1267.000 |
| 1989 | 0.000 | 112.000 | 77.000 | 1344.000 |
| 1990 | 0.000 | 112.000 | 77.000 | 1421.000 |
| 1991 | 0.000 | 112.000 | 77.000 | 1498.000 |
| 1992 | 0.000 | 112.000 | 77.000 | 1575.000 |
| 1993 | 0.000 | 112.000 | 77.000 | 1652.000 |
| 1994 | 0.000 | 112.000 | 77.000 | 1729.000 |
| 1995 | 0.000 | 112.000 | 77.000 | 1806.000 |
| 1996 | 0.000 | 112.000 | 77.000 | 1883.000 |
| 1997 | 0.000 | 112.000 | 77.000 | 1960.000 |
| 1998 | 0.000 | 112.000 | 77.000 | 2037.000 |
| 1999 | 0.000 | 112.000 | 77.000 | 2114.000 |
| 2000 | 0.000 | 112.000 | 77.000 | 2191.000 |
| 2001 | 0.000 | 112.000 | 77.000 | 2268.000 |
| 2002 | 0.000 | 112.000 | 77.000 | 2345.000 |
| 2003 | 0.000 | 112.000 | 77.000 | 2422.000 |
| 2004 | 0.000 | 112.000 | 77.000 | 2499.000 |
| 2005 | 0.000 | 112.000 | 77.000 | 2576.000 |
| 2006 | 0.000 | 112.000 | 77.000 | 2653.000 |
| 2007 | 0.000 | 112.000 | 77.000 | 2730.000 |
| 2008 | 0.000 | 112.000 | 77.000 | 2807.000 |
| 2009 | 0.000 | 112.000 | 77.000 | 2884.000 |
| 2010 | 0.000 | 112.000 | 77.000 | 2961.000 |
| 2011 | 0.000 | 112.000 | 77.000 | 3038.000 |
| 2012 | 0.000 | 112.000 | 77.000 | 3115.000 |
| 2013 | 0.000 | 112.000 | 77.000 | 3192.000 |
| 2014 | 0.000 | 112.000 | 77.000 | 3269.000 |
| 2015 | 0.000 | 112.000 | 77.000 | 3346.000 |
| 2016 | 0.000 | 112.000 | 77.000 | 3423.000 |
| 2017 | 0.000 | 112.000 | 77.000 | 3500.000 |
| 2018 | 0.000 | 112.000 | 77.000 | 3577.000 |
| 2019 | 0.000 | 112.000 | 77.000 | 3654.000 |
| 2020 | 0.000 | 112.000 | 77.000 | 3731.000 |
| 2021 | 0.000 | 112.000 | 77.000 | 3808.000 |
| 2022 | 0.000 | 112.000 | 77.000 | 3885.000 |
| 2023 | 0.000 | 112.000 | 77.000 | 3962.000 |
| 2024 | 0.000 | 112.000 | 77.000 | 4039.000 |
| 2025 | 0.000 | 112.000 | 77.000 | 4116.000 |
| 2026 | 0.000 | 112.000 | 77.000 | 4193.000 |
| 2027 | 0.000 | 112.000 | 77.000 | 4270.000 |
| 2028 | 0.000 | 112.000 | 77.000 | 4347.000 |
| 2029 | 0.000 | 112.000 | 77.000 | 4424.000 |
| 2030 | 0.000 | 112.000 | 0.000 | 4501.000 |

## Gases

| Year | Methane (m³/year) | Total landfill gas | Methane | Carbon dioxide | NMOC |
| --- | --- | --- | --- | --- | --- |
| 1971 | 124.676 | 249.352 | 124.676 | 124.676 | 0.997 |
| 1972 | 284.830 | 569.661 | 284.830 | 284.830 | 2.279 |
| 1973 | 910.943 | 1821.887 | 910.943 | 910.943 | 7.288 |
| 1974 | 1506.520 | 3013.041 | 1506.520 | 1506.520 | 12.052 |
| 1975 | 2073.051 | 4146.101 | 2073.051 | 2073.051 | 16.584 |
| 1976 | 2611.951 | 5223.902 | 2611.951 | 2611.951 | 20.896 |
| 1977 | 3124.569 | 6249.137 | 3124.569 | 3124.569 | 24.997 |
| 1978 | 3612.186 | 7224.372 | 3612.186 | 3612.186 | 28.897 |
| 1979 | 4076.022 | 8152.043 | 4076.022 | 4076.022 | 32.608 |
| 1980 | 4517.236 | 9034.472 | 4517.236 | 4517.236 | 36.138 |
| 1981 | 4936.932 | 9873.864 | 4936.932 | 4936.932 | 39.495 |
| 1982 | 5336.159 | 10672.318 | 5336.159 | 5336.159 | 42.689 |
| 1983 | 5715.916 | 11431.831 | 5715.916 | 5715.916 | 45.727 |
| 1984 | 6077.151 | 12154.303 | 6077.151 | 6077.151 | 48.617 |
| 1985 | 6420.769 | 12841.539 | 6420.769 | 6420.769 | 51.366 |
| 1986 | 6747.629 | 13495.258 | 6747.629 | 6747.629 | 53.981 |
| 1987 | 7058.547 | 14117.095 | 7058.547 | 7058.547 | 56.468 |
| 1988 | 7354.302 | 14708.604 | 7354.302 | 7354.302 | 58.834 |
| 1989 | 7635.633 | 15271.266 | 7635.633 | 7635.633 | 61.085 |
| 1990 | 7903.243 | 15806.486 | 7903.243 | 7903.243 | 63.226 |
| 1991 | 8157.801 | 16315.603 | 8157.801 | 8157.801 | 65.262 |
| 1992 | 8399.945 | 16799.890 | 8399.945 | 8399.945 | 67.200 |
| 1993 | 8630.279 | 17260.558 | 8630.279 | 8630.279 | 69.042 |
| 1994 | 8849.379 | 17698.759 | 8849.379 | 8849.379 | 70.795 |
| 1995 | 9057.794 | 18115.588 | 9057.794 | 9057.794 | 72.462 |
| 1996 | 9256.045 | 18512.089 | 9256.045 | 9256.045 | 74.048 |
| 1997 | 9444.626 | 18889.252 | 9444.626 | 9444.626 | 75.557 |
| 1998 | 9624.010 | 19248.021 | 9624.010 | 9624.010 | 76.992 |
| 1999 | 9794.646 | 19589.292 | 9794.646 | 9794.646 | 78.357 |
| 2000 | 9956.960 | 19913.919 | 9956.960 | 9956.960 | 79.656 |
| 2001 | 10111.357 | 20222.715 | 10111.357 | 10111.357 | 80.891 |
| 2002 | 10258.225 | 20516.449 | 10258.225 | 10258.225 | 82.066 |
| 2003 | 10397.929 | 20795.859 | 10397.929 | 10397.929 | 83.183 |
| 2004 | 10530.821 | 21061.641 | 10530.821 | 10530.821 | 84.247 |
| 2005 | 10657.231 | 21314.461 | 10657.231 | 10657.231 | 85.258 |
| 2006 | 10777.475 | 21554.951 | 10777.475 | 10777.475 | 86.220 |
| 2007 | 10891.856 | 21783.712 | 10891.856 | 10891.856 | 87.135 |
| 2008 | 11000.658 | 22001.316 | 11000.658 | 11000.658 | 88.005 |
| 2009 | 11104.154 | 22208.308 | 11104.154 | 11104.154 | 88.833 |
| 2010 | 11202.602 | 22405.204 | 11202.602 | 11202.602 | 89.621 |
| 2011 | 11296.249 | 22592.498 | 11296.249 | 11296.249 | 90.370 |
| 2012 | 11385.328 | 22770.657 | 11385.328 | 11385.328 | 91.083 |
| 2013 | 11470.064 | 22940.127 | 11470.064 | 11470.064 | 91.761 |
| 2014 | 11550.666 | 23101.332 | 11550.666 | 11550.666 | 92.405 |
| 2015 | 11627.338 | 23254.676 | 11627.338 | 11627.338 | 93.019 |
| 2016 | 11700.270 | 23400.540 | 11700.270 | 11700.270 | 93.602 |
| 2017 | 11769.645 | 23539.291 | 11769.645 | 11769.645 | 94.157 |
| 2018 | 11835.637 | 23671.274 | 11835.637 | 11835.637 | 94.685 |
| 2019 | 11898.410 | 23796.821 | 11898.410 | 11898.410 | 95.187 |
| 2020 | 11958.122 | 23916.245 | 11958.122 | 11958.122 | 95.665 |
| 2021 | 12014.922 | 24029.844 | 12014.922 | 12014.922 | 96.119 |
| 2022 | 12068.951 | 24137.903 | 12068.951 | 12068.951 | 96.552 |
| 2023 | 12120.346 | 24240.692 | 12120.346 | 12120.346 | 96.963 |
| 2024 | 12169.234 | 24338.468 | 12169.234 | 12169.234 | 97.354 |
| 2025 | 12215.738 | 24431.475 | 12215.738 | 12215.738 | 97.726 |
| 2026 | 12259.973 | 24519.946 | 12259.973 | 12259.973 | 98.080 |
| 2027 | 12302.051 | 24604.103 | 12302.051 | 12302.051 | 98.416 |
| 2028 | 12342.077 | 24684.155 | 12342.077 | 12342.077 | 98.737 |
| 2029 | 12380.151 | 24760.303 | 12380.151 | 12380.151 | 99.041 |
| 2030 | 12416.368 | 24832.737 | 12416.368 | 12416.368 | 99.331 |
| 2031 | 11810.815 | 23621.630 | 11810.815 | 11810.815 | 94.487 |
| 2032 | 11234.795 | 22469.590 | 11234.795 | 11234.795 | 89.878 |
| 2033 | 10686.867 | 21373.735 | 10686.867 | 10686.867 | 85.495 |
| 2034 | 10165.663 | 20331.325 | 10165.663 | 10165.663 | 81.325 |
| 2035 | 9669.877 | 19339.755 | 9669.877 | 9669.877 | 77.359 |
| 2036 | 9198.272 | 18396.544 | 9198.272 | 9198.272 | 73.586 |
| 2037 | 8749.667 | 17499.334 | 8749.667 | 8749.667 | 69.997 |
| 2038 | 8322.941 | 16645.881 | 8322.941 | 8322.941 | 66.584 |
| 2039 | 7917.026 | 15834.052 | 7917.026 | 7917.026 | 63.336 |
| 2040 | 7530.908 | 15061.816 | 7530.908 | 7530.908 | 60.247 |
| 2041 | 7163.621 | 14327.243 | 7163.621 | 7163.621 | 57.309 |
| 2042 | 6814.247 | 13628.495 | 6814.247 | 6814.247 | 54.514 |
| 2043 | 6481.913 | 12963.825 | 6481.913 | 6481.913 | 51.855 |
| 2044 | 6165.786 | 12331.572 | 6165.786 | 6165.786 | 49.326 |
| 2045 | 5865.077 | 11730.154 | 5865.077 | 5865.077 | 46.921 |
| 2046 | 5579.034 | 11158.068 | 5579.034 | 5579.034 | 44.632 |
| 2047 | 5306.941 | 10613.883 | 5306.941 | 5306.941 | 42.456 |
| 2048 | 5048.119 | 10096.237 | 5048.119 | 5048.119 | 40.385 |
| 2049 | 4801.919 | 9603.838 | 4801.919 | 4801.919 | 38.415 |
| 2050 | 4567.727 | 9135.453 | 4567.727 | 4567.727 | 36.542 |
| 2051 | 4344.956 | 8689.912 | 4344.956 | 4344.956 | 34.760 |
| 2052 | 4133.050 | 8266.100 | 4133.050 | 4133.050 | 33.064 |
| 2053 | 3931.479 | 7862.958 | 3931.479 | 3931.479 | 31.452 |
| 2054 | 3739.738 | 7479.477 | 3739.738 | 3739.738 | 29.918 |
| 2055 | 3557.349 | 7114.698 | 3557.349 | 3557.349 | 28.459 |
| 2056 | 3383.855 | 6767.710 | 3383.855 | 3383.855 | 27.071 |
| 2057 | 3218.823 | 6437.645 | 3218.823 | 3218.823 | 25.751 |
| 2058 | 3061.839 | 6123.678 | 3061.839 | 3061.839 | 24.495 |
| 2059 | 2912.511 | 5825.022 | 2912.511 | 2912.511 | 23.300 |
| 2060 | 2770.466 | 5540.933 | 2770.466 | 2770.466 | 22.164 |
| 2061 | 2635.349 | 5270.698 | 2635.349 | 2635.349 | 21.083 |
| 2062 | 2506.822 | 5013.643 | 2506.822 | 2506.822 | 20.055 |
| 2063 | 2384.562 | 4769.125 | 2384.562 | 2384.562 | 19.076 |
| 2064 | 2268.266 | 4536.532 | 2268.266 | 2268.266 | 18.146 |
| 2065 | 2157.641 | 4315.283 | 2157.641 | 2157.641 | 17.261 |
| 2066 | 2052.412 | 4104.824 | 2052.412 | 2052.412 | 16.419 |
| 2067 | 1952.315 | 3904.629 | 1952.315 | 1952.315 | 15.619 |
| 2068 | 1857.099 | 3714.198 | 1857.099 | 1857.099 | 14.857 |
| 2069 | 1766.527 | 3533.055 | 1766.527 | 1766.527 | 14.132 |
| 2070 | 1680.373 | 3360.745 | 1680.373 | 1680.373 | 13.443 |
| 2071 | 1598.420 | 3196.840 | 1598.420 | 1598.420 | 12.787 |
| 2072 | 1520.464 | 3040.928 | 1520.464 | 1520.464 | 12.164 |
| 2073 | 1446.310 | 2892.620 | 1446.310 | 1446.310 | 11.570 |
| 2074 | 1375.773 | 2751.546 | 1375.773 | 1375.773 | 11.006 |
| 2075 | 1308.676 | 2617.351 | 1308.676 | 1308.676 | 10.469 |
| 2076 | 1244.851 | 2489.701 | 1244.851 | 1244.851 | 9.959 |
| 2077 | 1184.139 | 2368.277 | 1184.139 | 1184.139 | 9.473 |
| 2078 | 1126.388 | 2252.775 | 1126.388 | 1126.388 | 9.011 |
| 2079 | 1071.453 | 2142.906 | 1071.453 | 1071.453 | 8.572 |
| 2080 | 1019.198 | 2038.395 | 1019.198 | 1019.198 | 8.154 |
| 2081 | 969.491 | 1938.981 | 969.491 | 969.491 | 7.756 |
| 2082 | 922.208 | 1844.416 | 922.208 | 922.208 | 7.378 |
| 2083 | 877.231 | 1754.463 | 877.231 | 877.231 | 7.018 |
| 2084 | 834.448 | 1668.897 | 834.448 | 834.448 | 6.676 |
| 2085 | 793.752 | 1587.504 | 793.752 | 793.752 | 6.350 |
| 2086 | 755.040 | 1510.080 | 755.040 | 755.040 | 6.040 |
| 2087 | 718.216 | 1436.433 | 718.216 | 718.216 | 5.746 |
| 2088 | 683.189 | 1366.377 | 683.189 | 683.189 | 5.466 |
| 2089 | 649.869 | 1299.738 | 649.869 | 649.869 | 5.199 |
| 2090 | 618.175 | 1236.349 | 618.175 | 618.175 | 4.945 |
| 2091 | 588.026 | 1176.052 | 588.026 | 588.026 | 4.704 |
| 2092 | 559.347 | 1118.695 | 559.347 | 559.347 | 4.475 |
| 2093 | 532.068 | 1064.136 | 532.068 | 532.068 | 4.257 |
| 2094 | 506.119 | 1012.237 | 506.119 | 506.119 | 4.049 |
| 2095 | 481.435 | 962.870 | 481.435 | 481.435 | 3.851 |
| 2096 | 457.955 | 915.910 | 457.955 | 457.955 | 3.664 |
| 2097 | 435.620 | 871.241 | 435.620 | 435.620 | 3.485 |
| 2098 | 414.375 | 828.750 | 414.375 | 414.375 | 3.315 |
| 2099 | 394.166 | 788.331 | 394.166 | 394.166 | 3.153 |
| 2100 | 374.942 | 749.884 | 374.942 | 374.942 | 3.000 |
| 2101 | 356.656 | 713.311 | 356.656 | 356.656 | 2.853 |
| 2102 | 339.261 | 678.523 | 339.261 | 339.261 | 2.714 |
| 2103 | 322.715 | 645.431 | 322.715 | 322.715 | 2.582 |
| 2104 | 306.976 | 613.953 | 306.976 | 306.976 | 2.456 |
| 2105 | 292.005 | 584.010 | 292.005 | 292.005 | 2.336 |
| 2106 | 277.764 | 555.527 | 277.764 | 277.764 | 2.222 |
| 2107 | 264.217 | 528.434 | 264.217 | 264.217 | 2.114 |
| 2108 | 251.331 | 502.662 | 251.331 | 251.331 | 2.011 |
| 2109 | 239.073 | 478.147 | 239.073 | 239.073 | 1.913 |
| 2110 | 227.414 | 454.827 | 227.414 | 227.414 | 1.819 |

| Year | 1,2-Dichloroethane (ethylene dichloride) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 1971 | 0.000 |  |  |  |  |
| 1972 | 0.000 |  |  |  |  |
| 1973 | 0.001 |  |  |  |  |
| 1974 | 0.001 |  |  |  |  |
| 1975 | 0.002 |  |  |  |  |
| 1976 | 0.002 |  |  |  |  |
| 1977 | 0.003 |  |  |  |  |
| 1978 | 0.003 |  |  |  |  |
| 1979 | 0.003 |  |  |  |  |
| 1980 | 0.004 |  |  |  |  |
| 1981 | 0.004 |  |  |  |  |
| 1982 | 0.004 |  |  |  |  |
| 1983 | 0.005 |  |  |  |  |
| 1984 | 0.005 |  |  |  |  |
| 1985 | 0.005 |  |  |  |  |
| 1986 | 0.006 |  |  |  |  |
| 1987 | 0.006 |  |  |  |  |
| 1988 | 0.006 |  |  |  |  |
| 1989 | 0.006 |  |  |  |  |
| 1990 | 0.006 |  |  |  |  |
| 1991 | 0.007 |  |  |  |  |
| 1992 | 0.007 |  |  |  |  |
| 1993 | 0.007 |  |  |  |  |
| 1994 | 0.007 |  |  |  |  |
| 1995 | 0.007 |  |  |  |  |
| 1996 | 0.008 |  |  |  |  |
| 1997 | 0.008 |  |  |  |  |
| 1998 | 0.008 |  |  |  |  |
| 1999 | 0.008 |  |  |  |  |
| 2000 | 0.008 |  |  |  |  |
| 2001 | 0.008 |  |  |  |  |
| 2002 | 0.008 |  |  |  |  |
| 2003 | 0.009 |  |  |  |  |
| 2004 | 0.009 |  |  |  |  |
| 2005 | 0.009 |  |  |  |  |
| 2006 | 0.009 |  |  |  |  |
| 2007 | 0.009 |  |  |  |  |
| 2008 | 0.009 |  |  |  |  |
| 2009 | 0.009 |  |  |  |  |
| 2010 | 0.009 |  |  |  |  |
| 2011 | 0.009 |  |  |  |  |
| 2012 | 0.009 |  |  |  |  |
| 2013 | 0.009 |  |  |  |  |
| 2014 | 0.009 |  |  |  |  |
| 2015 | 0.010 |  |  |  |  |
| 2016 | 0.010 |  |  |  |  |
| 2017 | 0.010 |  |  |  |  |
| 2018 | 0.010 |  |  |  |  |
| 2019 | 0.010 |  |  |  |  |
| 2020 | 0.010 |  |  |  |  |
| 2021 | 0.010 |  |  |  |  |
| 2022 | 0.010 |  |  |  |  |
| 2023 | 0.010 |  |  |  |  |
| 2024 | 0.010 |  |  |  |  |
| 2025 | 0.010 |  |  |  |  |
| 2026 | 0.010 |  |  |  |  |
| 2027 | 0.010 |  |  |  |  |
| 2028 | 0.010 |  |  |  |  |
| 2029 | 0.010 |  |  |  |  |
| 2030 | 0.010 |  |  |  |  |
| 2031 | 0.010 |  |  |  |  |
| 2032 | 0.009 |  |  |  |  |
| 2033 | 0.009 |  |  |  |  |
| 2034 | 0.008 |  |  |  |  |
| 2035 | 0.008 |  |  |  |  |
| 2036 | 0.008 |  |  |  |  |
| 2037 | 0.007 |  |  |  |  |
| 2038 | 0.007 |  |  |  |  |
| 2039 | 0.006 |  |  |  |  |
| 2040 | 0.006 |  |  |  |  |
| 2041 | 0.006 |  |  |  |  |
| 2042 | 0.006 |  |  |  |  |
| 2043 | 0.005 |  |  |  |  |
| 2044 | 0.005 |  |  |  |  |
| 2045 | 0.005 |  |  |  |  |
| 2046 | 0.005 |  |  |  |  |
| 2047 | 0.004 |  |  |  |  |
| 2048 | 0.004 |  |  |  |  |
| 2049 | 0.004 |  |  |  |  |
| 2050 | 0.004 |  |  |  |  |
| 2051 | 0.004 |  |  |  |  |
| 2052 | 0.003 |  |  |  |  |
| 2053 | 0.003 |  |  |  |  |
| 2054 | 0.003 |  |  |  |  |
| 2055 | 0.003 |  |  |  |  |
| 2056 | 0.003 |  |  |  |  |
| 2057 | 0.003 |  |  |  |  |
| 2058 | 0.003 |  |  |  |  |
| 2059 | 0.002 |  |  |  |  |
| 2060 | 0.002 |  |  |  |  |
| 2061 | 0.002 |  |  |  |  |
| 2062 | 0.002 |  |  |  |  |
| 2063 | 0.002 |  |  |  |  |
| 2064 | 0.002 |  |  |  |  |
| 2065 | 0.002 |  |  |  |  |
| 2066 | 0.002 |  |  |  |  |
| 2067 | 0.002 |  |  |  |  |
| 2068 | 0.002 |  |  |  |  |
| 2069 | 0.001 |  |  |  |  |
| 2070 | 0.001 |  |  |  |  |
| 2071 | 0.001 |  |  |  |  |
| 2072 | 0.001 |  |  |  |  |
| 2073 | 0.001 |  |  |  |  |
| 2074 | 0.001 |  |  |  |  |
| 2075 | 0.001 |  |  |  |  |
| 2076 | 0.001 |  |  |  |  |
| 2077 | 0.001 |  |  |  |  |
| 2078 | 0.001 |  |  |  |  |
| 2079 | 0.001 |  |  |  |  |
| 2080 | 0.001 |  |  |  |  |
| 2081 | 0.001 |  |  |  |  |
| 2082 | 0.001 |  |  |  |  |
| 2083 | 0.001 |  |  |  |  |
| 2084 | 0.001 |  |  |  |  |
| 2085 | 0.001 |  |  |  |  |
| 2086 | 0.001 |  |  |  |  |
| 2087 | 0.001 |  |  |  |  |
| 2088 | 0.001 |  |  |  |  |
| 2089 | 0.001 |  |  |  |  |
| 2090 | 0.001 |  |  |  |  |
| 2091 | 0.000 |  |  |  |  |
| 2092 | 0.000 |  |  |  |  |
| 2093 | 0.000 |  |  |  |  |
| 2094 | 0.000 |  |  |  |  |
| 2095 | 0.000 |  |  |  |  |
| 2096 | 0.000 |  |  |  |  |
| 2097 | 0.000 |  |  |  |  |
| 2098 | 0.000 |  |  |  |  |
| 2099 | 0.000 |  |  |  |  |
| 2100 | 0.000 |  |  |  |  |
| 2101 | 0.000 |  |  |  |  |
| 2102 | 0.000 |  |  |  |  |
| 2103 | 0.000 |  |  |  |  |
| 2104 | 0.000 |  |  |  |  |
| 2105 | 0.000 |  |  |  |  |
| 2106 | 0.000 |  |  |  |  |
| 2107 | 0.000 |  |  |  |  |
| 2108 | 0.000 |  |  |  |  |
| 2109 | 0.000 |  |  |  |  |
| 2110 | 0.000 |  |  |  |  |