Significant Wave v1.0 - Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Project information	3

Input Data	3

General data	3

Calculation Point P1	3

Calculation Point P2	3

Results	3

Results for : P1	3

Distances for N	3

Distances for NE	4

Distances for E	4

Distances for SE	5

Distances for S	6

Distances for SW	6

Distances for W	7

Distances for NW	7

Distances for fetch-control	8

Final SMB results	8

Results for : P2	9

Distances for N	9

Distances for NE	9

Distances for E	10

Distances for SE	10

Distances for S	11

Distances for SW	11

Distances for W	12

Distances for NW	13

Distances for fetch-control	13

Final SMB results	13

Sketch	14

# Project information

| Title | Sample 1 |
| --- | --- |
| Author | TechnoLogismiki |
| Comments | Comments here |

# Input Data

## General data

| Use of Cos^2 or Cos | Cos |
| --- | --- |
| Angle step (deg) | 5.000 |

## Calculation Point P1

| Name | P1 |
| --- | --- |
| X Coordinate | 582074.851 |
| Y Coordinate | 4278570.717 |

## Calculation Point P2

| Name | P2 |
| --- | --- |
| X Coordinate | 509058.354 |
| Y Coordinate | 4357483.303 |

# Results

## Results for : P1

### Distances for N

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | -45.000 | 107779.162 | 0.707 | 76211.376 |
| -40.000 | -40.000 | 106753.807 | 0.766 | 81778.16 |
| -35.000 | -35.000 | 95355.284 | 0.819 | 78110.475 |
| -30.000 | -30.000 | 165667.595 | 0.866 | 143472.346 |
| -25.000 | -25.000 | 202920.046 | 0.906 | 183908.018 |
| -20.000 | -20.000 | 180389.303 | 0.940 | 169510.497 |
| -15.000 | -15.000 | 243836.886 | 0.966 | 235528.345 |
| -10.000 | -10.000 | 223140.942 | 0.985 | 219750.93 |
| -5.000 | -5.000 | 235337.299 | 0.996 | 234441.77 |
| 0.000 | 0.000 | 252371.795 | 1.000 | 252371.795 |
| 5.000 | 5.000 | 97853.358 | 0.996 | 97480.996 |
| 10.000 | 10.000 | 130231.694 | 0.985 | 128253.182 |
| 15.000 | 15.000 | 130120.554 | 0.966 | 125686.804 |
| 20.000 | 20.000 | 178350.626 | 0.940 | 167594.767 |
| 25.000 | 25.000 | 195420.686 | 0.906 | 177111.29 |
| 30.000 | 30.000 | 218826.076 | 0.866 | 189508.941 |
| 35.000 | 35.000 | 158118.428 | 0.819 | 129523.033 |
| 40.000 | 40.000 | 158849.538 | 0.766 | 121685.806 |
| 45.000 | 45.000 | 135464.134 | 0.707 | 95787.607 |
|  |  | Sum | 16.903 | 2907716.139 |

### Distances for NE

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 0.000 | 252371.795 | 0.707 | 178453.808 |
| -40.000 | 5.000 | 97853.358 | 0.766 | 74960.021 |
| -35.000 | 10.000 | 130231.694 | 0.819 | 106679.558 |
| -30.000 | 15.000 | 130120.554 | 0.866 | 112687.706 |
| -25.000 | 20.000 | 178350.626 | 0.906 | 161640.561 |
| -20.000 | 25.000 | 195420.686 | 0.940 | 183635.377 |
| -15.000 | 30.000 | 218826.076 | 0.966 | 211369.758 |
| -10.000 | 35.000 | 158118.428 | 0.985 | 155716.253 |
| -5.000 | 40.000 | 158849.538 | 0.996 | 158245.068 |
| 0.000 | 45.000 | 135464.134 | 1.000 | 135464.134 |
| 5.000 | 50.000 | 100409.945 | 0.996 | 100027.855 |
| 10.000 | 55.000 | 97814.292 | 0.985 | 96328.273 |
| 15.000 | 60.000 | 102950.575 | 0.966 | 99442.619 |
| 20.000 | 65.000 | 111322.236 | 0.940 | 104608.684 |
| 25.000 | 70.000 | 120754.629 | 0.906 | 109440.861 |
| 30.000 | 75.000 | 164268.619 | 0.866 | 142260.797 |
| 35.000 | 80.000 | 184591.157 | 0.819 | 151208.224 |
| 40.000 | 85.000 | 162907.294 | 0.766 | 124794.227 |
| 45.000 | 90.000 | 122756.251 | 0.707 | 86801.778 |
|  |  | Sum | 16.903 | 2493765.561 |

### Distances for E

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 45.000 | 135464.134 | 0.707 | 95787.607 |
| -40.000 | 50.000 | 100409.945 | 0.766 | 76918.48 |
| -35.000 | 55.000 | 97814.292 | 0.819 | 80124.777 |
| -30.000 | 60.000 | 102950.575 | 0.866 | 89157.813 |
| -25.000 | 65.000 | 111322.236 | 0.906 | 100892.209 |
| -20.000 | 70.000 | 120754.629 | 0.940 | 113472.234 |
| -15.000 | 75.000 | 164268.619 | 0.966 | 158671.302 |
| -10.000 | 80.000 | 184591.157 | 0.985 | 181786.803 |
| -5.000 | 85.000 | 162907.294 | 0.996 | 162287.383 |
| 0.000 | 90.000 | 122756.251 | 1.000 | 122756.251 |
| 5.000 | 95.000 | 54582.29 | 0.996 | 54374.588 |
| 10.000 | 100.000 | 59124.641 | 0.985 | 58226.405 |
| 15.000 | 105.000 | 50566.931 | 0.966 | 48843.905 |
| 20.000 | 110.000 | 97108.242 | 0.940 | 91251.899 |
| 25.000 | 115.000 | 92784.479 | 0.906 | 84091.296 |
| 30.000 | 120.000 | 99813.369 | 0.866 | 86440.913 |
| 35.000 | 125.000 | 182037.977 | 0.819 | 149116.781 |
| 40.000 | 130.000 | 163493.149 | 0.766 | 125243.018 |
| 45.000 | 135.000 | 164513.533 | 0.707 | 116328.635 |
|  |  | Sum | 16.903 | 1995772.301 |

### Distances for SE

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 90.000 | 122756.251 | 0.707 | 86801.778 |
| -40.000 | 95.000 | 54582.29 | 0.766 | 41812.46 |
| -35.000 | 100.000 | 59124.641 | 0.819 | 48432.071 |
| -30.000 | 105.000 | 50566.931 | 0.866 | 43792.247 |
| -25.000 | 110.000 | 97108.242 | 0.906 | 88009.956 |
| -20.000 | 115.000 | 92784.479 | 0.940 | 87188.89 |
| -15.000 | 120.000 | 99813.369 | 0.966 | 96412.311 |
| -10.000 | 125.000 | 182037.977 | 0.985 | 179272.411 |
| -5.000 | 130.000 | 163493.149 | 0.996 | 162871.008 |
| 0.000 | 135.000 | 164513.533 | 1.000 | 164513.533 |
| 5.000 | 140.000 | 151031.719 | 0.996 | 150456.998 |
| 10.000 | 145.000 | Ν/Α |  |  |
| 15.000 | 150.000 | 222247.458 | 0.966 | 214674.559 |
| 20.000 | 155.000 | 185877.802 | 0.940 | 174667.999 |
| 25.000 | 160.000 | 141389.219 | 0.906 | 128142.15 |
| 30.000 | 165.000 | 132937.476 | 0.866 | 115127.231 |
| 35.000 | 170.000 | 113494.412 | 0.819 | 92969.179 |
| 40.000 | 175.000 | 108802.136 | 0.766 | 83347.272 |
| 45.000 | 180.000 | 83450.052 | 0.707 | 59008.097 |
|  |  | Sum | 15.918 | 2017500.152 |

### Distances for S

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 135.000 | 164513.533 | 0.707 | 116328.635 |
| -40.000 | 140.000 | 151031.719 | 0.766 | 115697.009 |
| -35.000 | 145.000 | Ν/Α |  |  |
| -30.000 | 150.000 | 222247.458 | 0.866 | 192471.944 |
| -25.000 | 155.000 | 185877.802 | 0.906 | 168462.5 |
| -20.000 | 160.000 | 141389.219 | 0.940 | 132862.406 |
| -15.000 | 165.000 | 132937.476 | 0.966 | 128407.741 |
| -10.000 | 170.000 | 113494.412 | 0.985 | 111770.177 |
| -5.000 | 175.000 | 108802.136 | 0.996 | 108388.111 |
| 0.000 | 180.000 | 83450.052 | 1.000 | 83450.052 |
| 5.000 | 185.000 | 82789.182 | 0.996 | 82474.144 |
| 10.000 | 190.000 | 74009.054 | 0.985 | 72884.69 |
| 15.000 | 195.000 | 78688.703 | 0.966 | 76007.45 |
| 20.000 | 200.000 | 144189.575 | 0.940 | 135493.88 |
| 25.000 | 205.000 | 72373.772 | 0.906 | 65592.913 |
| 30.000 | 210.000 | 65647.388 | 0.866 | 56852.305 |
| 35.000 | 215.000 | 69811.091 | 0.819 | 57185.898 |
| 40.000 | 220.000 | 72910.328 | 0.766 | 55852.551 |
| 45.000 | 225.000 | 75240.016 | 0.707 | 53202.726 |
|  |  | Sum | 16.083 | 1813385.133 |

### Distances for SW

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 180.000 | 83450.052 | 0.707 | 59008.097 |
| -40.000 | 185.000 | 82789.182 | 0.766 | 63420.193 |
| -35.000 | 190.000 | 74009.054 | 0.819 | 60624.668 |
| -30.000 | 195.000 | 78688.703 | 0.866 | 68146.415 |
| -25.000 | 200.000 | 144189.575 | 0.906 | 130680.135 |
| -20.000 | 205.000 | 72373.772 | 0.940 | 68009.1 |
| -15.000 | 210.000 | 65647.388 | 0.966 | 63410.507 |
| -10.000 | 215.000 | 69811.091 | 0.985 | 68750.504 |
| -5.000 | 220.000 | 72910.328 | 0.996 | 72632.882 |
| 0.000 | 225.000 | 75240.016 | 1.000 | 75240.016 |
| 5.000 | 230.000 | 77387.856 | 0.996 | 77093.372 |
| 10.000 | 235.000 | 72945.485 | 0.985 | 71837.279 |
| 15.000 | 240.000 | 72630.86 | 0.966 | 70156.023 |
| 20.000 | 245.000 | 71617.863 | 0.940 | 67298.778 |
| 25.000 | 250.000 | 70095.318 | 0.906 | 63527.933 |
| 30.000 | 255.000 | 66358.226 | 0.866 | 57467.91 |
| 35.000 | 260.000 | 67068.915 | 0.819 | 54939.639 |
| 40.000 | 265.000 | 71802.848 | 0.766 | 55004.173 |
| 45.000 | 270.000 | 68905.136 | 0.707 | 48723.289 |
|  |  | Sum | 16.903 | 1295970.912 |

### Distances for W

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 225.000 | 75240.016 | 0.707 | 53202.726 |
| -40.000 | 230.000 | 77387.856 | 0.766 | 59282.537 |
| -35.000 | 235.000 | 72945.485 | 0.819 | 59753.443 |
| -30.000 | 240.000 | 72630.86 | 0.866 | 62900.17 |
| -25.000 | 245.000 | 71617.863 | 0.906 | 64907.827 |
| -20.000 | 250.000 | 70095.318 | 0.940 | 65868.053 |
| -15.000 | 255.000 | 66358.226 | 0.966 | 64097.125 |
| -10.000 | 260.000 | 67068.915 | 0.985 | 66049.987 |
| -5.000 | 265.000 | 71802.848 | 0.996 | 71529.616 |
| 0.000 | 270.000 | 68905.136 | 1.000 | 68905.136 |
| 5.000 | 275.000 | 105876.766 | 0.996 | 105473.873 |
| 10.000 | 280.000 | 132246.35 | 0.985 | 130237.231 |
| 15.000 | 285.000 | 141335.348 | 0.966 | 136519.463 |
| 20.000 | 290.000 | 29591.154 | 0.940 | 27806.589 |
| 25.000 | 295.000 | 28389.3 | 0.906 | 25729.444 |
| 30.000 | 300.000 | 26364.838 | 0.866 | 22832.619 |
| 35.000 | 305.000 | 28037.238 | 0.819 | 22966.761 |
| 40.000 | 310.000 | 42496.413 | 0.766 | 32554.141 |
| 45.000 | 315.000 | 107779.162 | 0.707 | 76211.376 |
|  |  | Sum | 16.903 | 1216828.118 |

### Distances for NW

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 270.000 | 68905.136 | 0.707 | 48723.289 |
| -40.000 | 275.000 | 105876.766 | 0.766 | 81106.309 |
| -35.000 | 280.000 | 132246.35 | 0.819 | 108329.868 |
| -30.000 | 285.000 | 141335.348 | 0.866 | 122400.002 |
| -25.000 | 290.000 | 29591.154 | 0.906 | 26818.693 |
| -20.000 | 295.000 | 28389.3 | 0.940 | 26677.216 |
| -15.000 | 300.000 | 26364.838 | 0.966 | 25466.478 |
| -10.000 | 305.000 | 28037.238 | 0.985 | 27611.289 |
| -5.000 | 310.000 | 42496.413 | 0.996 | 42334.701 |
| 0.000 | 315.000 | 107779.162 | 1.000 | 107779.162 |
| 5.000 | 320.000 | 106753.807 | 0.996 | 106347.576 |
| 10.000 | 325.000 | 95355.284 | 0.985 | 93906.623 |
| 15.000 | 330.000 | 165667.595 | 0.966 | 160022.609 |
| 20.000 | 335.000 | 202920.046 | 0.940 | 190682.47 |
| 25.000 | 340.000 | 180389.303 | 0.906 | 163488.23 |
| 30.000 | 345.000 | 243836.886 | 0.866 | 211168.937 |
| 35.000 | 350.000 | 223140.942 | 0.819 | 182786.359 |
| 40.000 | 355.000 | 235337.299 | 0.766 | 180278.83 |
| 45.000 | 360.000 | 252371.795 | 0.707 | 178453.808 |
|  |  | Sum | 16.903 | 2084382.449 |

## Distances for fetch-control

|  | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| F.eff | 172028.612 | 147538.139 | 118075.466 | 126745.652 | 112749.129 | 76673.26 | 71990.952 | 123317.89 |

## Final SMB results

| Beaufort | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 1 | 0.055 | 0.043 | 0.06 | 0.052 | 0.048 | 0.038 | 0.058 | 0.062 |
| 2 | 0.288 | 0.223 | 0.29 | 0.281 | 0.229 | 0.151 | 0.272 | 0.292 |
| 3 | 0.627 | 0.412 | 0.663 | 0.673 | 0.369 | 0.247 | 0.589 | 0.67 |
| 4 | 0.801 | 0.53 | 1.171 | 1.091 | 0.369 | 0.308 | 1.005 | 1.185 |
| 5 | 0.552 | 0.29 | 1.173 | 0.766 | 0.363 | 0.29 | 0.891 | 1.118 |
| 6 | 0.286 | 0.358 | 0.833 | 0.571 | 0.195 | 0.286 | 0.694 | 0.8 |
| 7 | 0 | 0 | 0.573 | 0 | 0.266 | 0.266 | 0.266 | 0.39 |
| 8 | 0 | 0 | 0.515 | 0 | 0 | 0 | 0 | 0.35 |
| 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| maxHs (m) | 0.801 | 0.53 | 1.173 | 1.091 | 0.369 | 0.308 | 1.005 | 1.185 |
| Ts (s) | 3.568 | 2.872 | 4.296 | 4.187 | 2.42 | 2.136 | 4.012 | 4.374 |
| D (hr) | 4.836 | 2.083 | 4.092 | 9.97 | 3.199 | 0.744 | 8.11 | 12.482 |

## Results for : P2

### Distances for N

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | -45.000 | 175017.09 | 0.707 | 123755.771 |
| -40.000 | -40.000 | 87645.572 | 0.766 | 67140.403 |
| -35.000 | -35.000 | 75056.259 | 0.819 | 61482.488 |
| -30.000 | -30.000 | 69816.292 | 0.866 | 60462.683 |
| -25.000 | -25.000 | 105017.213 | 0.906 | 95177.918 |
| -20.000 | -20.000 | 77354.489 | 0.940 | 72689.443 |
| -15.000 | -15.000 | 68286.079 | 0.966 | 65959.288 |
| -10.000 | -10.000 | 65187.021 | 0.985 | 64196.684 |
| -5.000 | -5.000 | 105572.569 | 0.996 | 105170.834 |
| 0.000 | 0.000 | 102037.066 | 1.000 | 102037.066 |
| 5.000 | 5.000 | 96132.766 | 0.996 | 95766.952 |
| 10.000 | 10.000 | 88128.096 | 0.985 | 86789.232 |
| 15.000 | 15.000 | 87898.898 | 0.966 | 84903.816 |
| 20.000 | 20.000 | 144883.344 | 0.940 | 136145.81 |
| 25.000 | 25.000 | 16051.607 | 0.906 | 14547.696 |
| 30.000 | 30.000 | 202737.502 | 0.866 | 175575.827 |
| 35.000 | 35.000 | 205624.68 | 0.819 | 168437.877 |
| 40.000 | 40.000 | 215997.267 | 0.766 | 165463.506 |
| 45.000 | 45.000 | 7773.795 | 0.707 | 5496.903 |
|  |  | Sum | 16.903 | 1751200.195 |

### Distances for NE

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 0.000 | 102037.066 | 0.707 | 72151.101 |
| -40.000 | 5.000 | 96132.766 | 0.766 | 73641.971 |
| -35.000 | 10.000 | 88128.096 | 0.819 | 72190.31 |
| -30.000 | 15.000 | 87898.898 | 0.866 | 76122.679 |
| -25.000 | 20.000 | 144883.344 | 0.906 | 131308.903 |
| -20.000 | 25.000 | 16051.607 | 0.940 | 15083.576 |
| -15.000 | 30.000 | 202737.502 | 0.966 | 195829.39 |
| -10.000 | 35.000 | 205624.68 | 0.985 | 202500.779 |
| -5.000 | 40.000 | 215997.267 | 0.996 | 215175.332 |
| 0.000 | 45.000 | 7773.795 | 1.000 | 7773.795 |
| 5.000 | 50.000 | 5712.043 | 0.996 | 5690.307 |
| 10.000 | 55.000 | 5399.805 | 0.985 | 5317.77 |
| 15.000 | 60.000 | 4800.651 | 0.966 | 4637.073 |
| 20.000 | 65.000 | 4688.591 | 0.940 | 4405.834 |
| 25.000 | 70.000 | 4313.201 | 0.906 | 3909.088 |
| 30.000 | 75.000 | 3868.874 | 0.866 | 3350.543 |
| 35.000 | 80.000 | 2914.703 | 0.819 | 2387.585 |
| 40.000 | 85.000 | 2391.585 | 0.766 | 1832.06 |
| 45.000 | 90.000 | 4905.711 | 0.707 | 3468.862 |
|  |  | Sum | 16.903 | 1096776.957 |

### Distances for E

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 45.000 | 7773.795 | 0.707 | 5496.903 |
| -40.000 | 50.000 | 5712.043 | 0.766 | 4375.679 |
| -35.000 | 55.000 | 5399.805 | 0.819 | 4423.261 |
| -30.000 | 60.000 | 4800.651 | 0.866 | 4157.486 |
| -25.000 | 65.000 | 4688.591 | 0.906 | 4249.306 |
| -20.000 | 70.000 | 4313.201 | 0.940 | 4053.084 |
| -15.000 | 75.000 | 3868.874 | 0.966 | 3737.045 |
| -10.000 | 80.000 | 2914.703 | 0.985 | 2870.422 |
| -5.000 | 85.000 | 2391.585 | 0.996 | 2382.484 |
| 0.000 | 90.000 | 4905.711 | 1.000 | 4905.711 |
| 5.000 | 95.000 | 4754.74 | 0.996 | 4736.647 |
| 10.000 | 100.000 | 4640.166 | 0.985 | 4569.671 |
| 15.000 | 105.000 | 251185.147 | 0.966 | 242626.221 |
| 20.000 | 110.000 | 218810.42 | 0.940 | 205614.537 |
| 25.000 | 115.000 | 220136.123 | 0.906 | 199511.082 |
| 30.000 | 120.000 | 175013.919 | 0.866 | 151566.5 |
| 35.000 | 125.000 | 159763.261 | 0.819 | 130870.402 |
| 40.000 | 130.000 | 284956.411 | 0.766 | 218289.275 |
| 45.000 | 135.000 | 3221.564 | 0.707 | 2277.989 |
|  |  | Sum | 16.903 | 1200713.704 |

### Distances for SE

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 90.000 | 4905.711 | 0.707 | 3468.862 |
| -40.000 | 95.000 | 4754.74 | 0.766 | 3642.342 |
| -35.000 | 100.000 | 4640.166 | 0.819 | 3801.001 |
| -30.000 | 105.000 | 251185.147 | 0.866 | 217532.718 |
| -25.000 | 110.000 | 218810.42 | 0.906 | 198309.588 |
| -20.000 | 115.000 | 220136.123 | 0.940 | 206860.29 |
| -15.000 | 120.000 | 175013.919 | 0.966 | 169050.464 |
| -10.000 | 125.000 | 159763.261 | 0.985 | 157336.098 |
| -5.000 | 130.000 | 284956.411 | 0.996 | 283872.066 |
| 0.000 | 135.000 | 3221.564 | 1.000 | 3221.564 |
| 5.000 | 140.000 | 2642.693 | 0.996 | 2632.637 |
| 10.000 | 145.000 | 1902.204 | 0.985 | 1873.305 |
| 15.000 | 150.000 | 60429.174 | 0.966 | 58370.1 |
| 20.000 | 155.000 | 209724.417 | 0.940 | 197076.487 |
| 25.000 | 160.000 | 63895.973 | 0.906 | 57909.418 |
| 30.000 | 165.000 | 140704.576 | 0.866 | 121853.737 |
| 35.000 | 170.000 | 135796.176 | 0.819 | 111237.715 |
| 40.000 | 175.000 | 91667.701 | 0.766 | 70221.533 |
| 45.000 | 180.000 | 29779.829 | 0.707 | 21057.519 |
|  |  | Sum | 16.903 | 1889327.445 |

### Distances for S

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 135.000 | 3221.564 | 0.707 | 2277.989 |
| -40.000 | 140.000 | 2642.693 | 0.766 | 2024.421 |
| -35.000 | 145.000 | 1902.204 | 0.819 | 1558.194 |
| -30.000 | 150.000 | 60429.174 | 0.866 | 52333.2 |
| -25.000 | 155.000 | 209724.417 | 0.906 | 190074.872 |
| -20.000 | 160.000 | 63895.973 | 0.940 | 60042.575 |
| -15.000 | 165.000 | 140704.576 | 0.966 | 135910.184 |
| -10.000 | 170.000 | 135796.176 | 0.985 | 133733.127 |
| -5.000 | 175.000 | 91667.701 | 0.996 | 91318.878 |
| 0.000 | 180.000 | 29779.829 | 1.000 | 29779.829 |
| 5.000 | 185.000 | 76573.032 | 0.996 | 76281.648 |
| 10.000 | 190.000 | 5309.22 | 0.985 | 5228.561 |
| 15.000 | 195.000 | 3566.32 | 0.966 | 3444.801 |
| 20.000 | 200.000 | 2324.436 | 0.940 | 2184.255 |
| 25.000 | 205.000 | 2625.942 | 0.906 | 2379.911 |
| 30.000 | 210.000 | 2709.426 | 0.866 | 2346.432 |
| 35.000 | 215.000 | 2230.592 | 0.819 | 1827.194 |
| 40.000 | 220.000 | 2098.363 | 0.766 | 1607.44 |
| 45.000 | 225.000 | 2118.796 | 0.707 | 1498.215 |
|  |  | Sum | 16.903 | 795851.727 |

### Distances for SW

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 180.000 | 29779.829 | 0.707 | 21057.519 |
| -40.000 | 185.000 | 76573.032 | 0.766 | 58658.345 |
| -35.000 | 190.000 | 5309.22 | 0.819 | 4349.059 |
| -30.000 | 195.000 | 3566.32 | 0.866 | 3088.524 |
| -25.000 | 200.000 | 2324.436 | 0.906 | 2106.654 |
| -20.000 | 205.000 | 2625.942 | 0.940 | 2467.578 |
| -15.000 | 210.000 | 2709.426 | 0.966 | 2617.105 |
| -10.000 | 215.000 | 2230.592 | 0.985 | 2196.704 |
| -5.000 | 220.000 | 2098.363 | 0.996 | 2090.379 |
| 0.000 | 225.000 | 2118.796 | 1.000 | 2118.796 |
| 5.000 | 230.000 | 3531.401 | 0.996 | 3517.963 |
| 10.000 | 235.000 | 3320.557 | 0.985 | 3270.111 |
| 15.000 | 240.000 | 6204.761 | 0.966 | 5993.339 |
| 20.000 | 245.000 | 2520.225 | 0.940 | 2368.237 |
| 25.000 | 250.000 | 2653.459 | 0.906 | 2404.85 |
| 30.000 | 255.000 | 4265.302 | 0.866 | 3693.86 |
| 35.000 | 260.000 | 3994.791 | 0.819 | 3272.341 |
| 40.000 | 265.000 | 3497.852 | 0.766 | 2679.51 |
| 45.000 | 270.000 | 3151.297 | 0.707 | 2228.304 |
|  |  | Sum | 16.903 | 130179.177 |

### Distances for W

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 225.000 | 2118.796 | 0.707 | 1498.215 |
| -40.000 | 230.000 | 3531.401 | 0.766 | 2705.21 |
| -35.000 | 235.000 | 3320.557 | 0.819 | 2720.041 |
| -30.000 | 240.000 | 6204.761 | 0.866 | 5373.48 |
| -25.000 | 245.000 | 2520.225 | 0.906 | 2284.1 |
| -20.000 | 250.000 | 2653.459 | 0.940 | 2493.435 |
| -15.000 | 255.000 | 4265.302 | 0.966 | 4119.965 |
| -10.000 | 260.000 | 3994.791 | 0.985 | 3934.101 |
| -5.000 | 265.000 | 3497.852 | 0.996 | 3484.542 |
| 0.000 | 270.000 | 3151.297 | 1.000 | 3151.297 |
| 5.000 | 275.000 | 82456.023 | 0.996 | 82142.253 |
| 10.000 | 280.000 | 89056.555 | 0.985 | 87703.586 |
| 15.000 | 285.000 | 105991.248 | 0.966 | 102379.684 |
| 20.000 | 290.000 | 112246.996 | 0.940 | 105477.674 |
| 25.000 | 295.000 | 123260.739 | 0.906 | 111712.167 |
| 30.000 | 300.000 | 149681.087 | 0.866 | 129627.624 |
| 35.000 | 305.000 | 160098.692 | 0.819 | 131145.171 |
| 40.000 | 310.000 | 164524.049 | 0.766 | 126032.734 |
| 45.000 | 315.000 | 175017.09 | 0.707 | 123755.771 |
|  |  | Sum | 16.903 | 1031741.05 |

### Distances for NW

| Rel.theta (deg) | Theta (deg) | F | Cos(Rel.theta) | F x Cos(Rel.theta) |
| --- | --- | --- | --- | --- |
| -45.000 | 270.000 | 3151.297 | 0.707 | 2228.304 |
| -40.000 | 275.000 | 82456.023 | 0.766 | 63164.978 |
| -35.000 | 280.000 | 89056.555 | 0.819 | 72950.859 |
| -30.000 | 285.000 | 105991.248 | 0.866 | 91791.113 |
| -25.000 | 290.000 | 112246.996 | 0.906 | 101730.327 |
| -20.000 | 295.000 | 123260.739 | 0.940 | 115827.207 |
| -15.000 | 300.000 | 149681.087 | 0.966 | 144580.827 |
| -10.000 | 305.000 | 160098.692 | 0.985 | 157666.433 |
| -5.000 | 310.000 | 164524.049 | 0.996 | 163897.985 |
| 0.000 | 315.000 | 175017.09 | 1.000 | 175017.09 |
| 5.000 | 320.000 | 87645.572 | 0.996 | 87312.054 |
| 10.000 | 325.000 | 75056.259 | 0.985 | 73915.986 |
| 15.000 | 330.000 | 69816.292 | 0.966 | 67437.36 |
| 20.000 | 335.000 | 105017.213 | 0.940 | 98683.9 |
| 25.000 | 340.000 | 77354.489 | 0.906 | 70106.976 |
| 30.000 | 345.000 | 68286.079 | 0.866 | 59137.479 |
| 35.000 | 350.000 | 65187.021 | 0.819 | 53398.082 |
| 40.000 | 355.000 | 105572.569 | 0.766 | 80873.28 |
| 45.000 | 360.000 | 102037.066 | 0.707 | 72151.101 |
|  |  | Sum | 16.903 | 1751871.341 |

## Distances for fetch-control

|  | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| F.eff | 103605.897 | 64888.389 | 71037.578 | 111777.891 | 47084.812 | 7701.764 | 61040.683 | 103645.604 |

## Final SMB results

| Beaufort | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 1 | 0.055 | 0.043 | 0.06 | 0.052 | 0.048 | 0.038 | 0.058 | 0.062 |
| 2 | 0.286 | 0.223 | 0.271 | 0.281 | 0.229 | 0.148 | 0.264 | 0.286 |
| 3 | 0.627 | 0.412 | 0.587 | 0.656 | 0.369 | 0.247 | 0.563 | 0.644 |
| 4 | 0.801 | 0.53 | 1.001 | 1.091 | 0.369 | 0.308 | 0.951 | 1.127 |
| 5 | 0.552 | 0.29 | 1.173 | 0.766 | 0.363 | 0.29 | 0.891 | 1.118 |
| 6 | 0.286 | 0.358 | 0.833 | 0.571 | 0.195 | 0.286 | 0.694 | 0.8 |
| 7 | 0 | 0 | 0.573 | 0 | 0.266 | 0.266 | 0.266 | 0.39 |
| 8 | 0 | 0 | 0.515 | 0 | 0 | 0 | 0 | 0.35 |
| 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| maxHs (m) | 0.801 | 0.53 | 1.173 | 1.091 | 0.369 | 0.308 | 0.951 | 1.127 |
| Ts (s) | 3.568 | 2.872 | 4.296 | 4.187 | 2.42 | 2.136 | 3.9 | 4.258 |
| D (hr) | 4.836 | 2.083 | 4.092 | 9.97 | 3.199 | 0.744 | 7.116 | 10.851 |

## Sketch