Hydraulic Solver v9.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	4

GRATE ON GRADE	4

Data	4

Results	4

GRATE ON SAG	5

Data	5

Results	5

CURB ON GRADE	6

Data	6

Results	6

CURB ON SAG	7

Data	7

Results	7

WEIR RECTANGULAR	7

Data	8

Results	8

WEIR TRIANGULAR	8

Data	8

Results	9

WEIR TRAPEZOID	9

Data	9

Results	10

WEIR GENERIC	10

Data	10

Results	10

WEIR BROAD	11

Data	11

Results	11

ORIFICE GENERIC	11

Data	12

Results	12

ORIFICE RECTANGULAR	12

Data	12

Results	13

ORIFICE CIRCULAR	13

Data	13

Results	13

COMBO GRADE	14

Data	14

Results	14

SX1	15

Data	15

Results	16

DEE	16

Data	16

Results	17

PRESSURE SECTION	17

Data	18

Results	18

# Project information

# GRATE ON GRADE

| Solver type | Grates |
| --- | --- |
| Inlet position | On grade |

## Data

| Unknown variable | Length (m) |
| --- | --- |
| Flow rate (m³/s) | 10 |
| Slope | 0.001 |
| Gutter width (m) | 1.25 |
| Gutter cross slope (H:V) | 0.06 |
| Road cross slope (H:V) | 0.08 |
| Friction coefficient | 0.013 |
| Efficiency | 0.7 |
| Grate width (m) | 1.2 |
| Grate type | Reticuline |
| Clogging (0~1) | 0.15 |
| Friction type | Manning |

## Results

| Intercepted flow (m³/s) | 6.999 |
| --- | --- |
| Bypass flow (m³/s) | 3.001 |
| Spread (m) | 15.436 |
| Flow depth (m) | 0.926 |
| Wet area (m²) | 7.1481 |
| Gutter depression (m) | 0.000 |
| Total depression (m) | 0.000 |
| Flow velocity V (m/s) | 1.40 |
| Splash over velocity (m/s) | 2.65 |
| Frontal flow factor | 1.0000 |
| Side flow factor | 0.6241 |
| Frontal/side flow ratio | 0.2016 |
| Grate length (m) | 1.936 |
| Active grate length (m) | 1.646 |
| Efficiency | 0.6999 |

# GRATE ON SAG

| Solver type | Grates |
| --- | --- |
| Inlet position | In sag |

## Data

| Unknown variable | Length (m) |
| --- | --- |
| Spread (m) | 5 |
| Gutter cross slope (H:V) | 0.04 |
| Road cross slope (H:V) | 0.01 |
| Gutter width (m) | 0 |
| Flow rate (m³/s) | 10 |
| Grate width (m) | 1.5 |
| Depression width (m) | 0 |
| Depression height (m) | 0 |
| Grate type | Reticuline |
| Clogging (0~1) | 0.15 |
| Friction type | Manning |

## Results

| Flow depth (m) | 0.050 |
| --- | --- |
| Spread (m) | 5.000 |
| Gutter depression (m) | 0.000 |
| Total depression (m) | 0.000 |
| Open grate area (m²) | 546.9275 |
| Active grate weir length (m) | 538.753 |
| Grate length (m) | 536.203 |

# CURB ON GRADE

| Solver type | Curbs |
| --- | --- |
| Inlet position | On grade |

## Data

| Unknown variable | Length (m) |
| --- | --- |
| Flow rate (m³/s) | 10 |
| Slope | 0.5 |
| Gutter width (m) | 1.2 |
| Gutter cross slope (H:V) | 1 |
| Road cross slope (H:V) | 0.5 |
| Friction coefficient | 0.013 |
| Efficiency | 0.5 |
| Depression width (m) | 0 |
| Depression height (m) | 0 |
| Friction type | Manning |

## Results

| Intercepted flow (m³/s) | 5.000 |
| --- | --- |
| Bypass flow (m³/s) | 5.000 |
| Spread (m) | 1.019 |
| Flow depth (m) | 1.019 |
| Wet area (m²) | 0.5188 |
| Gutter depression (m) | 0.600 |
| Total depression (m) | 0.600 |
| Flow velocity V (m/s) | 19.28 |
| Equivalent cross slope | 1.00000 |
| Length factor | 0.0000 |
| Total interception length (m) | 23.635 |
| Efficiency | 0.5000 |
| Curb length (m) | 7.553 |

# CURB ON SAG

| Solver type | Curbs |
| --- | --- |
| Inlet position | In sag |

## Data

| Unknown variable | Length (m) |
| --- | --- |
| Flow rate (m³/s) | 10 |
| Spread (m) | 70 |
| Gutter width (m) | 2.56 |
| Gutter cross slope (H:V) | 0.06 |
| Road cross slope (H:V) | 0.02 |
| Height (m) | 0.4 |
| Depression width (m) | 0 |
| Depression height (m) | 0 |
| curb throat type | Inclined |
| throat incline angle | 45 |
| Friction type | Manning |

## Results

| Flow depth (m) | 1.502 |
| --- | --- |
| Gutter depression (m) | 0.102 |
| Total depression (m) | 0.102 |
| Spread (m) | 70.000 |
| Curb length (m) | 7.221 |

# WEIR RECTANGULAR

| Solver type | Weirs |
| --- | --- |
| Weir type | Rectangular sharp-crested |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 1.5 |
| Crest elevation (m) | 1.4 |
| Tailwater elevation (m) | 1.2 |
| Discharge coefficient | 0.6 |
| Crest length (m) | 2 |
| Number of contractions | 2 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 0.100 |
| --- | --- |
| Tailwater height above centroid (m) | -0.200 |
| Total top width (m) | 2.0000 |
| Flow velocity V (m/s) | 0.19 |
| Wet area (m²) | 0.200 |
| Wetted perimeter (m) | 2.200 |
| Flow rate Q (m³/s) | 0.038 |

# WEIR TRIANGULAR

| Solver type | Weirs |
| --- | --- |
| Weir type | Triangular sharp-crested |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 2 |
| Crest elevation (m) | 1 |
| Tailwater elevation (m) | 0.5 |
| Discharge coefficient | 0.6 |
| Angle (°) | 15 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 1.000 |
| --- | --- |
| Tailwater height above centroid (m) | -0.500 |
| Total top width (m) | 0.2633 |
| Flow velocity V (m/s) | 0.60 |
| Wet area (m²) | 0.132 |
| Wetted perimeter (m) | 2.017 |
| Flow rate Q (m³/s) | 0.079 |

# WEIR TRAPEZOID

| Solver type | Weirs |
| --- | --- |
| Weir type | Trapezoid (cipoletti) sharp-crested |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 2 |
| Crest elevation (m) | 1 |
| Tailwater elevation (m) | 0.5 |
| Discharge coefficient | 0.6 |
| Crest length (m) | 2 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 1.000 |
| --- | --- |
| Tailwater height above centroid (m) | -0.500 |
| Total top width (m) | 2.5000 |
| Flow velocity V (m/s) | 0.53 |
| Wet area (m²) | 2.250 |
| Wetted perimeter (m) | 4.062 |
| Equal side slopes (H/V) | 0.25000 |
| Flow rate Q (m³/s) | 1.200 |

# WEIR GENERIC

| Solver type | Weirs |
| --- | --- |
| Weir type | Generic |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 148 |
| Crest elevation (m) | 145 |
| Discharge coefficient | 0.6 |
| Crest length (m) | 1.2 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 3.000 |
| --- | --- |
| Total top width (m) | 1.2000 |
| Flow velocity V (m/s) | 1.04 |
| Wet area (m²) | 3.600 |
| Wetted perimeter (m) | 7.200 |
| Flow rate Q (m³/s) | 3.741 |

# WEIR BROAD

| Solver type | Weirs |
| --- | --- |
| Weir type | Broad |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 5 |
| Crest elevation (m) | 3 |
| Tailwater elevation (m) | 1 |
| Crest length (m) | 1.5 |
| Crest breadth (m) | 0.5 |
| Crest surface type | Gravel |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 2.000 |
| --- | --- |
| Tailwater height above centroid (m) | -2.000 |
| Total top width (m) | 1.5000 |
| Flow velocity V (m/s) | 2.41 |
| Wet area (m²) | 3.000 |
| Wetted perimeter (m) | 5.500 |
| Initial coefficient | 1.7057 |
| Submergence factor | 1.0000 |
| Adjusted discharge coefficient | 1.7057 |
| Flow rate Q (m³/s) | 7.237 |

# ORIFICE GENERIC

| Solver type | Orifices |
| --- | --- |
| Orifice type | Generic |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 150 |
| Centroid elevation (m) | 142 |
| Tailwater elevation (m) | 149 |
| Discharge coefficient | 0.6 |
| Opening area (m²) | 0.1 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 8.000 |
| --- | --- |
| Tailwater height above centroid (m) | 7.000 |
| Opening area (m²) | 0.1000 |
| Flow velocity V (m/s) | 2.66 |
| Flow rate Q (m³/s) | 0.266 |

# ORIFICE RECTANGULAR

| Solver type | Orifices |
| --- | --- |
| Orifice type | Rectangular |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 150 |
| Centroid elevation (m) | 142 |
| Tailwater elevation (m) | 158 |
| Discharge coefficient | 0.6 |
| Opening width (m) | 1 |
| Opening height (m) | 0.25 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 8.000 |
| --- | --- |
| Tailwater height above centroid (m) | 16.000 |
| Opening area (m²) | 0.0000 |
| Flow velocity V (m/s) | 0.00 |
| Flow rate Q (m³/s) | 0.000 |

# ORIFICE CIRCULAR

| Solver type | Orifices |
| --- | --- |
| Orifice type | Circular |

## Data

| Unknown variable | discharge |
| --- | --- |
| Headwater elevation (m) | 5 |
| Centroid elevation (m) | 4 |
| Tailwater elevation (m) | 3 |
| Discharge coefficient | 0.6 |
| Opening diameter (m) | 0.5 |
| Friction type | Manning |

## Results

| Headwater height above centroid (m) | 1.000 |
| --- | --- |
| Tailwater height above centroid (m) | -1.000 |
| Opening area (m²) | 0.1963 |
| Flow velocity V (m/s) | 2.66 |
| Flow rate Q (m³/s) | 0.522 |

# COMBO GRADE

| Solver type | Combination inlets |
| --- | --- |
| Inlet position | On grade |

## Data

| Unknown variable | equal opening widths |
| --- | --- |
| Flow rate (m³/s) | 10 |
| Slope | 0.001 |
| Gutter width (m) | 2.56 |
| Gutter cross slope (H:V) | 0.06 |
| Road cross slope (H:V) | 0.06 |
| Friction coefficient | 0.013 |
| Efficiency | 0.7 |
| Grate width (m) | 0.6 |
| Grate type | Parallel 30-mm gap |
| Clogging (0~1) | 0.15 |
| Depression width (m) | 0 |
| Depression height (m) | 0 |
| Friction type | Manning |

## Results

| Intercepted flow (m³/s) | 6.997 |
| --- | --- |
| Bypass flow (m³/s) | 3.003 |
| Spread (m) | 15.436 |
| Flow depth (m) | 0.926 |
| Wet area (m²) | 7.1482 |
| Gutter depression (m) | 0.000 |
| Total depression (m) | 0.000 |
| Flow velocity V (m/s) | 1.40 |
| Splash over velocity (m/s) | 3.13 |
| Frontal flow factor | 1.0000 |
| Side flow factor | 0.5130 |
| Frontal/side flow ratio | 0.3834 |
| Grate length (m) | 1.800 |
| Active grate length (m) | 1.530 |
| Efficiency | 0.6997 |
| Equivalent cross slope | 0.06000 |
| Length factor | 0.0000 |
| Total interception length (m) | 0.000 |
| Efficiency | 0.6997 |
| Curb length (m) | 1.800 |

# SX1

| Solver type | Grates |
| --- | --- |
| Inlet position | On grade |

## Data

| Unknown variable | efficiency |
| --- | --- |
| Flow rate (m³/s) | 10 |
| Slope | 0.001 |
| Gutter width (m) | 1.9 |
| Gutter cross slope (H:V) | 0.06 |
| Road cross slope (H:V) | 0.02 |
| Friction coefficient | 0.013 |
| Grate width (m) | 0.6 |
| Grate length (m) | 0 |
| Grate type | Parallel 30-mm gap |
| Clogging (0~1) | 0 |
| Friction type | Manning |

## Results

| Intercepted flow (m³/s) | 0.000 |
| --- | --- |
| Bypass flow (m³/s) | 10.000 |
| Spread (m) | 15.436 |
| Flow depth (m) | 0.926 |
| Wet area (m²) | 7.1481 |
| Gutter depression (m) | 0.076 |
| Total depression (m) | 0.076 |
| Flow velocity V (m/s) | 1.40 |
| Splash over velocity (m/s) | 0.00 |
| Frontal flow factor | 0.7457 |
| Side flow factor | 0.0000 |
| Frontal/side flow ratio | 0.2955 |
| Grate length (m) | 0.000 |
| Active grate length (m) | 0.000 |
| Efficiency | 0.0000 |

# DEE

| Solver type | Sections with free surface |
| --- | --- |
| Calculations | Hydraulic calculations will take place |

## Data

| Unknown variable | Flow depth (m) |
| --- | --- |
| Flow rate (m³/s) | 48000 |
| Slope | 0.00001 |
| Kinematic viscosity (m²/s) | 0 |
| Friction coefficient | 0.05 |
| Section | IRR |
| Friction type | Manning |

## Results

| Flow |  |
| --- | --- |
| Flow depth (m) | 196.499 |
| Friction factor | 0.0696 |
| Flow velocity V (m/s) | 0.59 |
| Flow rate Q (m³/s) | 48000.000 |
| Full flow | 0.28 |
| Critical depth (m) | 24.344 |
| Velocity head (m) | 0.018 |
| Specific energy (m) | 196.516 |
| Froude number | 0.0154 |
| Flow type | Subcritical |
| Geometry |  |
| Height (m) | 712.884 |
| Total section area (m²) | 230164.6558 |
| Total section perimeter (m) | 5005.466 |
| Total hydraulic radius (m) | 45.983 |
| Total top width (m) | 103.540 |
| Wet area (m²) | 81825.4571 |
| Wetted perimeter (m) | 1763.231 |
| Hydraulic radius (m) | 46.407 |
| Top width (m) | 552.888 |
| Slope | 0.00001 |
| Full flow |  |
| Friction factor in full flow | 0.0822 |
| Full flow rate Qf (m³/s) | 113709.827 |
| Full flow velocity Vf (m/s) | 0.49 |
| Ratio Q/Qf | 0.4221 |
| Ratio V/Vf | 1.1874 |
| Slope for full flow | 0.00000 |
| Ground works |  |
| Excavations (m³) | 0.000 |
| Landfills (m³) | 0.000 |
| Total ground works (m³) | 0.000 |

# PRESSURE SECTION

| Solver type | Sections under pressure |
| --- | --- |
| Calculations | Hydraulic calculations will take place |

## Data

| Unknown variable | Length (m) |
| --- | --- |
| Kinematic viscosity (m²/s) | 0.00000139 |
| Specific weight (N/m³) | 9808.8228 |
| Flow rate (m³/s) | 10 |
| Friction coefficient | 0.013 |
| Elevation 1 (m) | 50 |
| Pressure 1 (N/m²) | 30 |
| Elevation 2 (m) | 30 |
| Pressure 2 (N/m²) | 35 |
| Section | D 0.250 |
| Turbulent flow if Reynolds is greater than | 4000 |
| Friction type (Turbulent) | Manning |
| Laminar flow if Reynolds is lower than | 2000 |
| Friction type (Laminar) | Darcy - Laminar |
| Friction type (Transient) | Darcy - Moody Cubic |

## Results

| Geometry |  |
| --- | --- |
| Flow depth (m) | 0.250 |
| Elevation 1 (m) | 50.000 |
| Elevation 2 (m) | 30.000 |
| Pipe length (m) | 0.071 |
| Total section area (m²) | 0.0491 |
| Total section perimeter (m) | 0.785 |
| Total hydraulic radius (m) | 0.062 |
| Flow |  |
| Friction factor | 0.013000 |
| Flow rate Q (m³/s) | 10.000 |
| Flow velocity V (m/s) | 203.72 |
| Velocity head (m) | 2115.248 |
| Reynolds number | 36639987 |
| Flow type | Turbulent |
| Pressure 1 (N/m²) | 30.000 |
| Pressure 2 (N/m²) | 35.000 |
| Energy losses (m) | 20.000 |
| Pressure line 1 (m) | 50.003 |
| Pressure line 2 (m) | 30.004 |
| Energy line 1 (m) | 2165.251 |
| Energy line 2 (m) | 2145.251 |
| Friction slope | 282.77448 |
| Ground works |  |
| Excavations (m³) | 0.000 |
| Landfills (m³) | 0.000 |
| Total ground works (m³) | 0.000 |