Hydraulic Hammer v9.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

Data	3

Results	3

# Project information

# Data

| Turbulent flow if Reynolds is greater than | 4000 |
| --- | --- |
| Friction type (Turbulent) | Darcy - Colebrook |
| Laminar flow if Reynolds is lower than | 2000 |
| Friction type (Laminar) | Darcy - Laminar |
| Friction type (Transient) | Darcy - Moody Cubic |

| Total observation time (s) | 15.00 |
| --- | --- |
| Viscosity (kgr/m*sec) | 0.00000100 |
| Density (kgr/m³) | 1000.000 |
| Water level (m) | 20.000 |
| Shutoff exponent e | 1.0000 |
| Shutoff time for the valve Tc (s) | 5.00 |

| Pipe AB |
| --- |
| Pipe length (m) | 800.000 |
| Pipe diameter (mm) | 500.00 |
| Calculated friction | 0.0200 |
| Wave celerity (m/s) | 1000.00 |

| Pipe BD |
| --- |
| Pipe length (m) | 400.000 |
| Pipe diameter (mm) | 350.00 |
| Calculated friction | 0.0200 |
| Wave celerity (m/s) | 1000.00 |

| Pipe BC |
| --- |
| Pipe length (m) | 200.000 |
| Pipe diameter (mm) | 350.00 |
| Calculated friction | 0.0200 |
| Wave celerity (m/s) | 1000.00 |

# Results

| Pipe AB |  |
| --- | --- |
| Wave celerity (m/s) | 1000.00 |
| Flow area (m²) | 0.1963 |
| Calculation step (m) | 100.000 |
| Calculated friction | 0.065 |
| Maximum over-pressure (m) | 256.854 |
| Time when over-pressure occurs (s) | 0.60 |
| Maximum sub-pressure (m) | -141.532 |
| Time when sub-pressure occurs (s) | 8.10 |
| Pipe BD |  |
| Wave celerity (m/s) | 1000.00 |
| Flow area (m²) | 0.0962 |
| Calculation step (m) | 100.000 |
| Calculated friction | 0.076 |
| Maximum over-pressure (m) | 259.214 |
| Time when over-pressure occurs (s) | 5.00 |
| Maximum sub-pressure (m) | -240.544 |
| Time when sub-pressure occurs (s) | 7.50 |
| Pipe BC |  |
| Wave celerity (m/s) | 1000.00 |
| Flow area (m²) | 0.0962 |
| Calculation step (m) | 100.000 |
| Calculated friction | 0.076 |
| Maximum over-pressure (m) | 290.310 |
| Time when over-pressure occurs (s) | 0.50 |
| Maximum sub-pressure (m) | -146.682 |
| Time when sub-pressure occurs (s) | 8.00 |