Water Networks v9.0 - Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

1. Pipe Excavations	3

2. Excavation volume	8

2.1. Pipe excavations	8

2.1.1. Total	8

2.1.2. Soft soil excavation	8

2.1.3. Rock excavations	8

2.2. Trench backfill	8

2.2.1.Total backfill volume	8

2.2.2. Restoration (asphalt)	8

2.3. Augmented soil volume to be transported	8

2.4. Transportation of soil volume	9

2.5. Trench support	9

2.6. Water pumping	9

2.7. Dislocation of public utilities	9

3. Pipe Sections	9

3.1. Section : D65.8 x .0001	9

3.2. Section : D79 x .0001	10

3.3. Section : D97 x .0001	14

3.4. Section : D123.6 x .0001	14

4. Marking grid	14

5. Manholes (per type)	15

6. Manholes	15

7. Trenches	15

7.1. Trench : Φ75-110 ΧΩΜ ΕΝΤΟΣ (Type V)	15

7.2. Trench : Φ75-110 ΑΣΦ ΕΝΤΟΣ (Type V)	15

7.3. Trench : ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ (Type V)	19

7.4. Trench : Φ75-110 ΧΩΜ ΕΚΤΟΣ (Type V)	20

7.5. Trench : Φ75-110 ΑΣΦ ΕΚΤΟΣ (Type V)	20

7.6. Trench : ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ (Type V)	21

7.7. Trench : ΔΙΠΛΟΣ ΧΩΜ ΕΚΤΟΣ (Type V)	21

8. Special Devices Count	21

# Project information

| Project title | ΥΔΡΕΥΣΗ Δ.Δ. ΜΕΤΑΜΟΡΦΩΣΗΣ |
| --- | --- |
| Firm | ΦΩΤΙΟΣ Σ. ΦΩΤΟΠΟΥΛΟΣ |
| Comments | ΣΕΝΑΡΙΟ ΚΑΝΟΝΙΚΗΣ ΛΕΙΤΟΥΡΓΙΑΣ |

# 1. Pipe Excavations

| # | Name | Length (m) | Trench | Soil Volume (m³) | Rock Volume (m³) | Excavation Volume (m³) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | R1:K1 | 282.869 | ΔΙΠΛΟΣ ΧΩΜ ΕΚΤΟΣ | 153.072 | 38.268 | 191.340 |
| 2 | K4:K5 | 51.913 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 27.262 | 6.815 | 34.077 |
| 3 | K7:K10 | 4.624 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 2.456 | 0.614 | 3.070 |
| 4 | K10:K66 | 43.658 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.792 | 4.698 | 23.489 |
| 5 | K61:K62 | 58.904 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 25.340 | 6.335 | 31.675 |
| 6 | K60:K61 | 40.376 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.372 | 4.343 | 21.715 |
| 7 | K64:K70 | 43.824 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.845 | 4.711 | 23.557 |
| 8 | K180:K71 | 41.354 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.783 | 4.446 | 22.229 |
| 9 | K62:K63 | 41.009 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.635 | 4.409 | 22.043 |
| 10 | K75:K80 | 48.994 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.068 | 5.267 | 26.335 |
| 11 | K97:K98 | 36.179 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.558 | 3.889 | 19.447 |
| 12 | K72:K92 | 39.277 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.897 | 4.224 | 21.122 |
| 13 | K92:K93 | 49.104 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.132 | 5.283 | 26.415 |
| 14 | K108:K109 | 32.423 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.943 | 3.486 | 17.428 |
| 15 | K82:K83 | 34.307 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.753 | 3.688 | 18.441 |
| 16 | K83:K84 | 15.110 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.518 | 1.629 | 8.147 |
| 17 | K84:K85 | 23.309 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.036 | 2.509 | 12.545 |
| 18 | K98:K100 | 14.871 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.395 | 1.599 | 7.993 |
| 19 | K98:K81 | 31.417 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.530 | 3.382 | 16.912 |
| 20 | K100:K82 | 26.691 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.478 | 2.869 | 14.347 |
| 21 | K82:K88 | 49.234 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.172 | 5.293 | 26.465 |
| 22 | K87:K88 | 46.348 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.930 | 4.983 | 24.913 |
| 23 | K80:K81 | 20.466 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 8.814 | 2.203 | 11.017 |
| 24 | K81:K82 | 47.215 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.309 | 5.077 | 25.387 |
| 25 | K85:K111 | 53.373 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.952 | 5.738 | 28.689 |
| 26 | K111:K56 | 52.698 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.661 | 5.665 | 28.326 |
| 27 | K56:K112 | 20.260 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 8.725 | 2.181 | 10.906 |
| 28 | K112:K113 | 26.953 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.602 | 2.901 | 14.503 |
| 29 | K113:K130 | 24.892 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.715 | 2.679 | 13.394 |
| 30 | K132:K147 | 42.072 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.092 | 4.523 | 22.614 |
| 31 | K143:K142 | 14.532 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.249 | 1.562 | 7.811 |
| 32 | K142:K141 | 11.048 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 4.751 | 1.188 | 5.938 |
| 33 | K140:K141 | 42.491 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.272 | 4.568 | 22.840 |
| 34 | K138:K139 | 53.177 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.867 | 5.717 | 28.584 |
| 35 | K85:K86 | 10.581 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 4.550 | 1.138 | 5.688 |
| 36 | K139:K165 | 47.362 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.367 | 5.092 | 25.458 |
| 37 | K166:K175 | 26.373 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.341 | 2.835 | 14.176 |
| 38 | K173:K174 | 33.572 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.447 | 3.612 | 18.059 |
| 39 | K176:K173 | 43.421 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.672 | 4.668 | 23.340 |
| 40 | K141:K157 | 42.885 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.441 | 4.610 | 23.052 |
| 41 | K161:K160 | 35.838 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.411 | 3.853 | 19.264 |
| 42 | K160:K162 | 32.554 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.999 | 3.500 | 17.499 |
| 43 | K160:K159 | 11.120 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 4.782 | 1.195 | 5.977 |
| 44 | K66:K67 | 49.514 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.292 | 5.323 | 26.615 |
| 45 | K46:K47 | 23.336 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.035 | 2.509 | 12.544 |
| 46 | K75:K78 | 32.497 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.974 | 3.494 | 17.468 |
| 47 | K96:K75 | 55.207 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 23.740 | 5.935 | 29.675 |
| 48 | K71:K72 | 12.181 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 5.238 | 1.310 | 6.548 |
| 49 | K66:K64 | 16.239 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.983 | 1.746 | 8.729 |
| 50 | K125:K134 | 21.115 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 9.080 | 2.270 | 11.350 |
| 51 | K134:K149 | 44.127 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.975 | 4.744 | 23.719 |
| 52 | K148:K150 | 41.418 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.810 | 4.453 | 22.263 |
| 53 | K143:K144 | 39.636 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.058 | 4.265 | 21.323 |
| 54 | K151:K144 | 58.060 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 24.978 | 6.245 | 31.223 |
| 55 | K154:K155 | 38.416 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.536 | 4.134 | 20.670 |
| 56 | K166:K167 | 41.036 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.646 | 4.412 | 22.058 |
| 57 | K168:K164 | 36.006 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.496 | 3.874 | 19.370 |
| 58 | K168:K169 | 22.806 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 9.815 | 2.454 | 12.268 |
| 59 | K144:K145 | 44.326 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.076 | 4.769 | 23.845 |
| 60 | K155:K156 | 72.682 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 31.278 | 7.820 | 39.098 |
| 61 | K47:K48 | 40.532 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.430 | 4.357 | 21.787 |
| 62 | K79:K50 | 42.870 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.435 | 4.609 | 23.044 |
| 63 | K76:K78 | 47.790 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.575 | 5.144 | 25.719 |
| 64 | K47:K76 | 46.015 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.805 | 4.951 | 24.756 |
| 65 | K43:K46 | 13.007 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 5.593 | 1.398 | 6.992 |
| 66 | K43:K44 | 38.995 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.768 | 4.192 | 20.961 |
| 67 | K23:K24 | 52.659 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 22.644 | 5.661 | 28.306 |
| 68 | K26:K30 | 40.417 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.398 | 4.349 | 21.747 |
| 69 | K51:K31 | 20.864 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 8.972 | 2.243 | 11.215 |
| 70 | K50:K51 | 9.060 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 3.896 | 0.974 | 4.870 |
| 71 | K174:K179 | 15.234 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.556 | 1.639 | 8.195 |
| 72 | K114:K115 | 32.838 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.131 | 3.533 | 17.663 |
| 73 | K55:K56 | 16.079 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 6.922 | 1.731 | 8.653 |
| 74 | K171:K109 | 36.765 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.810 | 3.952 | 19.762 |
| 75 | K173:K172 | 13.192 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 5.691 | 1.423 | 7.113 |
| 76 | K172:K177 | 48.224 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.753 | 5.188 | 25.941 |
| 77 | K133:K134 | 45.326 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.491 | 4.873 | 24.364 |
| 78 | K90:K91 | 36.320 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.630 | 3.908 | 19.538 |
| 79 | K89:K83 | 47.706 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.515 | 5.129 | 25.643 |
| 80 | K88:K89 | 8.660 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 3.724 | 0.931 | 4.655 |
| 81 | K84:K110 | 40.214 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.306 | 4.326 | 21.632 |
| 82 | K10:K11 | 43.991 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 23.121 | 5.780 | 28.901 |
| 83 | K16:K20 | 11.893 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 6.270 | 1.568 | 7.838 |
| 84 | K20:K21 | 109.575 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 57.591 | 14.398 | 71.988 |
| 85 | K16:K17 | 35.739 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 15.380 | 3.845 | 19.225 |
| 86 | K26:K27 | 106.363 | Φ75-110 ΧΩΜ ΕΝΤΟΣ | 45.773 | 11.443 | 57.216 |
| 87 | K42:K43 | 49.649 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.350 | 5.337 | 26.687 |
| 88 | K120:K121 | 59.254 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 25.480 | 6.370 | 31.850 |
| 89 | K81:K99 | 32.527 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.998 | 3.499 | 17.497 |
| 90 | K76:K77 | 54.703 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 23.541 | 5.885 | 29.427 |
| 91 | K8:K9 | 26.831 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.547 | 2.887 | 14.433 |
| 92 | K127:K128 | 45.365 | Φ75-110 ΧΩΜ ΕΝΤΟΣ | 19.522 | 4.881 | 24.403 |
| 93 | K130:K135 | 38.263 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.466 | 4.117 | 20.583 |
| 94 | K55:K58 | 24.008 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.332 | 2.583 | 12.914 |
| 95 | K112:K126 | 26.355 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.342 | 2.835 | 14.177 |
| 96 | K54:K57 | 7.775 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 3.346 | 0.836 | 4.182 |
| 97 | K111:K90 | 23.955 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.315 | 2.579 | 12.893 |
| 98 | K61:K65 | 59.818 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 25.742 | 6.436 | 32.178 |
| 99 | K53:K54 | 47.841 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.580 | 5.145 | 25.725 |
| 100 | K54:K55 | 17.699 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 7.627 | 1.907 | 9.533 |
| 101 | K155:K152 | 48.237 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.758 | 5.189 | 25.947 |
| 102 | K150:K143 | 33.506 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.408 | 3.602 | 18.010 |
| 103 | K147:K148 | 48.745 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.961 | 5.240 | 26.202 |
| 104 | K132:K133 | 50.939 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.905 | 5.476 | 27.381 |
| 105 | K142:K161 | 29.601 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 12.729 | 3.182 | 15.911 |
| 106 | K157:K158 | 38.587 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.593 | 4.148 | 20.742 |
| 107 | K158:K159 | 36.766 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.810 | 3.953 | 19.763 |
| 108 | K139:K140 | 47.275 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.329 | 5.082 | 25.411 |
| 109 | K167:K168 | 51.533 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.172 | 5.543 | 27.715 |
| 110 | K165:K166 | 42.702 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.363 | 4.591 | 22.954 |
| 111 | K175:K174 | 36.420 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.671 | 3.918 | 19.588 |
| 112 | K139:K176 | 52.065 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.389 | 5.597 | 27.986 |
| 113 | K145:K146 | 46.635 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.069 | 5.017 | 25.086 |
| 114 | K125:K153 | 36.229 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.579 | 3.895 | 19.474 |
| 115 | K153:K154 | 48.262 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.754 | 5.188 | 25.942 |
| 116 | K149:K148 | 31.668 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.618 | 3.405 | 17.023 |
| 117 | K86:K137 | 54.057 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 23.246 | 5.811 | 29.057 |
| 118 | K137:K138 | 52.770 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.692 | 5.673 | 28.365 |
| 119 | K177:K178 | 48.082 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.692 | 5.173 | 25.865 |
| 120 | K172:K171 | 38.459 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.548 | 4.137 | 20.686 |
| 121 | K106:K107 | 43.022 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.500 | 4.625 | 23.125 |
| 122 | K105:K106 | 37.096 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.952 | 3.988 | 19.940 |
| 123 | K104:K105 | 46.631 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.052 | 5.013 | 25.065 |
| 124 | K107:K108 | 12.510 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 5.379 | 1.345 | 6.724 |
| 125 | K113:K114 | 45.325 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.491 | 4.873 | 24.364 |
| 126 | K115:K127 | 29.441 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 12.670 | 3.167 | 15.837 |
| 127 | K131:K132 | 39.035 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.786 | 4.196 | 20.982 |
| 128 | K130:K131 | 49.661 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.366 | 5.342 | 26.708 |
| 129 | K103:K104 | 41.638 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.905 | 4.476 | 22.382 |
| 130 | K102:K103 | 45.072 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.382 | 4.845 | 24.227 |
| 131 | K101:K102 | 38.541 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 16.573 | 4.143 | 20.717 |
| 132 | K100:K101 | 40.383 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.366 | 4.341 | 21.707 |
| 133 | K69:K46 | 53.552 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 23.028 | 5.757 | 28.785 |
| 134 | K68:K69 | 48.546 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.876 | 5.219 | 26.094 |
| 135 | K67:K68 | 46.600 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.039 | 5.010 | 25.049 |
| 136 | K70:K71 | 47.212 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.302 | 5.075 | 25.377 |
| 137 | K62:K180 | 46.539 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.013 | 5.003 | 25.016 |
| 138 | K63:K64 | 40.097 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.243 | 4.311 | 21.553 |
| 139 | K78:K79 | 45.597 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 19.608 | 4.902 | 24.509 |
| 140 | K48:K49 | 41.239 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.734 | 4.433 | 22.167 |
| 141 | K49:K50 | 27.444 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 11.801 | 2.950 | 14.752 |
| 142 | K51:K52 | 43.403 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.664 | 4.666 | 23.330 |
| 143 | K52:K53 | 48.983 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.064 | 5.266 | 26.330 |
| 144 | K80:K87 | 52.401 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.533 | 5.633 | 28.167 |
| 145 | K152:K151 | 46.776 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 20.115 | 5.029 | 25.143 |
| 146 | K93:K94 | 59.577 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 25.639 | 6.410 | 32.048 |
| 147 | K4:K59 | 49.796 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.395 | 5.349 | 26.744 |
| 148 | K59:K60 | 43.183 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.554 | 4.638 | 23.192 |
| 149 | K6:K7 | 48.432 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 25.468 | 6.367 | 31.835 |
| 150 | K5:K6 | 53.378 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 28.031 | 7.008 | 35.039 |
| 151 | K72:K95 | 35.820 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.403 | 3.851 | 19.254 |
| 152 | K95:K96 | 28.068 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 12.070 | 3.018 | 15.088 |
| 153 | K135:K136 | 32.520 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.995 | 3.499 | 17.494 |
| 154 | K30:K31 | 32.055 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.784 | 3.446 | 17.230 |
| 155 | K92:K97 | 31.548 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 13.573 | 3.393 | 16.966 |
| 156 | K7:K8 | 33.748 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.523 | 3.631 | 18.154 |
| 157 | K159:K163 | 24.808 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 10.668 | 2.667 | 13.335 |
| 158 | K164:K170 | 51.429 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 22.132 | 5.533 | 27.665 |
| 159 | K163:K181 | 9.770 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 4.201 | 1.050 | 5.251 |
| 160 | K181:K164 | 13.486 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 5.818 | 1.454 | 7.272 |
| 161 | K162:K163 | 42.831 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 18.418 | 4.605 | 23.023 |
| 162 | K120:K119 | 167.736 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 72.141 | 18.035 | 90.176 |
| 163 | K119:K129 | 88.073 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 37.902 | 9.475 | 47.377 |
| 164 | K119:K118 | 15.113 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 6.505 | 1.626 | 8.131 |
| 165 | K38:K39 | 96.772 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 41.614 | 10.404 | 52.018 |
| 166 | K34:K35 | 35.588 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 15.304 | 3.826 | 19.130 |
| 167 | K33:K34 | 65.248 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 28.058 | 7.014 | 35.072 |
| 168 | K35:K36 | 129.759 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 55.799 | 13.950 | 69.749 |
| 169 | K37:K38 | 98.190 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 42.224 | 10.556 | 52.780 |
| 170 | K124:K125 | 96.728 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 41.595 | 10.399 | 51.994 |
| 171 | K123:K124 | 43.872 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 18.866 | 4.716 | 23.582 |
| 172 | K122:K123 | 67.984 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 29.234 | 7.309 | 36.543 |
| 173 | K121:K122 | 57.472 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 24.714 | 6.179 | 30.893 |
| 174 | K116:K117 | 40.720 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 17.510 | 4.378 | 21.888 |
| 175 | K115:K116 | 49.792 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 21.427 | 5.357 | 26.784 |
| 176 | K13:K14 | 56.019 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 29.443 | 7.361 | 36.803 |
| 177 | K11:K12 | 45.888 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 24.118 | 6.029 | 30.147 |
| 178 | K12:K13 | 42.105 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 22.129 | 5.532 | 27.662 |
| 179 | K24:K25 | 101.961 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 43.845 | 10.961 | 54.807 |
| 180 | K41:K42 | 44.754 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 19.245 | 4.811 | 24.057 |
| 181 | K20:K40 | 138.567 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 59.587 | 14.897 | 74.483 |
| 182 | K40:K41 | 55.182 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 23.729 | 5.932 | 29.661 |
| 183 | K17:K18 | 142.143 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 61.171 | 15.293 | 76.463 |
| 184 | K14:K15 | 39.062 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 20.530 | 5.132 | 25.662 |
| 185 | K15:K16 | 92.739 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 48.762 | 12.191 | 60.953 |
| 186 | K1:K2 | 44.759 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 24.456 | 6.114 | 30.570 |
| 187 | K2:K3 | 55.075 | ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ | 30.092 | 7.523 | 37.616 |
| 188 | K22:K23 | 62.715 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 26.969 | 6.742 | 33.711 |
| 189 | K118:K117 | 44.048 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 18.942 | 4.735 | 23.677 |
| 190 | K45:K23 | 155.732 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 66.968 | 16.742 | 83.710 |
| 191 | K27:K28 | 212.639 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 91.508 | 22.877 | 114.385 |
| 192 | K28:K29 | 101.283 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 43.586 | 10.897 | 54.483 |
| 193 | K36:K37 | 92.485 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 39.771 | 9.943 | 49.713 |
| 194 | K21:K22 | 125.535 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 65.978 | 16.495 | 82.473 |
| 195 | K18:K19 | 162.098 | Φ75-110 ΧΩΜ ΕΚΤΟΣ | 69.758 | 17.439 | 87.197 |
| 196 | K44:K45 | 33.613 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 14.454 | 3.614 | 18.068 |
| 197 | K25:K26 | 124.543 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 53.566 | 13.391 | 66.957 |
| 198 | K89:K90 | 2.849 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 1.229 | 0.307 | 1.536 |
| 199 | K32:K33 | 58.886 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 25.322 | 6.331 | 31.653 |
| 200 | K86:K109 | 7.333 | Φ75-110 ΑΣΦ ΕΝΤΟΣ | 3.153 | 0.788 | 3.942 |
| 201 | R1:K1 | 144.348 | ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ | 78.871 | 19.718 | 98.588 |
| 202 | K54:K57 | 22.925 | Φ75-110 ΧΩΜ ΕΝΤΟΣ | 9.866 | 2.466 | 12.332 |
| 203 | K55:K58 | 25.122 | Φ75-110 ΧΩΜ ΕΝΤΟΣ | 10.811 | 2.703 | 13.514 |
| 204 | K115:K127 | 25.661 | Φ75-110 ΧΩΜ ΕΝΤΟΣ | 11.043 | 2.761 | 13.804 |
| 205 | K21:K22 | 41.730 | Φ75-110 ΑΣΦ ΕΚΤΟΣ | 17.945 | 4.486 | 22.431 |
|  | Total | 9786.226 | Total | 4338.500 | 1084.625 | 5423.124 |

# 2. Excavation volume

## 2.1. Pipe excavations

### 2.1.1. Total

| From excavation matrix (m³) | 5423.124 |
| --- | --- |

### 2.1.2. Soft soil excavation

| From excavation matrix (m³) | 4338.500 |
| --- | --- |

### 2.1.3. Rock excavations

| From excavation matrix (m³) | 1084.625 |
| --- | --- |

## 2.2. Trench backfill

### 2.2.1.Total backfill volume

| Total volume (m³) | 2386.460 |
| --- | --- |

### 2.2.2. Restoration (asphalt)

| Total length (m) | 8297.441 |
| --- | --- |
| Total area (m²) | 3830.7820 |
| Total volume (m³) | 409.735 |
| Mean thickness (m) | 0.107 |

## 2.3. Augmented soil volume to be transported

| Augmented soil volume to be transported (m³) | 3850.133 |
| --- | --- |

## 2.4. Transportation of soil volume

| Mean transportation distance (m) | 10000.000 |
| --- | --- |
| Total (km.m³) | 38501 |

## 2.5. Trench support

| Total support area (m²) | 0.0000 |
| --- | --- |

## 2.6. Water pumping

| Number of pumps | 0 |
| --- | --- |
| Pump diameter (inch) | 2 |
| Pump operation time (h) | 0.00 |

## 2.7. Dislocation of public utilities

| Expected dislocation of public utilities (m) | 0.000 |
| --- | --- |

# 3. Pipe Sections

## 3.1. Section : D65.8 x .0001

| # | From Node | To Node | Pipe Name | Length (m) |
| --- | --- | --- | --- | --- |
| 1 | K92 | K93 | K92:K93 | 49.104 |
| 2 | K168 | K169 | K168:K169 | 22.806 |
| 3 | K144 | K145 | K144:K145 | 44.326 |
| 4 | K155 | K156 | K155:K156 | 72.682 |
| 5 | K174 | K179 | K174:K179 | 15.234 |
| 6 | K172 | K177 | K172:K177 | 48.224 |
| 7 | K90 | K91 | K90:K91 | 36.320 |
| 8 | K84 | K110 | K84:K110 | 40.214 |
| 9 | K16 | K17 | K16:K17 | 35.739 |
| 10 | K26 | K27 | K26:K27 | 106.363 |
| 11 | K81 | K99 | K81:K99 | 32.527 |
| 12 | K76 | K77 | K76:K77 | 54.703 |
| 13 | K8 | K9 | K8:K9 | 26.831 |
| 14 | K127 | K128 | K127:K128 | 45.365 |
| 15 | K130 | K135 | K130:K135 | 38.263 |
| 16 | K55 | K58/55 | K55:K58 | 24.008 |
| 17 | K112 | K126 | K112:K126 | 26.355 |
| 18 | K54 | K54/K57 | K54:K57 | 7.775 |
| 19 | K61 | K65 | K61:K65 | 59.818 |
| 20 | K145 | K146 | K145:K146 | 46.635 |
| 21 | K177 | K178 | K177:K178 | 48.082 |
| 22 | K115 | K127/K115 | K115:K127 | 29.441 |
| 23 | K93 | K94 | K93:K94 | 59.577 |
| 24 | K135 | K136 | K135:K136 | 32.520 |
| 25 | K7 | K8 | K7:K8 | 33.748 |
| 26 | K164 | K170 | K164:K170 | 51.429 |
| 27 | K119 | K129 | K119:K129 | 88.073 |
| 28 | K17 | K18 | K17:K18 | 142.143 |
| 29 | K27 | K28 | K27:K28 | 212.639 |
| 30 | K28 | K29 | K28:K29 | 101.283 |
| 31 | K18 | K19 | K18:K19 | 162.098 |
| 32 | K54/K57 | K57 | K54:K57 | 22.925 |
| 33 | K58/55 | K58 | K55:K58 | 25.122 |
| 34 | K127/K115 | K127 | K115:K127 | 25.661 |
|  |  |  | Total | 1868.034 |

## 3.2. Section : D79 x .0001

| # | From Node | To Node | Pipe Name | Length (m) |
| --- | --- | --- | --- | --- |
| 1 | K64 | K70 | K64:K70 | 43.824 |
| 2 | K180 | K71 | K180:K71 | 41.354 |
| 3 | K62 | K63 | K62:K63 | 41.009 |
| 4 | K75 | K80 | K75:K80 | 48.994 |
| 5 | K97 | K98 | K97:K98 | 36.179 |
| 6 | K72 | K92 | K72:K92 | 39.277 |
| 7 | K108 | K109 | K108:K109 | 32.423 |
| 8 | K82 | K83 | K82:K83 | 34.307 |
| 9 | K83 | K84 | K83:K84 | 15.110 |
| 10 | K84 | K85 | K84:K85 | 23.309 |
| 11 | K98 | K100 | K98:K100 | 14.871 |
| 12 | K98 | K81 | K98:K81 | 31.417 |
| 13 | K100 | K82 | K100:K82 | 26.691 |
| 14 | K82 | K88 | K82:K88 | 49.234 |
| 15 | K87 | K88 | K87:K88 | 46.348 |
| 16 | K80 | K81 | K80:K81 | 20.466 |
| 17 | K81 | K82 | K81:K82 | 47.215 |
| 18 | K85 | K111 | K85:K111 | 53.373 |
| 19 | K111 | K56 | K111:K56 | 52.698 |
| 20 | K56 | K112 | K56:K112 | 20.260 |
| 21 | K112 | K113 | K112:K113 | 26.953 |
| 22 | K113 | K130 | K113:K130 | 24.892 |
| 23 | K132 | K147 | K132:K147 | 42.072 |
| 24 | K143 | K142 | K143:K142 | 14.532 |
| 25 | K142 | K141 | K142:K141 | 11.048 |
| 26 | K140 | K141 | K140:K141 | 42.491 |
| 27 | K138 | K139 | K138:K139 | 53.177 |
| 28 | K85 | K86 | K85:K86 | 10.581 |
| 29 | K139 | K165 | K139:K165 | 47.362 |
| 30 | K166 | K175 | K166:K175 | 26.373 |
| 31 | K173 | K174 | K173:K174 | 33.572 |
| 32 | K176 | K173 | K176:K173 | 43.421 |
| 33 | K141 | K157 | K141:K157 | 42.885 |
| 34 | K161 | K160 | K161:K160 | 35.838 |
| 35 | K160 | K162 | K160:K162 | 32.554 |
| 36 | K160 | K159 | K160:K159 | 11.120 |
| 37 | K66 | K67 | K66:K67 | 49.514 |
| 38 | K46 | K47 | K46:K47 | 23.336 |
| 39 | K75 | K78 | K75:K78 | 32.497 |
| 40 | K96 | K75 | K96:K75 | 55.207 |
| 41 | K71 | K72 | K71:K72 | 12.181 |
| 42 | K66 | K64 | K66:K64 | 16.239 |
| 43 | K125 | K134 | K125:K134 | 21.115 |
| 44 | K134 | K149 | K134:K149 | 44.127 |
| 45 | K148 | K150 | K148:K150 | 41.418 |
| 46 | K143 | K144 | K143:K144 | 39.636 |
| 47 | K151 | K144 | K151:K144 | 58.060 |
| 48 | K154 | K155 | K154:K155 | 38.416 |
| 49 | K166 | K167 | K166:K167 | 41.036 |
| 50 | K168 | K164 | K168:K164 | 36.006 |
| 51 | K47 | K48 | K47:K48 | 40.532 |
| 52 | K79 | K50 | K79:K50 | 42.870 |
| 53 | K76 | K78 | K76:K78 | 47.790 |
| 54 | K47 | K76 | K47:K76 | 46.015 |
| 55 | K43 | K46 | K43:K46 | 13.007 |
| 56 | K43 | K44 | K43:K44 | 38.995 |
| 57 | K23 | K24 | K23:K24 | 52.659 |
| 58 | K26 | K30 | K26:K30 | 40.417 |
| 59 | K51 | K31 | K51:K31 | 20.864 |
| 60 | K50 | K51 | K50:K51 | 9.060 |
| 61 | K114 | K115 | K114:K115 | 32.838 |
| 62 | K55 | K56 | K55:K56 | 16.079 |
| 63 | K171 | K109 | K171:K109 | 36.765 |
| 64 | K173 | K172 | K173:K172 | 13.192 |
| 65 | K133 | K134 | K133:K134 | 45.326 |
| 66 | K89 | K83 | K89:K83 | 47.706 |
| 67 | K88 | K89 | K88:K89 | 8.660 |
| 68 | K10 | K11 | K10:K11 | 43.991 |
| 69 | K16 | K20 | K16:K20 | 11.893 |
| 70 | K20 | K21 | K20:K21 | 109.575 |
| 71 | K42 | K43 | K42:K43 | 49.649 |
| 72 | K120 | K121 | K120:K121 | 59.254 |
| 73 | K111 | K90 | K111:K90 | 23.955 |
| 74 | K53 | K54 | K53:K54 | 47.841 |
| 75 | K54 | K55 | K54:K55 | 17.699 |
| 76 | K155 | K152 | K155:K152 | 48.237 |
| 77 | K150 | K143 | K150:K143 | 33.506 |
| 78 | K147 | K148 | K147:K148 | 48.745 |
| 79 | K132 | K133 | K132:K133 | 50.939 |
| 80 | K142 | K161 | K142:K161 | 29.601 |
| 81 | K157 | K158 | K157:K158 | 38.587 |
| 82 | K158 | K159 | K158:K159 | 36.766 |
| 83 | K139 | K140 | K139:K140 | 47.275 |
| 84 | K167 | K168 | K167:K168 | 51.533 |
| 85 | K165 | K166 | K165:K166 | 42.702 |
| 86 | K175 | K174 | K175:K174 | 36.420 |
| 87 | K139 | K176 | K139:K176 | 52.065 |
| 88 | K125 | K153 | K125:K153 | 36.229 |
| 89 | K153 | K154 | K153:K154 | 48.262 |
| 90 | K149 | K148 | K149:K148 | 31.668 |
| 91 | K86 | K137 | K86:K137 | 54.057 |
| 92 | K137 | K138 | K137:K138 | 52.770 |
| 93 | K172 | K171 | K172:K171 | 38.459 |
| 94 | K106 | K107 | K106:K107 | 43.022 |
| 95 | K105 | K106 | K105:K106 | 37.096 |
| 96 | K104 | K105 | K104:K105 | 46.631 |
| 97 | K107 | K108 | K107:K108 | 12.510 |
| 98 | K113 | K114 | K113:K114 | 45.325 |
| 99 | K131 | K132 | K131:K132 | 39.035 |
| 100 | K130 | K131 | K130:K131 | 49.661 |
| 101 | K103 | K104 | K103:K104 | 41.638 |
| 102 | K102 | K103 | K102:K103 | 45.072 |
| 103 | K101 | K102 | K101:K102 | 38.541 |
| 104 | K100 | K101 | K100:K101 | 40.383 |
| 105 | K69 | K46 | K69:K46 | 53.552 |
| 106 | K68 | K69 | K68:K69 | 48.546 |
| 107 | K67 | K68 | K67:K68 | 46.600 |
| 108 | K70 | K71 | K70:K71 | 47.212 |
| 109 | K62 | K180 | K62:K180 | 46.539 |
| 110 | K63 | K64 | K63:K64 | 40.097 |
| 111 | K78 | K79 | K78:K79 | 45.597 |
| 112 | K48 | K49 | K48:K49 | 41.239 |
| 113 | K49 | K50 | K49:K50 | 27.444 |
| 114 | K51 | K52 | K51:K52 | 43.403 |
| 115 | K52 | K53 | K52:K53 | 48.983 |
| 116 | K80 | K87 | K80:K87 | 52.401 |
| 117 | K152 | K151 | K152:K151 | 46.776 |
| 118 | K72 | K95 | K72:K95 | 35.820 |
| 119 | K95 | K96 | K95:K96 | 28.068 |
| 120 | K30 | K31 | K30:K31 | 32.055 |
| 121 | K92 | K97 | K92:K97 | 31.548 |
| 122 | K159 | K163 | K159:K163 | 24.808 |
| 123 | K163 | K181 | K163:K181 | 9.770 |
| 124 | K181 | K164 | K181:K164 | 13.486 |
| 125 | K162 | K163 | K162:K163 | 42.831 |
| 126 | K120 | K119 | K120:K119 | 167.736 |
| 127 | K119 | K118 | K119:K118 | 15.113 |
| 128 | K38 | K39 | K38:K39 | 96.772 |
| 129 | K34 | K35 | K34:K35 | 35.588 |
| 130 | K33 | K34 | K33:K34 | 65.248 |
| 131 | K35 | K36 | K35:K36 | 129.759 |
| 132 | K37 | K38 | K37:K38 | 98.190 |
| 133 | K124 | K125 | K124:K125 | 96.728 |
| 134 | K123 | K124 | K123:K124 | 43.872 |
| 135 | K122 | K123 | K122:K123 | 67.984 |
| 136 | K121 | K122 | K121:K122 | 57.472 |
| 137 | K116 | K117 | K116:K117 | 40.720 |
| 138 | K115 | K116 | K115:K116 | 49.792 |
| 139 | K13 | K14 | K13:K14 | 56.019 |
| 140 | K11 | K12 | K11:K12 | 45.888 |
| 141 | K12 | K13 | K12:K13 | 42.105 |
| 142 | K24 | K25 | K24:K25 | 101.961 |
| 143 | K41 | K42 | K41:K42 | 44.754 |
| 144 | K20 | K40 | K20:K40 | 138.567 |
| 145 | K40 | K41 | K40:K41 | 55.182 |
| 146 | K14 | K15 | K14:K15 | 39.062 |
| 147 | K15 | K16 | K15:K16 | 92.739 |
| 148 | K22 | K23 | K22:K23 | 62.715 |
| 149 | K118 | K117 | K118:K117 | 44.048 |
| 150 | K45 | K23 | K45:K23 | 155.732 |
| 151 | K36 | K37 | K36:K37 | 92.485 |
| 152 | K21 | K21/K22 | K21:K22 | 125.535 |
| 153 | K44 | K45 | K44:K45 | 33.613 |
| 154 | K25 | K26 | K25:K26 | 124.543 |
| 155 | K89 | K90 | K89:K90 | 2.849 |
| 156 | K32 | K33 | K32:K33 | 58.886 |
| 157 | K86 | K109 | K86:K109 | 7.333 |
| 158 | K21/K22 | K22 | K21:K22 | 41.730 |
|  |  |  | Total | 6996.877 |

## 3.3. Section : D97 x .0001

| # | From Node | To Node | Pipe Name | Length (m) |
| --- | --- | --- | --- | --- |
| 1 | K4 | K5 | K4:K5 | 51.913 |
| 2 | K7 | K10 | K7:K10 | 4.624 |
| 3 | K10 | K66 | K10:K66 | 43.658 |
| 4 | K61 | K62 | K61:K62 | 58.904 |
| 5 | K60 | K61 | K60:K61 | 40.376 |
| 6 | K4 | K59 | K4:K59 | 49.796 |
| 7 | K59 | K60 | K59:K60 | 43.183 |
| 8 | K6 | K7 | K6:K7 | 48.432 |
| 9 | K5 | K6 | K5:K6 | 53.378 |
|  |  |  | Total | 394.264 |

## 3.4. Section : D123.6 x .0001

| # | From Node | To Node | Pipe Name | Length (m) |
| --- | --- | --- | --- | --- |
| 1 | R1 | R1/K1 | R1:K1 | 282.869 |
| 2 | K1 | K2 | K1:K2 | 44.759 |
| 3 | K2 | K3 | K2:K3 | 55.075 |
| 4 | R1/K1 | K1 | R1:K1 | 144.348 |
|  |  |  | Total | 527.051 |

# 4. Marking grid

| Total length (m) | 9786.226 |
| --- | --- |

# 5. Manholes (per type)

# 6. Manholes

# 7. Trenches

## 7.1. Trench : Φ75-110 ΧΩΜ ΕΝΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K26:K27 | 106.363 | 9.573 | 2.788 | 14.359 |
| 2 | K127:K128 | 45.365 | 4.083 | 1.189 | 6.124 |
| 3 | K54:K57 | 22.925 | 2.063 | 0.601 | 3.095 |
| 4 | K55:K58 | 25.122 | 2.261 | 0.658 | 3.392 |
| 5 | K115:K127 | 25.661 | 2.310 | 0.673 | 3.464 |
|  | Σύνολο: | 225.437 | 20.289 | 5.909 | 30.434 |

## 7.2. Trench : Φ75-110 ΑΣΦ ΕΝΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K10:K66 | 43.658 | 3.929 | 1.583 | 5.894 |
| 2 | K61:K62 | 58.904 | 5.301 | 2.136 | 7.952 |
| 3 | K60:K61 | 40.376 | 3.634 | 1.464 | 5.451 |
| 4 | K64:K70 | 43.824 | 3.944 | 1.343 | 5.916 |
| 5 | K180:K71 | 41.354 | 3.722 | 1.267 | 5.583 |
| 6 | K62:K63 | 41.009 | 3.691 | 1.257 | 5.536 |
| 7 | K75:K80 | 48.994 | 4.409 | 1.502 | 6.614 |
| 8 | K97:K98 | 36.179 | 3.256 | 1.109 | 4.884 |
| 9 | K72:K92 | 39.277 | 3.535 | 1.204 | 5.302 |
| 10 | K92:K93 | 49.104 | 4.419 | 1.287 | 6.629 |
| 11 | K108:K109 | 32.423 | 2.918 | 0.994 | 4.377 |
| 12 | K82:K83 | 34.307 | 3.088 | 1.051 | 4.631 |
| 13 | K83:K84 | 15.110 | 1.360 | 0.463 | 2.040 |
| 14 | K84:K85 | 23.309 | 2.098 | 0.714 | 3.147 |
| 15 | K98:K100 | 14.871 | 1.338 | 0.456 | 2.008 |
| 16 | K98:K81 | 31.417 | 2.828 | 0.963 | 4.241 |
| 17 | K100:K82 | 26.691 | 2.402 | 0.818 | 3.603 |
| 18 | K82:K88 | 49.234 | 4.431 | 1.509 | 6.647 |
| 19 | K87:K88 | 46.348 | 4.171 | 1.420 | 6.257 |
| 20 | K80:K81 | 20.466 | 1.842 | 0.627 | 2.763 |
| 21 | K81:K82 | 47.215 | 4.249 | 1.447 | 6.374 |
| 22 | K85:K111 | 53.373 | 4.804 | 1.636 | 7.205 |
| 23 | K111:K56 | 52.698 | 4.743 | 1.615 | 7.114 |
| 24 | K56:K112 | 20.260 | 1.823 | 0.621 | 2.735 |
| 25 | K112:K113 | 26.953 | 2.426 | 0.826 | 3.639 |
| 26 | K113:K130 | 24.892 | 2.240 | 0.763 | 3.360 |
| 27 | K132:K147 | 42.072 | 3.786 | 1.289 | 5.680 |
| 28 | K143:K142 | 14.532 | 1.308 | 0.445 | 1.962 |
| 29 | K142:K141 | 11.048 | 0.994 | 0.339 | 1.491 |
| 30 | K140:K141 | 42.491 | 3.824 | 1.302 | 5.736 |
| 31 | K138:K139 | 53.177 | 4.786 | 1.630 | 7.179 |
| 32 | K85:K86 | 10.581 | 0.952 | 0.324 | 1.428 |
| 33 | K139:K165 | 47.362 | 4.263 | 1.452 | 6.394 |
| 34 | K166:K175 | 26.373 | 2.374 | 0.808 | 3.560 |
| 35 | K173:K174 | 33.572 | 3.021 | 1.029 | 4.532 |
| 36 | K176:K173 | 43.421 | 3.908 | 1.331 | 5.862 |
| 37 | K141:K157 | 42.885 | 3.860 | 1.314 | 5.789 |
| 38 | K161:K160 | 35.838 | 3.225 | 1.098 | 4.838 |
| 39 | K160:K162 | 32.554 | 2.930 | 0.998 | 4.395 |
| 40 | K160:K159 | 11.120 | 1.001 | 0.341 | 1.501 |
| 41 | K66:K67 | 49.514 | 4.456 | 1.518 | 6.684 |
| 42 | K46:K47 | 23.336 | 2.100 | 0.715 | 3.150 |
| 43 | K75:K78 | 32.497 | 2.925 | 0.996 | 4.387 |
| 44 | K96:K75 | 55.207 | 4.969 | 1.692 | 7.453 |
| 45 | K71:K72 | 12.181 | 1.096 | 0.373 | 1.644 |
| 46 | K66:K64 | 16.239 | 1.462 | 0.498 | 2.192 |
| 47 | K125:K134 | 21.115 | 1.900 | 0.647 | 2.851 |
| 48 | K134:K149 | 44.127 | 3.971 | 1.352 | 5.957 |
| 49 | K148:K150 | 41.418 | 3.728 | 1.269 | 5.591 |
| 50 | K143:K144 | 39.636 | 3.567 | 1.215 | 5.351 |
| 51 | K151:K144 | 58.060 | 5.225 | 1.779 | 7.838 |
| 52 | K154:K155 | 38.416 | 3.457 | 1.177 | 5.186 |
| 53 | K166:K167 | 41.036 | 3.693 | 1.258 | 5.540 |
| 54 | K168:K164 | 36.006 | 3.241 | 1.104 | 4.861 |
| 55 | K168:K169 | 22.806 | 2.053 | 0.598 | 3.079 |
| 56 | K144:K145 | 44.326 | 3.989 | 1.162 | 5.984 |
| 57 | K47:K48 | 40.532 | 3.648 | 1.242 | 5.472 |
| 58 | K79:K50 | 42.870 | 3.858 | 1.314 | 5.787 |
| 59 | K76:K78 | 47.790 | 4.301 | 1.465 | 6.452 |
| 60 | K47:K76 | 46.015 | 4.141 | 1.410 | 6.212 |
| 61 | K43:K46 | 13.007 | 1.171 | 0.399 | 1.756 |
| 62 | K43:K44 | 38.995 | 3.510 | 1.195 | 5.264 |
| 63 | K26:K30 | 40.417 | 3.638 | 1.239 | 5.456 |
| 64 | K51:K31 | 20.864 | 1.878 | 0.639 | 2.817 |
| 65 | K50:K51 | 9.060 | 0.815 | 0.278 | 1.223 |
| 66 | K174:K179 | 15.234 | 1.371 | 0.399 | 2.057 |
| 67 | K114:K115 | 32.838 | 2.955 | 1.006 | 4.433 |
| 68 | K55:K56 | 16.079 | 1.447 | 0.493 | 2.171 |
| 69 | K171:K109 | 36.765 | 3.309 | 1.127 | 4.963 |
| 70 | K173:K172 | 13.192 | 1.187 | 0.404 | 1.781 |
| 71 | K172:K177 | 48.224 | 4.340 | 1.264 | 6.510 |
| 72 | K133:K134 | 45.326 | 4.079 | 1.389 | 6.119 |
| 73 | K90:K91 | 36.320 | 3.269 | 0.952 | 4.903 |
| 74 | K89:K83 | 47.706 | 4.294 | 1.462 | 6.440 |
| 75 | K88:K89 | 8.660 | 0.779 | 0.265 | 1.169 |
| 76 | K84:K110 | 40.214 | 3.619 | 1.054 | 5.429 |
| 77 | K42:K43 | 49.649 | 4.468 | 1.522 | 6.703 |
| 78 | K81:K99 | 32.527 | 2.927 | 0.853 | 4.391 |
| 79 | K76:K77 | 54.703 | 4.923 | 1.434 | 7.385 |
| 80 | K8:K9 | 26.831 | 2.415 | 0.703 | 3.622 |
| 81 | K130:K135 | 38.263 | 3.444 | 1.003 | 5.165 |
| 82 | K55:K58 | 24.008 | 2.161 | 0.629 | 3.241 |
| 83 | K112:K126 | 26.355 | 2.372 | 0.691 | 3.558 |
| 84 | K54:K57 | 7.775 | 0.700 | 0.204 | 1.050 |
| 85 | K111:K90 | 23.955 | 2.156 | 0.734 | 3.234 |
| 86 | K61:K65 | 59.818 | 5.384 | 1.568 | 8.075 |
| 87 | K53:K54 | 47.841 | 4.306 | 1.466 | 6.458 |
| 88 | K54:K55 | 17.699 | 1.593 | 0.542 | 2.389 |
| 89 | K155:K152 | 48.237 | 4.341 | 1.478 | 6.512 |
| 90 | K150:K143 | 33.506 | 3.016 | 1.027 | 4.523 |
| 91 | K147:K148 | 48.745 | 4.387 | 1.494 | 6.581 |
| 92 | K132:K133 | 50.939 | 4.585 | 1.561 | 6.877 |
| 93 | K142:K161 | 29.601 | 2.664 | 0.907 | 3.996 |
| 94 | K157:K158 | 38.587 | 3.473 | 1.183 | 5.209 |
| 95 | K158:K159 | 36.766 | 3.309 | 1.127 | 4.963 |
| 96 | K139:K140 | 47.275 | 4.255 | 1.449 | 6.382 |
| 97 | K167:K168 | 51.533 | 4.638 | 1.579 | 6.957 |
| 98 | K165:K166 | 42.702 | 3.843 | 1.309 | 5.765 |
| 99 | K175:K174 | 36.420 | 3.278 | 1.116 | 4.917 |
| 100 | K139:K176 | 52.065 | 4.686 | 1.596 | 7.029 |
| 101 | K145:K146 | 46.635 | 4.197 | 1.222 | 6.296 |
| 102 | K125:K153 | 36.229 | 3.261 | 1.110 | 4.891 |
| 103 | K153:K154 | 48.262 | 4.344 | 1.479 | 6.515 |
| 104 | K149:K148 | 31.668 | 2.850 | 0.971 | 4.275 |
| 105 | K86:K137 | 54.057 | 4.865 | 1.657 | 7.298 |
| 106 | K137:K138 | 52.770 | 4.749 | 1.617 | 7.124 |
| 107 | K177:K178 | 48.082 | 4.327 | 1.260 | 6.491 |
| 108 | K172:K171 | 38.459 | 3.461 | 1.179 | 5.192 |
| 109 | K106:K107 | 43.022 | 3.872 | 1.319 | 5.808 |
| 110 | K105:K106 | 37.096 | 3.339 | 1.137 | 5.008 |
| 111 | K104:K105 | 46.631 | 4.197 | 1.429 | 6.295 |
| 112 | K107:K108 | 12.510 | 1.126 | 0.383 | 1.689 |
| 113 | K113:K114 | 45.325 | 4.079 | 1.389 | 6.119 |
| 114 | K115:K127 | 29.441 | 2.650 | 0.772 | 3.974 |
| 115 | K131:K132 | 39.035 | 3.513 | 1.196 | 5.270 |
| 116 | K130:K131 | 49.661 | 4.469 | 1.522 | 6.704 |
| 117 | K103:K104 | 41.638 | 3.747 | 1.276 | 5.621 |
| 118 | K102:K103 | 45.072 | 4.056 | 1.381 | 6.085 |
| 119 | K101:K102 | 38.541 | 3.469 | 1.181 | 5.203 |
| 120 | K100:K101 | 40.383 | 3.635 | 1.238 | 5.452 |
| 121 | K69:K46 | 53.552 | 4.820 | 1.641 | 7.229 |
| 122 | K68:K69 | 48.546 | 4.369 | 1.488 | 6.554 |
| 123 | K67:K68 | 46.600 | 4.194 | 1.428 | 6.291 |
| 124 | K70:K71 | 47.212 | 4.249 | 1.447 | 6.374 |
| 125 | K62:K180 | 46.539 | 4.188 | 1.426 | 6.283 |
| 126 | K63:K64 | 40.097 | 3.609 | 1.229 | 5.413 |
| 127 | K78:K79 | 45.597 | 4.104 | 1.397 | 6.156 |
| 128 | K48:K49 | 41.239 | 3.712 | 1.264 | 5.567 |
| 129 | K49:K50 | 27.444 | 2.470 | 0.841 | 3.705 |
| 130 | K51:K52 | 43.403 | 3.906 | 1.330 | 5.859 |
| 131 | K52:K53 | 48.983 | 4.408 | 1.501 | 6.613 |
| 132 | K80:K87 | 52.401 | 4.716 | 1.606 | 7.074 |
| 133 | K152:K151 | 46.776 | 4.210 | 1.434 | 6.315 |
| 134 | K93:K94 | 59.577 | 5.362 | 1.561 | 8.043 |
| 135 | K4:K59 | 49.796 | 4.482 | 1.806 | 6.722 |
| 136 | K59:K60 | 43.183 | 3.886 | 1.566 | 5.830 |
| 137 | K72:K95 | 35.820 | 3.224 | 1.098 | 4.836 |
| 138 | K95:K96 | 28.068 | 2.526 | 0.860 | 3.789 |
| 139 | K135:K136 | 32.520 | 2.927 | 0.852 | 4.390 |
| 140 | K30:K31 | 32.055 | 2.885 | 0.982 | 4.327 |
| 141 | K92:K97 | 31.548 | 2.839 | 0.967 | 4.259 |
| 142 | K7:K8 | 33.748 | 3.037 | 0.885 | 4.556 |
| 143 | K159:K163 | 24.808 | 2.233 | 0.760 | 3.349 |
| 144 | K164:K170 | 51.429 | 4.629 | 1.348 | 6.943 |
| 145 | K163:K181 | 9.770 | 0.879 | 0.299 | 1.319 |
| 146 | K181:K164 | 13.486 | 1.214 | 0.413 | 1.821 |
| 147 | K162:K163 | 42.831 | 3.855 | 1.313 | 5.782 |
| 148 | K34:K35 | 35.588 | 3.203 | 1.091 | 4.804 |
| 149 | K33:K34 | 65.248 | 5.872 | 2.000 | 8.808 |
| 150 | K124:K125 | 96.728 | 8.706 | 2.965 | 13.058 |
| 151 | K116:K117 | 40.720 | 3.665 | 1.248 | 5.497 |
| 152 | K115:K116 | 49.792 | 4.481 | 1.526 | 6.722 |
| 153 | K44:K45 | 33.613 | 3.025 | 1.030 | 4.538 |
| 154 | K89:K90 | 2.849 | 0.256 | 0.087 | 0.385 |
| 155 | K32:K33 | 58.886 | 5.300 | 1.805 | 7.950 |
| 156 | K86:K109 | 7.333 | 0.660 | 0.225 | 0.990 |
|  | Σύνολο: | 5843.399 | 525.906 | 176.739 | 788.859 |

## 7.3. Trench : ΔΙΠΛΟΣ ΑΣΦ ΕΝΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K4:K5 | 51.913 | 5.710 | 2.386 | 8.566 |
| 2 | K7:K10 | 4.624 | 0.509 | 0.213 | 0.763 |
| 3 | K10:K11 | 43.991 | 4.839 | 1.696 | 7.259 |
| 4 | K6:K7 | 48.432 | 5.327 | 2.226 | 7.991 |
| 5 | K5:K6 | 53.378 | 5.872 | 2.453 | 8.807 |
| 6 | K11:K12 | 45.888 | 5.048 | 1.769 | 7.572 |
| 7 | K12:K13 | 42.105 | 4.632 | 1.623 | 6.947 |
| 8 | K1:K2 | 44.759 | 4.923 | 2.506 | 7.385 |
| 9 | K2:K3 | 55.075 | 6.058 | 3.083 | 9.087 |
|  | Σύνολο: | 390.165 | 42.918 | 17.954 | 64.377 |

## 7.4. Trench : Φ75-110 ΧΩΜ ΕΚΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K16:K17 | 35.739 | 3.217 | 0.937 | 4.825 |
| 2 | K119:K129 | 88.073 | 7.927 | 2.308 | 11.890 |
| 3 | K41:K42 | 44.754 | 4.028 | 1.372 | 6.042 |
| 4 | K20:K40 | 138.567 | 12.471 | 4.247 | 18.707 |
| 5 | K40:K41 | 55.182 | 4.966 | 1.691 | 7.450 |
| 6 | K17:K18 | 142.143 | 12.793 | 3.726 | 19.189 |
| 7 | K27:K28 | 212.639 | 19.138 | 5.573 | 28.706 |
| 8 | K28:K29 | 101.283 | 9.115 | 2.655 | 13.673 |
| 9 | K18:K19 | 162.098 | 14.589 | 4.249 | 21.883 |
|  | Σύνολο: | 980.479 | 88.243 | 26.757 | 132.365 |

## 7.5. Trench : Φ75-110 ΑΣΦ ΕΚΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K155:K156 | 72.682 | 6.541 | 1.905 | 9.812 |
| 2 | K23:K24 | 52.659 | 4.739 | 1.614 | 7.109 |
| 3 | K120:K121 | 59.254 | 5.333 | 1.816 | 7.999 |
| 4 | K120:K119 | 167.736 | 15.096 | 5.141 | 22.644 |
| 5 | K119:K118 | 15.113 | 1.360 | 0.463 | 2.040 |
| 6 | K38:K39 | 96.772 | 8.710 | 2.966 | 13.064 |
| 7 | K35:K36 | 129.759 | 11.678 | 3.977 | 17.517 |
| 8 | K37:K38 | 98.190 | 8.837 | 3.009 | 13.256 |
| 9 | K123:K124 | 43.872 | 3.948 | 1.345 | 5.923 |
| 10 | K122:K123 | 67.984 | 6.119 | 2.084 | 9.178 |
| 11 | K121:K122 | 57.472 | 5.172 | 1.761 | 7.759 |
| 12 | K24:K25 | 101.961 | 9.176 | 3.125 | 13.765 |
| 13 | K22:K23 | 62.715 | 5.644 | 1.922 | 8.467 |
| 14 | K118:K117 | 44.048 | 3.964 | 1.350 | 5.946 |
| 15 | K45:K23 | 155.732 | 14.016 | 4.773 | 21.024 |
| 16 | K36:K37 | 92.485 | 8.324 | 2.835 | 12.486 |
| 17 | K25:K26 | 124.543 | 11.209 | 3.817 | 16.813 |
| 18 | K21:K22 | 41.730 | 3.756 | 1.279 | 5.634 |
|  | Σύνολο: | 1484.708 | 133.624 | 45.181 | 200.436 |

## 7.6. Trench : ΔΙΠΛΟΣ ΑΣΦ ΕΚΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | K16:K20 | 11.893 | 1.308 | 0.458 | 1.962 |
| 2 | K20:K21 | 109.575 | 12.053 | 4.224 | 18.080 |
| 3 | K13:K14 | 56.019 | 6.162 | 2.159 | 9.243 |
| 4 | K14:K15 | 39.062 | 4.297 | 1.506 | 6.445 |
| 5 | K15:K16 | 92.739 | 10.201 | 3.575 | 15.302 |
| 6 | K21:K22 | 125.535 | 13.809 | 4.839 | 20.713 |
| 7 | R1:K1 | 144.348 | 15.878 | 8.081 | 23.817 |
|  | Σύνολο: | 579.170 | 63.709 | 24.842 | 95.563 |

## 7.7. Trench : ΔΙΠΛΟΣ ΧΩΜ ΕΚΤΟΣ (Type V)

| # | Pipe | Length (m) | Base Quarry sand (m³) | Confinement Quarry sand (m³) | Cover Quarry sand (m³) |
| --- | --- | --- | --- | --- | --- |
| 1 | R1:K1 | 282.869 | 31.116 | 15.835 | 46.673 |
|  | Σύνολο: | 282.869 | 31.116 | 15.835 | 46.673 |

# 8. Special Devices Count

| No | Type | Number |
| --- | --- | --- |
| 1 | Vacuum valves | 7 |
| 2 | Air release valves | 8 |
| 3 | Pipe valves | 0 |
| 4 | Fire hydrants | 10 |
| 5 | Pressure release valves | 0 |