Water Networks v9.0 - Calculations Report Copyright ©1996-2010 TechnoLogismiki www.technologismiki.com

Contents

Project information	3

Pipes Specifications	3

D67.8 x .000125	3

D81.4 x .000125	3

Nodes	4

Reservoirs	11

Pipes	11

Energy	24

Reactions	25

General options	25

Times	25

Coordinates	25

Background	33

Results	33

Time instant01/01/2005 - 00:00:00	33

Junctions	33

Pipes	41

Reservoirs	48

# Project information

# Pipes Specifications

## D67.8 x .000125

| Shape data |
| --- |
| Type | Circular |
| Inner diameter (m) | 0.068 |
| Barrels | 1 |
| Available quantity | Unlimited |
| Material | PVC |
| Thickness (m) | 0.000 |
| Hydraulics |
| Manning coefficient | 0.0000 |
| Darcy-Weisbach coefficient | 0.0001 |
| Hazen-Williams coefficient | 0.0000 |
| Minimum velocity (m/s) | 1.00 |
| Maximum velocity (m/s) | 3.00 |
| Pipe class | 12.5 atm |
| Minimum pressure (m) | 10.00 |
| Maximum pressure (m) | 100.00 |
| Max. pressure increase (hammer) (%) | 20.0000 |

## D81.4 x .000125

| Shape data |
| --- |
| Type | Circular |
| Inner diameter (m) | 0.081 |
| Barrels | 1 |
| Available quantity | Unlimited |
| Material | PVC |
| Thickness (m) | 0.000 |
| Hydraulics |
| Manning coefficient | 0.0000 |
| Darcy-Weisbach coefficient | 0.0001 |
| Hazen-Williams coefficient | 0.0000 |
| Minimum velocity (m/s) | 1.00 |
| Maximum velocity (m/s) | 3.00 |
| Pipe class | 12.5 atm |
| Minimum pressure (m) | 10.00 |
| Maximum pressure (m) | 100.00 |
| Max. pressure increase (hammer) (%) | 20.0000 |

# Nodes

| Name | Axis elevation (m) | Demand (L/s) | Demand curve | Description |
| --- | --- | --- | --- | --- |
| N1 | 659.010 | 0.00 | (No Curve) |  |
| N2 | 658.786 | 0.00 | (No Curve) |  |
| N3 | 657.717 | 0.00 | (No Curve) |  |
| N4 | 645.601 | 0.25 | (No Curve) |  |
| N5 | 645.694 | 0.00 | (No Curve) |  |
| N6 | 645.650 | 0.00 | (No Curve) |  |
| N7 | 645.799 | 0.00 | (No Curve) |  |
| N8 | 645.894 | 0.00 | (No Curve) |  |
| N9 | 646.075 | 0.00 | (No Curve) |  |
| N10 | 646.053 | 0.00 | (No Curve) |  |
| N11 | 646.017 | 0.00 | (No Curve) |  |
| N12 | 646.207 | 0.00 | (No Curve) |  |
| N13 | 646.279 | 0.00 | (No Curve) |  |
| N14 | 646.478 | 0.00 | (No Curve) |  |
| N15 | 646.877 | 0.00 | (No Curve) |  |
| N16 | 647.197 | 0.00 | (No Curve) |  |
| N17 | 647.596 | 0.00 | (No Curve) |  |
| N18 | 648.022 | 0.00 | (No Curve) |  |
| N19 | 648.591 | 0.00 | (No Curve) |  |
| N20 | 649.651 | 0.00 | (No Curve) |  |
| N21 | 650.127 | 0.00 | (No Curve) |  |
| N22 | 650.907 | 0.00 | (No Curve) |  |
| N23 | 651.508 | 0.00 | (No Curve) |  |
| N24 | 652.144 | 0.00 | (No Curve) |  |
| N25 | 652.627 | 0.00 | (No Curve) |  |
| N26 | 653.408 | 0.00 | (No Curve) |  |
| N27 | 653.802 | 0.00 | (No Curve) |  |
| N28 | 654.207 | 0.00 | (No Curve) |  |
| N29 | 655.306 | 0.00 | (No Curve) |  |
| N30 | 656.207 | 0.00 | (No Curve) |  |
| N31 | 656.683 | 0.00 | (No Curve) |  |
| N32 | 657.212 | 0.00 | (No Curve) |  |
| N33 | 657.779 | 0.00 | (No Curve) |  |
| N34 | 658.856 | 0.00 | (No Curve) |  |
| N35 | 659.289 | 0.00 | (No Curve) |  |
| N36 | 659.870 | 0.00 | (No Curve) |  |
| N37 | 660.385 | 0.00 | (No Curve) |  |
| N38 | 661.091 | 0.00 | (No Curve) |  |
| N39 | 661.550 | 0.00 | (No Curve) |  |
| N40 | 662.160 | 0.00 | (No Curve) |  |
| N41 | 662.887 | 0.00 | (No Curve) |  |
| N42 | 663.861 | 0.00 | (No Curve) |  |
| N43 | 665.196 | 0.00 | (No Curve) |  |
| N44 | 665.864 | 0.00 | (No Curve) |  |
| N45 | 666.363 | 0.00 | (No Curve) |  |
| N46 | 667.335 | 0.00 | (No Curve) |  |
| N47 | 667.939 | 0.00 | (No Curve) |  |
| N48 | 669.234 | 0.00 | (No Curve) |  |
| N49 | 670.128 | 0.00 | (No Curve) |  |
| N50 | 671.018 | 0.00 | (No Curve) |  |
| N51 | 672.023 | 0.00 | (No Curve) |  |
| N52 | 673.113 | 0.00 | (No Curve) |  |
| N53 | 674.730 | 0.00 | (No Curve) |  |
| N54 | 676.124 | 0.10 | (No Curve) |  |
| N55 | 676.972 | 0.00 | (No Curve) |  |
| N56 | 677.748 | 0.00 | (No Curve) |  |
| N57 | 678.723 | 0.00 | (No Curve) |  |
| N58 | 679.690 | 0.10 | (No Curve) |  |
| N59 | 680.858 | 0.00 | (No Curve) |  |
| N60 | 681.957 | 0.00 | (No Curve) |  |
| N61 | 683.486 | 0.00 | (No Curve) |  |
| N62 | 684.021 | 0.00 | (No Curve) |  |
| N63 | 684.608 | 0.00 | (No Curve) |  |
| N64 | 685.627 | 0.00 | (No Curve) |  |
| N65 | 686.730 | 0.10 | (No Curve) |  |
| N66 | 687.782 | 0.00 | (No Curve) |  |
| N67 | 689.002 | 0.00 | (No Curve) |  |
| N68 | 689.698 | 0.00 | (No Curve) |  |
| N69 | 690.937 | 0.00 | (No Curve) |  |
| N70 | 691.845 | 0.00 | (No Curve) |  |
| N71 | 693.392 | 0.00 | (No Curve) |  |
| N72 | 694.630 | 0.00 | (No Curve) |  |
| N73 | 695.932 | 0.00 | (No Curve) |  |
| N74 | 696.742 | 0.10 | (No Curve) |  |
| N75 | 696.433 | 0.00 | (No Curve) |  |
| N76 | 697.956 | 0.00 | (No Curve) |  |
| N77 | 698.476 | 0.00 | (No Curve) |  |
| N78 | 699.659 | 0.00 | (No Curve) |  |
| N79 | 699.216 | 0.10 | (No Curve) |  |
| N80 | 700.571 | 0.00 | (No Curve) |  |
| N81 | 702.197 | 0.00 | (No Curve) |  |
| N82 | 704.256 | 0.00 | (No Curve) |  |
| N83 | 705.956 | 0.00 | (No Curve) |  |
| N84 | 707.819 | 0.00 | (No Curve) |  |
| N85 | 709.329 | 0.00 | (No Curve) |  |
| N86 | 710.413 | 0.00 | (No Curve) |  |
| N87 | 713.002 | 0.00 | (No Curve) |  |
| N88 | 715.449 | 0.00 | (No Curve) |  |
| N89 | 717.747 | 0.00 | (No Curve) |  |
| N91 | 645.196 | 0.00 | (No Curve) |  |
| N92 | 645.166 | 0.00 | (No Curve) |  |
| N93 | 645.555 | 0.00 | (No Curve) |  |
| N94 | 645.475 | 0.00 | (No Curve) |  |
| N95 | 645.417 | 0.00 | (No Curve) |  |
| N96 | 645.360 | 0.00 | (No Curve) |  |
| N97 | 645.529 | 0.00 | (No Curve) |  |
| N98 | 645.619 | 0.00 | (No Curve) |  |
| N99 | 645.704 | 0.25 | (No Curve) |  |
| N100 | 645.917 | 0.00 | (No Curve) |  |
| N101 | 645.686 | 0.00 | (No Curve) |  |
| N102 | 645.849 | 0.00 | (No Curve) |  |
| N103 | 646.129 | 0.00 | (No Curve) |  |
| N104 | 646.594 | 0.00 | (No Curve) |  |
| N105 | 646.861 | 0.00 | (No Curve) |  |
| N106 | 647.297 | 0.00 | (No Curve) |  |
| N107 | 647.718 | 0.00 | (No Curve) |  |
| N108 | 648.223 | 0.00 | (No Curve) |  |
| N109 | 645.406 | 0.00 | (No Curve) |  |
| N110 | 645.377 | 0.00 | (No Curve) |  |
| N111 | 645.349 | 0.00 | (No Curve) |  |
| N112 | 645.428 | 0.00 | (No Curve) |  |
| N113 | 645.370 | 0.00 | (No Curve) |  |
| N114 | 645.513 | 0.00 | (No Curve) |  |
| N115 | 645.400 | 0.00 | (No Curve) |  |
| N116 | 645.399 | 0.00 | (No Curve) |  |
| N117 | 645.708 | 0.00 | (No Curve) |  |
| N118 | 646.064 | 0.00 | (No Curve) |  |
| N119 | 646.201 | 0.00 | (No Curve) |  |
| N120 | 646.364 | 0.00 | (No Curve) |  |
| N121 | 646.499 | 0.00 | (No Curve) |  |
| N122 | 646.753 | 0.00 | (No Curve) |  |
| N123 | 646.925 | 0.00 | (No Curve) |  |
| N124 | 647.361 | 0.00 | (No Curve) |  |
| N125 | 647.602 | 0.00 | (No Curve) |  |
| N126 | 647.699 | 0.00 | (No Curve) |  |
| N127 | 648.072 | 0.00 | (No Curve) |  |
| N128 | 648.370 | 0.00 | (No Curve) |  |
| N129 | 648.586 | 0.00 | (No Curve) |  |
| N130 | 648.703 | 0.00 | (No Curve) |  |
| N131 | 648.661 | 0.00 | (No Curve) |  |
| N132 | 648.587 | 0.00 | (No Curve) |  |
| N133 | 648.400 | 0.00 | (No Curve) |  |
| N134 | 648.071 | 0.00 | (No Curve) |  |
| N135 | 647.100 | 0.00 | (No Curve) |  |
| N136 | 646.761 | 0.00 | (No Curve) |  |
| N137 | 646.614 | 0.00 | (No Curve) |  |
| N138 | 646.614 | 0.00 | (No Curve) |  |
| N139 | 646.384 | 0.00 | (No Curve) |  |
| N140 | 646.358 | 0.00 | (No Curve) |  |
| N141 | 646.616 | 0.00 | (No Curve) |  |
| N142 | 646.820 | 0.00 | (No Curve) |  |
| N143 | 647.700 | 0.00 | (No Curve) |  |
| N144 | 648.221 | 0.00 | (No Curve) |  |
| N145 | 649.005 | 0.00 | (No Curve) |  |
| N146 | 649.842 | 0.00 | (No Curve) |  |
| N147 | 650.853 | 0.00 | (No Curve) |  |
| N148 | 651.272 | 0.00 | (No Curve) |  |
| N149 | 652.453 | 0.00 | (No Curve) |  |
| N150 | 653.203 | 0.00 | (No Curve) |  |
| N151 | 653.309 | 0.00 | (No Curve) |  |
| N152 | 653.487 | 0.00 | (No Curve) |  |
| N153 | 653.897 | 0.00 | (No Curve) |  |
| N154 | 654.278 | 0.25 | (No Curve) |  |
| N155 | 653.397 | 0.00 | (No Curve) |  |
| N156 | 653.514 | 0.00 | (No Curve) |  |
| N157 | 653.511 | 0.00 | (No Curve) |  |
| N158 | 653.458 | 0.00 | (No Curve) |  |
| N159 | 654.112 | 0.00 | (No Curve) |  |
| N160 | 654.390 | 0.00 | (No Curve) |  |
| N161 | 657.312 | 0.00 | (No Curve) |  |
| N162 | 656.180 | 0.00 | (No Curve) |  |
| N163 | 655.220 | 0.00 | (No Curve) |  |
| N164 | 654.306 | 0.00 | (No Curve) |  |
| N165 | 654.480 | 0.00 | (No Curve) |  |
| N166 | 654.419 | 0.00 | (No Curve) |  |
| N167 | 654.388 | 0.00 | (No Curve) |  |
| N168 | 654.299 | 0.00 | (No Curve) |  |
| N169 | 653.792 | 0.00 | (No Curve) |  |
| N170 | 654.154 | 0.00 | (No Curve) |  |
| N171 | 654.094 | 0.00 | (No Curve) |  |
| N172 | 653.774 | 0.00 | (No Curve) |  |
| N173 | 654.041 | 0.00 | (No Curve) |  |
| N174 | 654.468 | 0.00 | (No Curve) |  |
| N175 | 654.918 | 0.00 | (No Curve) |  |
| N176 | 655.072 | 0.00 | (No Curve) |  |
| N177 | 655.519 | 0.00 | (No Curve) |  |
| N178 | 656.206 | 0.00 | (No Curve) |  |
| N179 | 656.378 | 0.00 | (No Curve) |  |
| N180 | 657.196 | 0.00 | (No Curve) |  |
| N181 | 657.431 | 0.00 | (No Curve) |  |
| N182 | 658.244 | 0.00 | (No Curve) |  |
| N183 | 658.658 | 0.00 | (No Curve) |  |
| N184 | 658.386 | 0.00 | (No Curve) |  |
| N185 | 658.585 | 0.00 | (No Curve) |  |
| N186 | 658.626 | 0.00 | (No Curve) |  |
| N187 | 658.777 | 0.00 | (No Curve) |  |
| N188 | 659.015 | 0.00 | (No Curve) |  |
| N189 | 659.544 | 0.00 | (No Curve) |  |
| N190 | 659.446 | 0.00 | (No Curve) |  |
| N191 | 659.094 | 0.00 | (No Curve) |  |
| N192 | 666.244 | 0.00 | (No Curve) |  |
| N193 | 666.327 | 0.00 | (No Curve) |  |
| N194 | 667.524 | 0.00 | (No Curve) |  |
| N195 | 668.585 | 0.00 | (No Curve) |  |
| N196 | 669.987 | 0.00 | (No Curve) |  |
| N197 | 671.174 | 0.00 | (No Curve) |  |
| N198 | 671.411 | 0.00 | (No Curve) |  |
| N199 | 671.583 | 0.00 | (No Curve) |  |
| N200 | 671.838 | 0.00 | (No Curve) |  |
| N201 | 672.084 | 0.00 | (No Curve) |  |
| N202 | 671.984 | 0.00 | (No Curve) |  |
| N203 | 669.952 | 0.00 | (No Curve) |  |
| N204 | 670.197 | 0.00 | (No Curve) |  |
| N205 | 670.417 | 0.00 | (No Curve) |  |
| N206 | 670.085 | 0.00 | (No Curve) |  |
| N207 | 666.517 | 0.00 | (No Curve) |  |
| N208 | 667.156 | 0.00 | (No Curve) |  |
| N209 | 673.050 | 0.25 | (No Curve) |  |
| N210 | 671.810 | 0.00 | (No Curve) |  |
| N211 | 671.631 | 0.00 | (No Curve) |  |
| N212 | 654.758 | 0.00 | (No Curve) |  |
| N213 | 655.001 | 0.00 | (No Curve) |  |
| N214 | 655.537 | 0.00 | (No Curve) |  |
| N215 | 656.897 | 0.00 | (No Curve) |  |
| N216 | 657.890 | 0.00 | (No Curve) |  |
| N217 | 658.450 | 0.00 | (No Curve) |  |
| N218 | 656.861 | 0.00 | (No Curve) |  |
| N219 | 657.361 | 0.00 | (No Curve) |  |
| N220 | 657.666 | 0.00 | (No Curve) |  |
| N221 | 659.818 | 0.10 | (No Curve) |  |
| N222 | 659.181 | 0.00 | (No Curve) |  |
| N223 | 658.583 | 0.00 | (No Curve) |  |
| N224 | 661.677 | 0.00 | (No Curve) |  |
| N225 | 662.156 | 0.00 | (No Curve) |  |
| N226 | 662.807 | 0.00 | (No Curve) |  |
| N227 | 664.130 | 0.25 | (No Curve) |  |
| N228 | 664.325 | 0.00 | (No Curve) |  |
| N229 | 664.973 | 0.00 | (No Curve) |  |
| N230 | 665.595 | 0.10 | (No Curve) |  |
| N231 | 665.980 | 0.00 | (No Curve) |  |
| N232 | 666.169 | 0.00 | (No Curve) |  |
| N233 | 666.868 | 0.00 | (No Curve) |  |
| N234 | 667.658 | 0.25 | (No Curve) |  |
| N235 | 669.072 | 0.00 | (No Curve) |  |
| N236 | 670.939 | 0.00 | (No Curve) |  |
| N237 | 672.465 | 0.00 | (No Curve) |  |
| N238 | 675.000 | 0.00 | (No Curve) |  |
| N239 | 676.887 | 0.00 | (No Curve) |  |
| N240 | 679.680 | 0.25 | (No Curve) |  |
| N241 | 664.181 | 0.00 | (No Curve) |  |
| N242 | 664.947 | 0.00 | (No Curve) |  |
| N243 | 664.725 | 0.00 | (No Curve) |  |
| N244 | 664.336 | 0.00 | (No Curve) |  |
| N245 | 663.164 | 0.25 | (No Curve) |  |
| N246 | 661.712 | 0.00 | (No Curve) |  |
| N247 | 661.116 | 0.00 | (No Curve) |  |
| N248 | 661.026 | 0.00 | (No Curve) |  |
| N249 | 660.856 | 0.00 | (No Curve) |  |
| N250 | 667.136 | 0.00 | (No Curve) |  |
| N251 | 669.691 | 0.25 | (No Curve) |  |
| N252 | 667.073 | 0.00 | (No Curve) |  |
| N253 | 668.475 | 0.00 | (No Curve) |  |
| N254 | 668.082 | 0.00 | (No Curve) |  |
| N255 | 668.793 | 0.00 | (No Curve) |  |
| N256 | 670.221 | 0.00 | (No Curve) |  |
| N257 | 672.837 | 0.25 | (No Curve) |  |
| N258 | 669.039 | 0.00 | (No Curve) |  |
| N259 | 669.386 | 0.00 | (No Curve) |  |
| N260 | 669.805 | 0.00 | (No Curve) |  |
| N261 | 670.466 | 0.00 | (No Curve) |  |
| N262 | 673.018 | 0.00 | (No Curve) |  |
| N263 | 674.825 | 0.00 | (No Curve) |  |
| N264 | 677.701 | 0.25 | (No Curve) |  |
| N265 | 671.454 | 0.00 | (No Curve) |  |
| N266 | 672.928 | 0.00 | (No Curve) |  |
| N267 | 674.840 | 0.00 | (No Curve) |  |
| N268 | 676.499 | 0.00 | (No Curve) |  |
| N269 | 680.004 | 0.25 | (No Curve) |  |
| N270 | 653.881 | 0.00 | (No Curve) |  |
| N271 | 653.618 | 0.00 | (No Curve) |  |
| N272 | 653.332 | 0.00 | (No Curve) |  |
| N273 | 653.063 | 0.00 | (No Curve) |  |
| N274 | 652.555 | 0.00 | (No Curve) |  |
| N275 | 652.063 | 0.00 | (No Curve) |  |
| N276 | 651.648 | 0.00 | (No Curve) |  |
| N277 | 651.678 | 0.00 | (No Curve) |  |
| N278 | 651.608 | 0.15 | (No Curve) |  |
| N279 | 651.500 | 0.00 | (No Curve) |  |
| N280 | 651.667 | 0.00 | (No Curve) |  |
| N281 | 651.913 | 0.00 | (No Curve) |  |
| N282 | 652.274 | 0.00 | (No Curve) |  |
| N283 | 652.429 | 0.00 | (No Curve) |  |
| N284 | 652.482 | 0.00 | (No Curve) |  |
| N285 | 653.317 | 0.00 | (No Curve) |  |
| N286 | 654.434 | 0.00 | (No Curve) |  |
| N287 | 654.643 | 0.00 | (No Curve) |  |
| N288 | 656.439 | 0.00 | (No Curve) |  |
| N289 | 657.680 | 0.00 | (No Curve) |  |
| N290 | 659.080 | 0.00 | (No Curve) |  |
| N291 | 659.756 | 0.00 | (No Curve) |  |
| N292 | 661.567 | 0.20 | (No Curve) |  |
| N293 | 651.608 | 0.00 | (No Curve) |  |
| N294 | 652.144 | 0.00 | (No Curve) |  |
| N295 | 652.840 | 0.00 | (No Curve) |  |
| N296 | 653.595 | 0.00 | (No Curve) |  |
| N297 | 654.371 | 0.00 | (No Curve) |  |
| N298 | 655.564 | 0.00 | (No Curve) |  |
| N299 | 657.367 | 0.00 | (No Curve) |  |
| N300 | 658.037 | 0.00 | (No Curve) |  |
| N301 | 658.398 | 0.00 | (No Curve) |  |
| N302 | 658.263 | 0.00 | (No Curve) |  |
| N303 | 657.733 | 0.00 | (No Curve) |  |
| N304 | 657.601 | 0.00 | (No Curve) |  |
| N305 | 658.079 | 0.15 | (No Curve) |  |

# Reservoirs

| Name | Level (m) | Flow rate - headloss curve | Description |
| --- | --- | --- | --- |
| N90 | 724.500 | (No Curve) |  |

# Pipes

| Name | Start node | End node | Length (m) | Pipe specification | Initial status |
| --- | --- | --- | --- | --- | --- |
| P1 | N1 | N2 | 9.760 | D67.8 x .000125 | Open |
| P2 | N2 | N3 | 13.959 | D67.8 x .000125 | Open |
| P3 | N4 | N5 | 13.501 | D81.4 x .000125 | Open |
| P4 | N5 | N6 | 16.832 | D81.4 x .000125 | Open |
| P5 | N6 | N7 | 15.372 | D81.4 x .000125 | Open |
| P6 | N7 | N8 | 24.460 | D81.4 x .000125 | Open |
| P7 | N8 | N9 | 18.760 | D81.4 x .000125 | Open |
| P8 | N9 | N10 | 19.956 | D81.4 x .000125 | Open |
| P9 | N10 | N11 | 24.782 | D81.4 x .000125 | Open |
| P10 | N11 | N12 | 22.390 | D81.4 x .000125 | Open |
| P11 | N12 | N13 | 18.871 | D81.4 x .000125 | Open |
| P12 | N13 | N14 | 23.704 | D81.4 x .000125 | Open |
| P13 | N14 | N15 | 29.684 | D81.4 x .000125 | Open |
| P14 | N15 | N16 | 27.788 | D81.4 x .000125 | Open |
| P15 | N16 | N17 | 20.228 | D81.4 x .000125 | Open |
| P16 | N17 | N18 | 25.082 | D81.4 x .000125 | Open |
| P17 | N18 | N19 | 24.181 | D81.4 x .000125 | Open |
| P18 | N19 | N20 | 29.636 | D81.4 x .000125 | Open |
| P19 | N20 | N21 | 17.968 | D81.4 x .000125 | Open |
| P20 | N21 | N22 | 24.024 | D81.4 x .000125 | Open |
| P21 | N22 | N23 | 15.141 | D81.4 x .000125 | Open |
| P22 | N23 | N24 | 19.269 | D81.4 x .000125 | Open |
| P23 | N24 | N25 | 17.762 | D81.4 x .000125 | Open |
| P24 | N25 | N26 | 13.434 | D81.4 x .000125 | Open |
| P25 | N26 | N27 | 14.567 | D81.4 x .000125 | Open |
| P26 | N27 | N28 | 18.801 | D81.4 x .000125 | Open |
| P27 | N28 | N29 | 16.717 | D81.4 x .000125 | Open |
| P28 | N29 | N30 | 24.007 | D81.4 x .000125 | Open |
| P29 | N30 | N31 | 13.728 | D81.4 x .000125 | Open |
| P30 | N31 | N32 | 14.727 | D81.4 x .000125 | Open |
| P31 | N32 | N33 | 14.907 | D81.4 x .000125 | Open |
| P32 | N33 | N34 | 15.016 | D81.4 x .000125 | Open |
| P33 | N34 | N35 | 20.128 | D81.4 x .000125 | Open |
| P34 | N35 | N36 | 19.609 | D81.4 x .000125 | Open |
| P35 | N36 | N37 | 18.416 | D81.4 x .000125 | Open |
| P36 | N37 | N38 | 20.028 | D81.4 x .000125 | Open |
| P37 | N38 | N39 | 14.659 | D81.4 x .000125 | Open |
| P38 | N39 | N40 | 20.941 | D81.4 x .000125 | Open |
| P39 | N40 | N41 | 18.606 | D81.4 x .000125 | Open |
| P40 | N41 | N42 | 20.074 | D81.4 x .000125 | Open |
| P41 | N42 | N43 | 21.234 | D81.4 x .000125 | Open |
| P42 | N43 | N44 | 13.753 | D81.4 x .000125 | Open |
| P43 | N44 | N45 | 11.976 | D81.4 x .000125 | Open |
| P44 | N45 | N46 | 19.949 | D81.4 x .000125 | Open |
| P45 | N46 | N47 | 24.438 | D81.4 x .000125 | Open |
| P46 | N47 | N48 | 17.756 | D81.4 x .000125 | Open |
| P47 | N48 | N49 | 17.329 | D81.4 x .000125 | Open |
| P48 | N49 | N50 | 17.934 | D81.4 x .000125 | Open |
| P49 | N50 | N51 | 18.516 | D81.4 x .000125 | Open |
| P50 | N51 | N52 | 18.348 | D81.4 x .000125 | Open |
| P51 | N52 | N53 | 17.633 | D81.4 x .000125 | Open |
| P52 | N53 | N54 | 19.259 | D81.4 x .000125 | Open |
| P53 | N54 | N55 | 15.093 | D81.4 x .000125 | Open |
| P54 | N55 | N56 | 12.767 | D81.4 x .000125 | Open |
| P55 | N56 | N57 | 14.425 | D81.4 x .000125 | Open |
| P56 | N57 | N58 | 16.662 | D81.4 x .000125 | Open |
| P57 | N58 | N59 | 16.976 | D81.4 x .000125 | Open |
| P58 | N59 | N60 | 15.932 | D81.4 x .000125 | Open |
| P59 | N60 | N61 | 16.386 | D81.4 x .000125 | Open |
| P60 | N61 | N62 | 11.568 | D81.4 x .000125 | Open |
| P61 | N62 | N63 | 17.446 | D81.4 x .000125 | Open |
| P62 | N63 | N64 | 17.486 | D81.4 x .000125 | Open |
| P63 | N64 | N65 | 17.566 | D81.4 x .000125 | Open |
| P64 | N65 | N66 | 19.246 | D81.4 x .000125 | Open |
| P65 | N66 | N67 | 16.968 | D81.4 x .000125 | Open |
| P66 | N67 | N68 | 18.178 | D81.4 x .000125 | Open |
| P67 | N68 | N69 | 18.205 | D81.4 x .000125 | Open |
| P68 | N69 | N70 | 18.990 | D81.4 x .000125 | Open |
| P69 | N70 | N71 | 21.167 | D81.4 x .000125 | Open |
| P70 | N71 | N72 | 17.958 | D81.4 x .000125 | Open |
| P71 | N72 | N73 | 20.936 | D81.4 x .000125 | Open |
| P72 | N73 | N74 | 19.821 | D81.4 x .000125 | Open |
| P73 | N74 | N75 | 18.849 | D81.4 x .000125 | Open |
| P74 | N75 | N76 | 18.961 | D81.4 x .000125 | Open |
| P75 | N76 | N77 | 19.302 | D81.4 x .000125 | Open |
| P76 | N77 | N78 | 14.651 | D81.4 x .000125 | Open |
| P77 | N78 | N79 | 14.021 | D81.4 x .000125 | Open |
| P78 | N79 | N80 | 15.522 | D81.4 x .000125 | Open |
| P79 | N80 | N81 | 12.151 | D81.4 x .000125 | Open |
| P80 | N81 | N82 | 15.129 | D81.4 x .000125 | Open |
| P81 | N82 | N83 | 12.970 | D81.4 x .000125 | Open |
| P82 | N83 | N84 | 13.647 | D81.4 x .000125 | Open |
| P83 | N84 | N85 | 11.416 | D81.4 x .000125 | Open |
| P84 | N85 | N86 | 9.284 | D81.4 x .000125 | Open |
| P85 | N86 | N87 | 16.469 | D81.4 x .000125 | Open |
| P86 | N87 | N88 | 15.198 | D81.4 x .000125 | Open |
| P87 | N88 | N89 | 15.175 | D81.4 x .000125 | Open |
| P88 | N89 | N90 | 15.337 | D81.4 x .000125 | Open |
| P89 | N5 | N91 | 18.800 | D67.8 x .000125 | Open |
| P90 | N91 | N92 | 20.878 | D67.8 x .000125 | Open |
| P91 | N92 | N93 | 20.073 | D67.8 x .000125 | Open |
| P92 | N93 | N94 | 23.238 | D67.8 x .000125 | Open |
| P93 | N94 | N95 | 17.248 | D67.8 x .000125 | Open |
| P94 | N95 | N96 | 19.608 | D67.8 x .000125 | Open |
| P95 | N96 | N97 | 18.084 | D67.8 x .000125 | Open |
| P96 | N97 | N98 | 19.096 | D67.8 x .000125 | Open |
| P97 | N98 | N99 | 15.048 | D67.8 x .000125 | Open |
| P98 | N99 | N100 | 28.650 | D67.8 x .000125 | Open |
| P99 | N100 | N101 | 19.968 | D67.8 x .000125 | Open |
| P100 | N101 | N102 | 25.913 | D67.8 x .000125 | Open |
| P101 | N102 | N103 | 21.010 | D67.8 x .000125 | Open |
| P102 | N103 | N104 | 26.246 | D67.8 x .000125 | Open |
| P103 | N104 | N105 | 31.833 | D67.8 x .000125 | Open |
| P104 | N105 | N106 | 25.802 | D67.8 x .000125 | Open |
| P105 | N106 | N107 | 22.688 | D67.8 x .000125 | Open |
| P106 | N107 | N108 | 22.007 | D67.8 x .000125 | Open |
| P107 | N108 | N19 | 28.321 | D67.8 x .000125 | Open |
| P108 | N6 | N109 | 17.999 | D67.8 x .000125 | Open |
| P109 | N109 | N110 | 13.231 | D67.8 x .000125 | Open |
| P110 | N110 | N111 | 17.933 | D67.8 x .000125 | Open |
| P111 | N111 | N112 | 20.080 | D67.8 x .000125 | Open |
| P112 | N112 | N113 | 17.779 | D67.8 x .000125 | Open |
| P113 | N113 | N114 | 12.184 | D67.8 x .000125 | Open |
| P114 | N114 | N115 | 17.094 | D67.8 x .000125 | Open |
| P115 | N115 | N116 | 15.601 | D67.8 x .000125 | Open |
| P116 | N116 | N117 | 17.695 | D67.8 x .000125 | Open |
| P117 | N117 | N118 | 15.913 | D67.8 x .000125 | Open |
| P118 | N118 | N119 | 14.835 | D67.8 x .000125 | Open |
| P119 | N119 | N120 | 12.141 | D67.8 x .000125 | Open |
| P120 | N120 | N121 | 11.563 | D67.8 x .000125 | Open |
| P121 | N121 | N122 | 11.512 | D67.8 x .000125 | Open |
| P122 | N122 | N123 | 11.133 | D67.8 x .000125 | Open |
| P123 | N123 | N124 | 17.040 | D67.8 x .000125 | Open |
| P124 | N124 | N125 | 17.801 | D67.8 x .000125 | Open |
| P125 | N125 | N126 | 9.543 | D67.8 x .000125 | Open |
| P126 | N126 | N127 | 13.803 | D67.8 x .000125 | Open |
| P127 | N127 | N128 | 13.716 | D67.8 x .000125 | Open |
| P128 | N128 | N129 | 11.690 | D67.8 x .000125 | Open |
| P129 | N129 | N130 | 13.125 | D67.8 x .000125 | Open |
| P130 | N130 | N131 | 14.418 | D67.8 x .000125 | Open |
| P131 | N131 | N132 | 13.550 | D67.8 x .000125 | Open |
| P132 | N132 | N133 | 15.477 | D67.8 x .000125 | Open |
| P133 | N133 | N134 | 18.066 | D67.8 x .000125 | Open |
| P134 | N134 | N18 | 16.748 | D67.8 x .000125 | Open |
| P135 | N124 | N135 | 14.035 | D67.8 x .000125 | Open |
| P136 | N135 | N136 | 12.599 | D67.8 x .000125 | Open |
| P137 | N136 | N137 | 14.082 | D67.8 x .000125 | Open |
| P138 | N137 | N138 | 13.511 | D67.8 x .000125 | Open |
| P139 | N138 | N139 | 13.873 | D67.8 x .000125 | Open |
| P140 | N139 | N140 | 9.924 | D67.8 x .000125 | Open |
| P141 | N140 | N141 | 16.730 | D67.8 x .000125 | Open |
| P142 | N141 | N142 | 18.373 | D67.8 x .000125 | Open |
| P143 | N142 | N143 | 14.723 | D67.8 x .000125 | Open |
| P144 | N143 | N144 | 17.187 | D67.8 x .000125 | Open |
| P145 | N144 | N145 | 14.938 | D67.8 x .000125 | Open |
| P146 | N145 | N146 | 14.274 | D67.8 x .000125 | Open |
| P147 | N146 | N147 | 12.341 | D67.8 x .000125 | Open |
| P148 | N147 | N148 | 13.396 | D67.8 x .000125 | Open |
| P149 | N148 | N149 | 13.254 | D67.8 x .000125 | Open |
| P150 | N149 | N150 | 10.280 | D67.8 x .000125 | Open |
| P151 | N150 | N151 | 12.001 | D67.8 x .000125 | Open |
| P152 | N151 | N152 | 14.082 | D67.8 x .000125 | Open |
| P153 | N152 | N153 | 11.308 | D67.8 x .000125 | Open |
| P154 | N153 | N154 | 12.958 | D67.8 x .000125 | Open |
| P155 | N26 | N155 | 10.932 | D67.8 x .000125 | Open |
| P156 | N155 | N156 | 17.945 | D67.8 x .000125 | Open |
| P157 | N156 | N157 | 16.004 | D67.8 x .000125 | Open |
| P158 | N157 | N158 | 15.736 | D67.8 x .000125 | Open |
| P159 | N158 | N159 | 16.218 | D67.8 x .000125 | Open |
| P160 | N159 | N160 | 14.814 | D67.8 x .000125 | Open |
| P161 | N160 | N161 | 16.840 | D67.8 x .000125 | Open |
| P162 | N161 | N162 | 19.244 | D67.8 x .000125 | Open |
| P163 | N162 | N163 | 18.150 | D67.8 x .000125 | Open |
| P164 | N163 | N164 | 24.691 | D67.8 x .000125 | Open |
| P165 | N164 | N165 | 22.491 | D67.8 x .000125 | Open |
| P166 | N165 | N166 | 16.172 | D67.8 x .000125 | Open |
| P167 | N166 | N167 | 16.607 | D67.8 x .000125 | Open |
| P168 | N167 | N168 | 19.233 | D67.8 x .000125 | Open |
| P169 | N168 | N169 | 17.499 | D67.8 x .000125 | Open |
| P170 | N169 | N170 | 16.041 | D67.8 x .000125 | Open |
| P171 | N170 | N171 | 14.909 | D67.8 x .000125 | Open |
| P172 | N171 | N172 | 17.390 | D67.8 x .000125 | Open |
| P173 | N172 | N173 | 16.577 | D67.8 x .000125 | Open |
| P174 | N173 | N174 | 19.748 | D67.8 x .000125 | Open |
| P175 | N174 | N175 | 20.458 | D81.4 x .000125 | Open |
| P176 | N175 | N176 | 18.078 | D81.4 x .000125 | Open |
| P177 | N176 | N177 | 18.620 | D81.4 x .000125 | Open |
| P178 | N177 | N178 | 16.121 | D81.4 x .000125 | Open |
| P179 | N178 | N179 | 16.981 | D81.4 x .000125 | Open |
| P180 | N179 | N180 | 18.499 | D81.4 x .000125 | Open |
| P181 | N180 | N181 | 20.593 | D81.4 x .000125 | Open |
| P182 | N181 | N182 | 17.740 | D81.4 x .000125 | Open |
| P183 | N182 | N183 | 18.149 | D81.4 x .000125 | Open |
| P184 | N183 | N184 | 21.720 | D81.4 x .000125 | Open |
| P185 | N184 | N185 | 16.425 | D81.4 x .000125 | Open |
| P186 | N185 | N186 | 16.030 | D81.4 x .000125 | Open |
| P187 | N186 | N187 | 20.369 | D81.4 x .000125 | Open |
| P188 | N187 | N188 | 17.029 | D81.4 x .000125 | Open |
| P189 | N188 | N189 | 23.548 | D81.4 x .000125 | Open |
| P190 | N189 | N190 | 22.193 | D81.4 x .000125 | Open |
| P191 | N190 | N191 | 16.751 | D81.4 x .000125 | Open |
| P192 | N191 | N35 | 18.456 | D81.4 x .000125 | Open |
| P193 | N44 | N192 | 14.538 | D67.8 x .000125 | Open |
| P194 | N192 | N193 | 18.921 | D67.8 x .000125 | Open |
| P195 | N193 | N194 | 24.265 | D67.8 x .000125 | Open |
| P196 | N194 | N195 | 21.483 | D67.8 x .000125 | Open |
| P197 | N195 | N196 | 24.815 | D67.8 x .000125 | Open |
| P198 | N196 | N197 | 23.020 | D67.8 x .000125 | Open |
| P199 | N197 | N198 | 14.097 | D67.8 x .000125 | Open |
| P200 | N198 | N199 | 10.437 | D67.8 x .000125 | Open |
| P201 | N199 | N200 | 15.115 | D67.8 x .000125 | Open |
| P202 | N200 | N201 | 12.505 | D67.8 x .000125 | Open |
| P203 | N201 | N202 | 12.098 | D67.8 x .000125 | Open |
| P204 | N202 | N51 | 11.689 | D67.8 x .000125 | Open |
| P205 | N196 | N203 | 11.279 | D67.8 x .000125 | Open |
| P206 | N203 | N204 | 13.090 | D67.8 x .000125 | Open |
| P207 | N204 | N205 | 14.475 | D67.8 x .000125 | Open |
| P208 | N205 | N206 | 13.461 | D67.8 x .000125 | Open |
| P209 | N206 | N49 | 9.178 | D67.8 x .000125 | Open |
| P210 | N193 | N207 | 11.269 | D67.8 x .000125 | Open |
| P211 | N207 | N208 | 11.387 | D67.8 x .000125 | Open |
| P212 | N208 | N46 | 13.108 | D67.8 x .000125 | Open |
| P213 | N209 | N210 | 30.583 | D67.8 x .000125 | Open |
| P214 | N210 | N211 | 22.733 | D67.8 x .000125 | Open |
| P215 | N211 | N197 | 18.382 | D67.8 x .000125 | Open |
| P216 | N29 | N212 | 14.964 | D67.8 x .000125 | Open |
| P217 | N212 | N213 | 10.402 | D67.8 x .000125 | Open |
| P218 | N213 | N214 | 14.982 | D67.8 x .000125 | Open |
| P219 | N214 | N215 | 11.268 | D67.8 x .000125 | Open |
| P220 | N215 | N216 | 8.041 | D67.8 x .000125 | Open |
| P221 | N216 | N217 | 9.161 | D67.8 x .000125 | Open |
| P222 | N217 | N1 | 11.391 | D67.8 x .000125 | Open |
| P223 | N3 | N218 | 10.197 | D67.8 x .000125 | Open |
| P224 | N218 | N219 | 8.970 | D67.8 x .000125 | Open |
| P225 | N219 | N220 | 10.423 | D67.8 x .000125 | Open |
| P226 | N220 | N33 | 10.265 | D67.8 x .000125 | Open |
| P227 | N221 | N222 | 17.082 | D67.8 x .000125 | Open |
| P228 | N222 | N223 | 17.585 | D67.8 x .000125 | Open |
| P229 | N223 | N35 | 18.446 | D67.8 x .000125 | Open |
| P230 | N38 | N224 | 23.062 | D67.8 x .000125 | Open |
| P231 | N224 | N225 | 16.211 | D67.8 x .000125 | Open |
| P232 | N225 | N226 | 15.655 | D67.8 x .000125 | Open |
| P233 | N226 | N227 | 19.298 | D67.8 x .000125 | Open |
| P234 | N227 | N228 | 16.977 | D67.8 x .000125 | Open |
| P235 | N228 | N229 | 14.527 | D67.8 x .000125 | Open |
| P236 | N229 | N230 | 14.900 | D67.8 x .000125 | Open |
| P237 | N230 | N231 | 11.561 | D67.8 x .000125 | Open |
| P238 | N231 | N45 | 13.874 | D67.8 x .000125 | Open |
| P239 | N230 | N232 | 16.379 | D67.8 x .000125 | Open |
| P240 | N232 | N233 | 17.710 | D67.8 x .000125 | Open |
| P241 | N233 | N234 | 16.421 | D67.8 x .000125 | Open |
| P242 | N234 | N235 | 16.979 | D67.8 x .000125 | Open |
| P243 | N235 | N236 | 16.476 | D67.8 x .000125 | Open |
| P244 | N236 | N237 | 13.388 | D67.8 x .000125 | Open |
| P245 | N237 | N238 | 14.328 | D67.8 x .000125 | Open |
| P246 | N238 | N239 | 16.233 | D67.8 x .000125 | Open |
| P247 | N239 | N240 | 15.874 | D67.8 x .000125 | Open |
| P248 | N227 | N241 | 15.639 | D67.8 x .000125 | Open |
| P249 | N241 | N242 | 14.898 | D67.8 x .000125 | Open |
| P250 | N242 | N243 | 17.515 | D67.8 x .000125 | Open |
| P251 | N243 | N244 | 16.714 | D67.8 x .000125 | Open |
| P252 | N244 | N245 | 22.775 | D67.8 x .000125 | Open |
| P253 | N245 | N246 | 22.163 | D67.8 x .000125 | Open |
| P254 | N246 | N247 | 16.191 | D67.8 x .000125 | Open |
| P255 | N247 | N248 | 19.192 | D67.8 x .000125 | Open |
| P256 | N248 | N249 | 13.371 | D67.8 x .000125 | Open |
| P257 | N249 | N37 | 11.088 | D67.8 x .000125 | Open |
| P258 | N242 | N250 | 23.030 | D67.8 x .000125 | Open |
| P259 | N250 | N251 | 21.182 | D67.8 x .000125 | Open |
| P260 | N46 | N252 | 15.520 | D67.8 x .000125 | Open |
| P261 | N252 | N253 | 16.149 | D67.8 x .000125 | Open |
| P262 | N253 | N254 | 18.535 | D67.8 x .000125 | Open |
| P263 | N254 | N255 | 21.367 | D67.8 x .000125 | Open |
| P264 | N255 | N256 | 20.709 | D67.8 x .000125 | Open |
| P265 | N256 | N257 | 22.171 | D67.8 x .000125 | Open |
| P266 | N48 | N258 | 16.663 | D67.8 x .000125 | Open |
| P267 | N258 | N259 | 13.793 | D67.8 x .000125 | Open |
| P268 | N259 | N260 | 19.287 | D67.8 x .000125 | Open |
| P269 | N260 | N261 | 18.900 | D67.8 x .000125 | Open |
| P270 | N261 | N262 | 17.758 | D67.8 x .000125 | Open |
| P271 | N262 | N263 | 25.795 | D67.8 x .000125 | Open |
| P272 | N263 | N264 | 12.807 | D67.8 x .000125 | Open |
| P273 | N50 | N265 | 19.481 | D67.8 x .000125 | Open |
| P274 | N265 | N266 | 23.060 | D67.8 x .000125 | Open |
| P275 | N266 | N267 | 28.414 | D67.8 x .000125 | Open |
| P276 | N267 | N268 | 20.313 | D67.8 x .000125 | Open |
| P277 | N268 | N269 | 22.496 | D67.8 x .000125 | Open |
| P278 | N174 | N270 | 24.930 | D81.4 x .000125 | Open |
| P279 | N270 | N271 | 18.206 | D81.4 x .000125 | Open |
| P280 | N271 | N272 | 23.596 | D81.4 x .000125 | Open |
| P281 | N272 | N273 | 17.987 | D81.4 x .000125 | Open |
| P282 | N273 | N274 | 23.683 | D81.4 x .000125 | Open |
| P283 | N274 | N275 | 21.482 | D81.4 x .000125 | Open |
| P284 | N275 | N276 | 26.611 | D81.4 x .000125 | Open |
| P285 | N276 | N277 | 22.856 | D81.4 x .000125 | Open |
| P286 | N277 | N278 | 37.879 | D81.4 x .000125 | Open |
| P287 | N278 | N279 | 25.201 | D81.4 x .000125 | Open |
| P288 | N279 | N280 | 22.515 | D81.4 x .000125 | Open |
| P289 | N280 | N281 | 23.082 | D81.4 x .000125 | Open |
| P290 | N281 | N282 | 26.167 | D81.4 x .000125 | Open |
| P291 | N282 | N283 | 24.267 | D81.4 x .000125 | Open |
| P292 | N283 | N284 | 21.125 | D81.4 x .000125 | Open |
| P293 | N284 | N285 | 31.723 | D81.4 x .000125 | Open |
| P294 | N285 | N286 | 30.791 | D81.4 x .000125 | Open |
| P295 | N286 | N287 | 18.681 | D81.4 x .000125 | Open |
| P296 | N287 | N288 | 23.967 | D81.4 x .000125 | Open |
| P297 | N288 | N289 | 23.367 | D81.4 x .000125 | Open |
| P298 | N289 | N290 | 27.958 | D81.4 x .000125 | Open |
| P299 | N290 | N291 | 22.276 | D81.4 x .000125 | Open |
| P300 | N291 | N292 | 42.844 | D81.4 x .000125 | Open |
| P301 | N278 | N293 | 16.914 | D67.8 x .000125 | Open |
| P302 | N293 | N294 | 21.357 | D67.8 x .000125 | Open |
| P303 | N294 | N295 | 22.776 | D67.8 x .000125 | Open |
| P304 | N295 | N296 | 23.239 | D67.8 x .000125 | Open |
| P305 | N296 | N297 | 23.991 | D67.8 x .000125 | Open |
| P306 | N297 | N298 | 30.887 | D67.8 x .000125 | Open |
| P307 | N298 | N299 | 31.097 | D67.8 x .000125 | Open |
| P308 | N299 | N300 | 22.580 | D67.8 x .000125 | Open |
| P309 | N300 | N301 | 31.350 | D67.8 x .000125 | Open |
| P310 | N301 | N302 | 14.502 | D67.8 x .000125 | Open |
| P311 | N302 | N303 | 24.048 | D67.8 x .000125 | Open |
| P312 | N303 | N304 | 24.828 | D67.8 x .000125 | Open |
| P313 | N304 | N305 | 26.299 | D67.8 x .000125 | Open |

# Energy

| Pump efficiency (%) | 75.00 |
| --- | --- |
| Energy price (€/kWh) | 0.00 |
| Demand charge (€) | 0.00 |

# Reactions

| Bulk reaction order | 0 |
| --- | --- |
| Wall reaction order |  |
| Global bulk coefficient | 0 |
| Global wall coefficient | 0 |
| Limiting concentration | 0 |
| Wall coefficient correlation | 0 |

# General options

| Formula | Darcy-Weisbach |
| --- | --- |
| Kinematic viscosity (m²/s) | 0.00000139 |
| Fluid density (kg/m³) | 999.88 |
| Constant emitter coefficient k | 0.9 |
| Pressure exponent x | 0.5 |
| Demand multiplier | 1 |
| Molecular diffusion (m²/day) | 0 |
| Quality type check | None |

# Times

| Start date | 01-01-2005 |
| --- | --- |
| Start time | 00:00:00 |
| Total simulation duration | 00:00:00 |
| Hydraulic solver step | 01:00:00 |
| Quality solver step | 00:05:00 |
| Start time frame | 00:00:00 |
| Report time step | 01:00:00 |
| Start time frame | 00:00:00 |
| Pattern time step | 01:00:00 |

# Coordinates

| Name | X coordinate | Y coordinate |
| --- | --- | --- |
| Node N1 | 363038.004137 | 4152164.512865 |
| Node N2 | 363047.761555 | 4152164.577059 |
| Node N3 | 363056.235102 | 4152153.53577 |
| Node N4 | 362508.444479 | 4152246.89272 |
| Node N5 | 362520.377432 | 4152240.582024 |
| Node N6 | 362535.523102 | 4152233.238669 |
| Node N7 | 362548.259234 | 4152224.633174 |
| Node N8 | 362570.97774 | 4152215.56872 |
| Node N9 | 362588.762429 | 4152209.602243 |
| Node N10 | 362608.038737 | 4152204.438947 |
| Node N11 | 362631.560422 | 4152196.636632 |
| Node N12 | 362652.902048 | 4152189.866976 |
| Node N13 | 362670.916217 | 4152184.244719 |
| Node N14 | 362693.175763 | 4152176.098185 |
| Node N15 | 362720.828086 | 4152165.312631 |
| Node N16 | 362746.75931 | 4152155.330258 |
| Node N17 | 362765.691398 | 4152148.216382 |
| Node N18 | 362789.901522 | 4152141.676206 |
| Node N19 | 362813.996907 | 4152139.725627 |
| Node N20 | 362843.599809 | 4152138.807708 |
| Node N21 | 362861.499237 | 4152137.316089 |
| Node N22 | 362885.365142 | 4152134.677071 |
| Node N23 | 362900.396073 | 4152132.955972 |
| Node N24 | 362919.427951 | 4152130.008239 |
| Node N25 | 362937.003342 | 4152127.485456 |
| Node N26 | 362950.205909 | 4152125.130858 |
| Node N27 | 362964.669867 | 4152123.449002 |
| Node N28 | 362983.338465 | 4152121.26259 |
| Node N29 | 362999.988835 | 4152120.253477 |
| Node N30 | 363023.871185 | 4152117.982972 |
| Node N31 | 363037.578309 | 4152117.394322 |
| Node N32 | 363052.294545 | 4152117.226137 |
| Node N33 | 363067.178967 | 4152117.814786 |
| Node N34 | 363082.147483 | 4152117.310229 |
| Node N35 | 363102.245657 | 4152116.301116 |
| Node N36 | 363121.839275 | 4152115.796559 |
| Node N37 | 363140.171501 | 4152114.114704 |
| Node N38 | 363160.101491 | 4152112.264663 |
| Node N39 | 363174.733634 | 4152111.507827 |
| Node N40 | 363195.420459 | 4152108.312302 |
| Node N41 | 363214.004963 | 4152107.807745 |
| Node N42 | 363233.85086 | 4152110.6669 |
| Node N43 | 363253.192199 | 4152119.328456 |
| Node N44 | 363263.031055 | 4152128.915033 |
| Node N45 | 363273.038095 | 4152135.47427 |
| Node N46 | 363291.538507 | 4152142.874435 |
| Node N47 | 363315.000393 | 4152149.68595 |
| Node N48 | 363332.071228 | 4152154.395146 |
| Node N49 | 363346.95565 | 4152163.224888 |
| Node N50 | 363361.335516 | 4152173.904671 |
| Node N51 | 363377.144958 | 4152183.491248 |
| Node N52 | 363391.777102 | 4152194.507402 |
| Node N53 | 363403.634184 | 4152207.457691 |
| Node N54 | 363417.004937 | 4152221.248907 |
| Node N55 | 363426.086957 | 4152233.274174 |
| Node N56 | 363430.964338 | 4152245.047164 |
| Node N57 | 363441.30775 | 4152255.054205 |
| Node N58 | 363454.59441 | 4152265.061246 |
| Node N59 | 363468.133348 | 4152275.236472 |
| Node N60 | 363481.340554 | 4152284.079835 |
| Node N61 | 363494.958945 | 4152293.064142 |
| Node N62 | 363504.293243 | 4152299.875657 |
| Node N63 | 363519.177666 | 4152308.957677 |
| Node N64 | 363534.566645 | 4152317.19877 |
| Node N65 | 363550.039716 | 4152325.439862 |
| Node N66 | 363567.194644 | 4152334.101419 |
| Node N67 | 363582.415437 | 4152341.501584 |
| Node N68 | 363598.729436 | 4152349.490398 |
| Node N69 | 363615.968457 | 4152355.208707 |
| Node N70 | 363634.132497 | 4152360.674738 |
| Node N71 | 363654.567043 | 4152365.972583 |
| Node N72 | 363671.806063 | 4152370.849964 |
| Node N73 | 363691.904238 | 4152376.568273 |
| Node N74 | 363711.077392 | 4152381.529747 |
| Node N75 | 363729.325525 | 4152386.238943 |
| Node N76 | 363748.078216 | 4152388.593541 |
| Node N77 | 363766.830906 | 4152393.134551 |
| Node N78 | 363780.790307 | 4152397.423283 |
| Node N79 | 363794.329245 | 4152401.039273 |
| Node N80 | 363795.842915 | 4152416.428252 |
| Node N81 | 363793.740596 | 4152428.285334 |
| Node N82 | 363789.846131 | 4152442.759247 |
| Node N83 | 363786.666847 | 4152455.218601 |
| Node N84 | 363784.34683 | 4152468.537221 |
| Node N85 | 363781.888983 | 4152479.582535 |
| Node N86 | 363777.727599 | 4152487.810726 |
| Node N87 | 363783.35197 | 4152503.07102 |
| Node N88 | 363787.682889 | 4152517.432188 |
| Node N89 | 363796.201021 | 4152529.778905 |
| Node N91 | 362528.719369 | 4152223.74092 |
| Node N92 | 362532.006217 | 4152203.12342 |
| Node N93 | 362540.073934 | 4152184.746952 |
| Node N94 | 362544.257195 | 4152161.88842 |
| Node N95 | 362548.440456 | 4152145.155376 |
| Node N96 | 362554.416543 | 4152126.480104 |
| Node N97 | 362559.04801 | 4152109.00005 |
| Node N98 | 362563.679478 | 4152090.47418 |
| Node N99 | 362571.000184 | 4152077.326789 |
| Node N100 | 362598.490184 | 4152085.394506 |
| Node N101 | 362617.912467 | 4152090.025974 |
| Node N102 | 362643.161434 | 4152095.852659 |
| Node N103 | 362663.778934 | 4152099.886517 |
| Node N104 | 362689.774913 | 4152103.472169 |
| Node N105 | 362721.149369 | 4152108.850648 |
| Node N106 | 362746.697141 | 4152112.4363 |
| Node N107 | 362768.659261 | 4152118.113583 |
| Node N108 | 362789.127359 | 4152126.1813 |
| Node N109 | 362553.334688 | 4152235.816708 |
| Node N110 | 362566.437004 | 4152237.658115 |
| Node N111 | 362584.072015 | 4152240.915988 |
| Node N112 | 362603.548431 | 4152245.802798 |
| Node N113 | 362620.758502 | 4152250.264668 |
| Node N114 | 362632.656822 | 4152252.885131 |
| Node N115 | 362649.725245 | 4152253.805835 |
| Node N116 | 362665.306379 | 4152254.584892 |
| Node N117 | 362682.941389 | 4152256.001358 |
| Node N118 | 362698.734992 | 4152257.913588 |
| Node N119 | 362713.253776 | 4152260.958992 |
| Node N120 | 362725.152096 | 4152263.366985 |
| Node N121 | 362736.413006 | 4152265.987448 |
| Node N122 | 362747.603093 | 4152268.678735 |
| Node N123 | 362758.439063 | 4152271.228375 |
| Node N124 | 362774.799253 | 4152275.973538 |
| Node N125 | 362792.15097 | 4152279.939645 |
| Node N126 | 362795.33802 | 4152270.945082 |
| Node N127 | 362797.67519 | 4152257.347002 |
| Node N128 | 362799.445773 | 4152243.748921 |
| Node N129 | 362799.658243 | 4152232.063071 |
| Node N130 | 362795.55049 | 4152219.598165 |
| Node N131 | 362792.859203 | 4152205.433498 |
| Node N132 | 362792.080146 | 4152191.906241 |
| Node N133 | 362791.017796 | 4152176.466754 |
| Node N134 | 362790.66368 | 4152158.406804 |
| Node N135 | 362771.760011 | 4152289.673398 |
| Node N136 | 362769.550231 | 4152302.07272 |
| Node N137 | 362765.56035 | 4152315.576932 |
| Node N138 | 362761.14079 | 4152328.34455 |
| Node N139 | 362759.851751 | 4152342.155676 |
| Node N140 | 362758.439947 | 4152351.976921 |
| Node N141 | 362756.168784 | 4152368.550272 |
| Node N142 | 362753.897621 | 4152386.780958 |
| Node N143 | 362751.810607 | 4152401.328678 |
| Node N144 | 362749.355296 | 4152418.331708 |
| Node N145 | 362749.171147 | 4152433.247724 |
| Node N146 | 362750.582951 | 4152447.427147 |
| Node N147 | 362755.002511 | 4152458.905727 |
| Node N148 | 362758.624096 | 4152471.796111 |
| Node N149 | 362771.207566 | 4152475.785992 |
| Node N150 | 362778.757648 | 4152482.722246 |
| Node N151 | 362775.688509 | 4152494.323592 |
| Node N152 | 362771.698628 | 4152507.827804 |
| Node N153 | 362769.059169 | 4152518.815322 |
| Node N154 | 362765.314819 | 4152531.214644 |
| Node N155 | 362950.154204 | 4152114.198993 |
| Node N156 | 362948.953907 | 4152096.294559 |
| Node N157 | 362948.853882 | 4152080.290596 |
| Node N158 | 362949.85413 | 4152064.586707 |
| Node N159 | 362951.654576 | 4152048.482719 |
| Node N160 | 362955.855616 | 4152034.279202 |
| Node N161 | 362960.55678 | 4152018.375264 |
| Node N162 | 362966.058143 | 4151999.970706 |
| Node N163 | 362971.759555 | 4151982.766446 |
| Node N164 | 362977.460966 | 4151958.760501 |
| Node N165 | 362984.362676 | 4151937.3552 |
| Node N166 | 362988.963815 | 4151921.851361 |
| Node N167 | 362994.365153 | 4151906.147472 |
| Node N168 | 363000.266614 | 4151887.842939 |
| Node N169 | 363005.767976 | 4151871.238827 |
| Node N170 | 363012.169562 | 4151856.535186 |
| Node N171 | 363018.271073 | 4151842.931817 |
| Node N172 | 363025.068408 | 4151826.928176 |
| Node N173 | 363030.562844 | 4151811.290165 |
| Node N174 | 363038.276188 | 4151793.11626 |
| Node N175 | 363043.5593 | 4151812.875099 |
| Node N176 | 363049.370723 | 4151829.992381 |
| Node N177 | 363055.604795 | 4151847.532312 |
| Node N178 | 363060.887906 | 4151862.747674 |
| Node N179 | 363066.699329 | 4151878.702672 |
| Node N180 | 363072.193766 | 4151896.348266 |
| Node N181 | 363079.273136 | 4151915.684455 |
| Node N182 | 363084.239261 | 4151932.696075 |
| Node N183 | 363088.46575 | 4151950.341669 |
| Node N184 | 363095.333796 | 4151970.945805 |
| Node N185 | 363101.250881 | 4151986.266829 |
| Node N186 | 363107.167966 | 4152001.165205 |
| Node N187 | 363114.45866 | 4152020.184407 |
| Node N188 | 363113.719025 | 4152037.196027 |
| Node N189 | 363109.386873 | 4152060.336057 |
| Node N190 | 363108.964224 | 4152082.525127 |
| Node N191 | 363102.201841 | 4152097.846151 |
| Node N192 | 363270.556346 | 4152116.481944 |
| Node N193 | 363287.174619 | 4152107.436555 |
| Node N194 | 363310.629523 | 4152101.336177 |
| Node N195 | 363332.086027 | 4152101.230998 |
| Node N196 | 363356.6979 | 4152104.070829 |
| Node N197 | 363379.363962 | 4152107.909861 |
| Node N198 | 363379.206193 | 4152122.003839 |
| Node N199 | 363379.889857 | 4152132.416554 |
| Node N200 | 363378.417351 | 4152147.457143 |
| Node N201 | 363376.208594 | 4152159.763079 |
| Node N202 | 363375.998236 | 4152171.858657 |
| Node N203 | 363355.254518 | 4152115.256777 |
| Node N204 | 363355.66652 | 4152128.337837 |
| Node N205 | 363351.649501 | 4152142.242901 |
| Node N206 | 363345.428451 | 4152154.17535 |
| Node N207 | 363288.635035 | 4152118.609316 |
| Node N208 | 363290.658304 | 4152129.796801 |
| Node N209 | 363431.751526 | 4152059.220436 |
| Node N210 | 363409.614589 | 4152080.286231 |
| Node N211 | 363394.02352 | 4152096.829426 |
| Node N212 | 363001.670594 | 4152135.112224 |
| Node N213 | 363001.606401 | 4152145.511578 |
| Node N214 | 363000.065756 | 4152160.404479 |
| Node N215 | 363010.336722 | 4152164.833833 |
| Node N216 | 363018.232527 | 4152165.989317 |
| Node N217 | 363026.770268 | 4152162.715446 |
| Node N218 | 363061.434779 | 4152144.805449 |
| Node N219 | 363066.506068 | 4152137.423192 |
| Node N220 | 363070.116598 | 4152127.650082 |
| Node N221 | 363098.545174 | 4152169.216904 |
| Node N222 | 363100.519466 | 4152152.261219 |
| Node N223 | 363101.680815 | 4152134.72486 |
| Node N224 | 363182.213857 | 4152118.789217 |
| Node N225 | 363196.283204 | 4152126.828844 |
| Node N226 | 363204.490324 | 4152140.144476 |
| Node N227 | 363212.864935 | 4152157.479922 |
| Node N228 | 363229.614158 | 4152154.7163 |
| Node N229 | 363244.102236 | 4152153.878839 |
| Node N230 | 363258.841553 | 4152155.972492 |
| Node N231 | 363267.29991 | 4152148.100357 |
| Node N232 | 363255.576117 | 4152172.012824 |
| Node N233 | 363251.042178 | 4152189.118138 |
| Node N234 | 363245.271711 | 4152204.471702 |
| Node N235 | 363241.046904 | 4152220.855708 |
| Node N236 | 363237.028186 | 4152236.724493 |
| Node N237 | 363231.875983 | 4152248.986736 |
| Node N238 | 363226.620736 | 4152262.073331 |
| Node N239 | 363222.39593 | 4152277.632984 |
| Node N240 | 363226.620736 | 4152292.677417 |
| Node N241 | 363210.329442 | 4152172.911981 |
| Node N242 | 363204.903991 | 4152186.766258 |
| Node N243 | 363188.046339 | 4152191.513528 |
| Node N244 | 363171.769985 | 4152195.291967 |
| Node N245 | 363149.09935 | 4152193.451189 |
| Node N246 | 363148.033636 | 4152171.361852 |
| Node N247 | 363147.936753 | 4152155.182382 |
| Node N248 | 363147.355455 | 4152135.999536 |
| Node N249 | 363147.258572 | 4152122.629674 |
| Node N250 | 363203.854053 | 4152209.667623 |
| Node N251 | 363204.182562 | 4152230.692171 |
| Node N252 | 363283.528331 | 4152156.164527 |
| Node N253 | 363276.859607 | 4152170.805059 |
| Node N254 | 363269.347711 | 4152187.745151 |
| Node N255 | 363262.755639 | 4152208.057931 |
| Node N256 | 363257.313347 | 4152227.98745 |
| Node N257 | 363252.407619 | 4152249.45001 |
| Node N258 | 363323.993109 | 4152168.96728 |
| Node N259 | 363319.43138 | 4152181.979425 |
| Node N260 | 363315.019216 | 4152200.749817 |
| Node N261 | 363312.327048 | 4152219.445426 |
| Node N262 | 363312.252266 | 4152237.019299 |
| Node N263 | 363312.850525 | 4152262.744458 |
| Node N264 | 363310.980964 | 4152275.083561 |
| Node N265 | 363353.684396 | 4152191.815143 |
| Node N266 | 363366.100275 | 4152211.191439 |
| Node N267 | 363363.372544 | 4152239.409346 |
| Node N268 | 363361.209171 | 4152259.53812 |
| Node N269 | 363368.545827 | 4152280.51343 |
| Node N270 | 363031.247781 | 4151769.204959 |
| Node N271 | 363025.604199 | 4151751.897977 |
| Node N272 | 363019.39626 | 4151729.135532 |
| Node N273 | 363014.505156 | 4151711.828549 |
| Node N274 | 363006.792262 | 4151689.442343 |
| Node N275 | 362999.831845 | 4151669.12545 |
| Node N276 | 362994.000144 | 4151643.164976 |
| Node N277 | 362990.425876 | 4151620.59065 |
| Node N278 | 362988.168443 | 4151582.778655 |
| Node N279 | 362985.158533 | 4151557.758778 |
| Node N280 | 362981.396145 | 4151535.560691 |
| Node N281 | 362978.950594 | 4151512.610127 |
| Node N282 | 362974.435728 | 4151486.837772 |
| Node N283 | 362971.425818 | 4151462.758492 |
| Node N284 | 362966.346595 | 4151442.253479 |
| Node N285 | 362962.01985 | 4151410.837543 |
| Node N286 | 362955.623791 | 4151380.738443 |
| Node N287 | 362949.603971 | 4151363.055221 |
| Node N288 | 362939.445524 | 4151341.421493 |
| Node N289 | 362927.970242 | 4151321.1046 |
| Node N290 | 362921.197944 | 4151294.015409 |
| Node N291 | 362915.930602 | 4151272.381681 |
| Node N292 | 362908.405827 | 4151230.24294 |
| Node N293 | 363005.065744 | 4151583.541166 |
| Node N294 | 363022.42122 | 4151595.976275 |
| Node N295 | 363043.355144 | 4151604.922396 |
| Node N296 | 363066.525599 | 4151606.532698 |
| Node N297 | 363090.501205 | 4151606.174853 |
| Node N298 | 363121.365324 | 4151606.174853 |
| Node N299 | 363152.408366 | 4151605.90647 |
| Node N300 | 363172.805523 | 4151596.244658 |
| Node N301 | 363198.033586 | 4151577.636726 |
| Node N302 | 363200.359577 | 4151563.322931 |
| Node N303 | 363194.276215 | 4151540.063015 |
| Node N304 | 363191.533465 | 4151515.387539 |
| Node N305 | 363202.685569 | 4151491.575036 |
| Reservoir N90 | 363804.719153 | 4152542.125622 |

# Background

| Units | None |
| --- | --- |

# Results

# Time instant01/01/2005 - 00:00:00

## Junctions

| # | Name | Pressure elevation (m) | Pressure height (m) | Real demand (L/s) | Quality |
| --- | --- | --- | --- | --- | --- |
| 1 | N1 | 717.817 | 58.800 | 0.00 | 0.000 |
| 2 | N2 | 717.818 | 59.025 | 0.00 | 0.000 |
| 3 | N3 | 717.820 | 60.096 | 0.00 | 0.000 |
| 4 | N4 | 717.694 | 72.085 | 0.25 | 0.000 |
| 5 | N5 | 717.695 | 71.992 | 0.00 | 0.000 |
| 6 | N6 | 717.696 | 72.037 | 0.00 | 0.000 |
| 7 | N7 | 717.697 | 71.890 | 0.00 | 0.000 |
| 8 | N8 | 717.699 | 71.796 | 0.00 | 0.000 |
| 9 | N9 | 717.700 | 71.616 | 0.00 | 0.000 |
| 10 | N10 | 717.701 | 71.640 | 0.00 | 0.000 |
| 11 | N11 | 717.703 | 71.677 | 0.00 | 0.000 |
| 12 | N12 | 717.705 | 71.489 | 0.00 | 0.000 |
| 13 | N13 | 717.706 | 71.419 | 0.00 | 0.000 |
| 14 | N14 | 717.708 | 71.221 | 0.00 | 0.000 |
| 15 | N15 | 717.710 | 70.825 | 0.00 | 0.000 |
| 16 | N16 | 717.712 | 70.507 | 0.00 | 0.000 |
| 17 | N17 | 717.713 | 70.109 | 0.00 | 0.000 |
| 18 | N18 | 717.715 | 69.684 | 0.00 | 0.000 |
| 19 | N19 | 717.721 | 69.122 | 0.00 | 0.000 |
| 20 | N20 | 717.734 | 68.075 | 0.00 | 0.000 |
| 21 | N21 | 717.742 | 67.607 | 0.00 | 0.000 |
| 22 | N22 | 717.753 | 66.838 | 0.00 | 0.000 |
| 23 | N23 | 717.760 | 66.244 | 0.00 | 0.000 |
| 24 | N24 | 717.768 | 65.616 | 0.00 | 0.000 |
| 25 | N25 | 717.776 | 65.141 | 0.00 | 0.000 |
| 26 | N26 | 717.782 | 64.367 | 0.00 | 0.000 |
| 27 | N27 | 717.790 | 63.980 | 0.00 | 0.000 |
| 28 | N28 | 717.799 | 63.584 | 0.00 | 0.000 |
| 29 | N29 | 717.807 | 62.494 | 0.00 | 0.000 |
| 30 | N30 | 717.814 | 61.599 | 0.00 | 0.000 |
| 31 | N31 | 717.817 | 61.127 | 0.00 | 0.000 |
| 32 | N32 | 717.821 | 60.602 | 0.00 | 0.000 |
| 33 | N33 | 717.825 | 60.039 | 0.00 | 0.000 |
| 34 | N34 | 717.833 | 58.969 | 0.00 | 0.000 |
| 35 | N35 | 717.843 | 58.546 | 0.00 | 0.000 |
| 36 | N36 | 717.868 | 57.990 | 0.00 | 0.000 |
| 37 | N37 | 717.892 | 57.500 | 0.00 | 0.000 |
| 38 | N38 | 717.917 | 56.819 | 0.00 | 0.000 |
| 39 | N39 | 717.935 | 56.379 | 0.00 | 0.000 |
| 40 | N40 | 717.961 | 55.794 | 0.00 | 0.000 |
| 41 | N41 | 717.984 | 55.091 | 0.00 | 0.000 |
| 42 | N42 | 718.009 | 54.142 | 0.00 | 0.000 |
| 43 | N43 | 718.035 | 52.833 | 0.00 | 0.000 |
| 44 | N44 | 718.052 | 52.182 | 0.00 | 0.000 |
| 45 | N45 | 718.055 | 51.685 | 0.00 | 0.000 |
| 46 | N46 | 718.099 | 50.758 | 0.00 | 0.000 |
| 47 | N47 | 718.158 | 50.213 | 0.00 | 0.000 |
| 48 | N48 | 718.201 | 48.961 | 0.00 | 0.000 |
| 49 | N49 | 718.253 | 48.119 | 0.00 | 0.000 |
| 50 | N50 | 718.321 | 47.298 | 0.00 | 0.000 |
| 51 | N51 | 718.406 | 46.378 | 0.00 | 0.000 |
| 52 | N52 | 718.557 | 45.439 | 0.00 | 0.000 |
| 53 | N53 | 718.703 | 43.967 | 0.00 | 0.000 |
| 54 | N54 | 718.862 | 42.733 | 0.10 | 0.000 |
| 55 | N55 | 718.993 | 42.016 | 0.00 | 0.000 |
| 56 | N56 | 719.104 | 41.351 | 0.00 | 0.000 |
| 57 | N57 | 719.229 | 40.501 | 0.00 | 0.000 |
| 58 | N58 | 719.374 | 39.678 | 0.10 | 0.000 |
| 59 | N59 | 719.528 | 38.666 | 0.00 | 0.000 |
| 60 | N60 | 719.673 | 37.712 | 0.00 | 0.000 |
| 61 | N61 | 719.823 | 36.332 | 0.00 | 0.000 |
| 62 | N62 | 719.928 | 35.903 | 0.00 | 0.000 |
| 63 | N63 | 720.087 | 35.475 | 0.00 | 0.000 |
| 64 | N64 | 720.247 | 34.615 | 0.00 | 0.000 |
| 65 | N65 | 720.407 | 33.673 | 0.10 | 0.000 |
| 66 | N66 | 720.591 | 32.804 | 0.00 | 0.000 |
| 67 | N67 | 720.753 | 31.747 | 0.00 | 0.000 |
| 68 | N68 | 720.926 | 31.224 | 0.00 | 0.000 |
| 69 | N69 | 721.100 | 30.160 | 0.00 | 0.000 |
| 70 | N70 | 721.282 | 29.433 | 0.00 | 0.000 |
| 71 | N71 | 721.484 | 28.089 | 0.00 | 0.000 |
| 72 | N72 | 721.656 | 27.023 | 0.00 | 0.000 |
| 73 | N73 | 721.856 | 25.921 | 0.00 | 0.000 |
| 74 | N74 | 722.045 | 25.300 | 0.10 | 0.000 |
| 75 | N75 | 722.234 | 25.798 | 0.00 | 0.000 |
| 76 | N76 | 722.424 | 24.465 | 0.00 | 0.000 |
| 77 | N77 | 722.617 | 24.139 | 0.00 | 0.000 |
| 78 | N78 | 722.764 | 23.102 | 0.00 | 0.000 |
| 79 | N79 | 722.904 | 23.685 | 0.10 | 0.000 |
| 80 | N80 | 723.067 | 22.493 | 0.00 | 0.000 |
| 81 | N81 | 723.194 | 20.994 | 0.00 | 0.000 |
| 82 | N82 | 723.353 | 19.094 | 0.00 | 0.000 |
| 83 | N83 | 723.489 | 17.531 | 0.00 | 0.000 |
| 84 | N84 | 723.632 | 15.811 | 0.00 | 0.000 |
| 85 | N85 | 723.751 | 14.420 | 0.00 | 0.000 |
| 86 | N86 | 723.849 | 13.434 | 0.00 | 0.000 |
| 87 | N87 | 724.021 | 11.018 | 0.00 | 0.000 |
| 88 | N88 | 724.180 | 8.730 | 0.00 | 0.000 |
| 89 | N89 | 724.339 | 6.591 | 0.00 | 0.000 |
| 90 | N91 | 717.695 | 72.490 | 0.00 | 0.000 |
| 91 | N92 | 717.695 | 72.520 | 0.00 | 0.000 |
| 92 | N93 | 717.694 | 72.131 | 0.00 | 0.000 |
| 93 | N94 | 717.694 | 72.210 | 0.00 | 0.000 |
| 94 | N95 | 717.694 | 72.269 | 0.00 | 0.000 |
| 95 | N96 | 717.694 | 72.325 | 0.00 | 0.000 |
| 96 | N97 | 717.694 | 72.157 | 0.00 | 0.000 |
| 97 | N98 | 717.694 | 72.066 | 0.00 | 0.000 |
| 98 | N99 | 717.694 | 71.981 | 0.25 | 0.000 |
| 99 | N100 | 717.697 | 71.772 | 0.00 | 0.000 |
| 100 | N101 | 717.699 | 72.004 | 0.00 | 0.000 |
| 101 | N102 | 717.702 | 71.844 | 0.00 | 0.000 |
| 102 | N103 | 717.704 | 71.567 | 0.00 | 0.000 |
| 103 | N104 | 717.707 | 71.104 | 0.00 | 0.000 |
| 104 | N105 | 717.710 | 70.840 | 0.00 | 0.000 |
| 105 | N106 | 717.713 | 70.408 | 0.00 | 0.000 |
| 106 | N107 | 717.715 | 69.989 | 0.00 | 0.000 |
| 107 | N108 | 717.718 | 69.486 | 0.00 | 0.000 |
| 108 | N109 | 717.696 | 72.281 | 0.00 | 0.000 |
| 109 | N110 | 717.696 | 72.310 | 0.00 | 0.000 |
| 110 | N111 | 717.696 | 72.338 | 0.00 | 0.000 |
| 111 | N112 | 717.696 | 72.259 | 0.00 | 0.000 |
| 112 | N113 | 717.696 | 72.317 | 0.00 | 0.000 |
| 113 | N114 | 717.696 | 72.174 | 0.00 | 0.000 |
| 114 | N115 | 717.695 | 72.286 | 0.00 | 0.000 |
| 115 | N116 | 717.695 | 72.288 | 0.00 | 0.000 |
| 116 | N117 | 717.695 | 71.979 | 0.00 | 0.000 |
| 117 | N118 | 717.695 | 71.623 | 0.00 | 0.000 |
| 118 | N119 | 717.695 | 71.485 | 0.00 | 0.000 |
| 119 | N120 | 717.695 | 71.323 | 0.00 | 0.000 |
| 120 | N121 | 717.695 | 71.188 | 0.00 | 0.000 |
| 121 | N122 | 717.695 | 70.933 | 0.00 | 0.000 |
| 122 | N123 | 717.695 | 70.762 | 0.00 | 0.000 |
| 123 | N124 | 717.695 | 70.325 | 0.00 | 0.000 |
| 124 | N125 | 717.697 | 70.087 | 0.00 | 0.000 |
| 125 | N126 | 717.699 | 69.991 | 0.00 | 0.000 |
| 126 | N127 | 717.700 | 69.620 | 0.00 | 0.000 |
| 127 | N128 | 717.702 | 69.324 | 0.00 | 0.000 |
| 128 | N129 | 717.703 | 69.110 | 0.00 | 0.000 |
| 129 | N130 | 717.705 | 68.994 | 0.00 | 0.000 |
| 130 | N131 | 717.707 | 69.038 | 0.00 | 0.000 |
| 131 | N132 | 717.709 | 69.113 | 0.00 | 0.000 |
| 132 | N133 | 717.711 | 69.303 | 0.00 | 0.000 |
| 133 | N134 | 717.713 | 69.634 | 0.00 | 0.000 |
| 134 | N135 | 717.693 | 70.585 | 0.00 | 0.000 |
| 135 | N136 | 717.691 | 70.922 | 0.00 | 0.000 |
| 136 | N137 | 717.689 | 71.067 | 0.00 | 0.000 |
| 137 | N138 | 717.687 | 71.065 | 0.00 | 0.000 |
| 138 | N139 | 717.685 | 71.293 | 0.00 | 0.000 |
| 139 | N140 | 717.684 | 71.317 | 0.00 | 0.000 |
| 140 | N141 | 717.681 | 71.057 | 0.00 | 0.000 |
| 141 | N142 | 717.679 | 70.850 | 0.00 | 0.000 |
| 142 | N143 | 717.677 | 69.968 | 0.00 | 0.000 |
| 143 | N144 | 717.674 | 69.445 | 0.00 | 0.000 |
| 144 | N145 | 717.672 | 68.659 | 0.00 | 0.000 |
| 145 | N146 | 717.670 | 67.820 | 0.00 | 0.000 |
| 146 | N147 | 717.668 | 66.808 | 0.00 | 0.000 |
| 147 | N148 | 717.666 | 66.386 | 0.00 | 0.000 |
| 148 | N149 | 717.664 | 65.203 | 0.00 | 0.000 |
| 149 | N150 | 717.663 | 64.452 | 0.00 | 0.000 |
| 150 | N151 | 717.661 | 64.345 | 0.00 | 0.000 |
| 151 | N152 | 717.659 | 64.164 | 0.00 | 0.000 |
| 152 | N153 | 717.657 | 63.752 | 0.00 | 0.000 |
| 153 | N154 | 717.655 | 63.369 | 0.25 | 0.000 |
| 154 | N155 | 717.782 | 64.378 | 0.00 | 0.000 |
| 155 | N156 | 717.782 | 64.261 | 0.00 | 0.000 |
| 156 | N157 | 717.782 | 64.263 | 0.00 | 0.000 |
| 157 | N158 | 717.782 | 64.316 | 0.00 | 0.000 |
| 158 | N159 | 717.782 | 63.662 | 0.00 | 0.000 |
| 159 | N160 | 717.782 | 63.383 | 0.00 | 0.000 |
| 160 | N161 | 717.781 | 60.462 | 0.00 | 0.000 |
| 161 | N162 | 717.781 | 61.594 | 0.00 | 0.000 |
| 162 | N163 | 717.781 | 62.553 | 0.00 | 0.000 |
| 163 | N164 | 717.781 | 63.467 | 0.00 | 0.000 |
| 164 | N165 | 717.780 | 63.293 | 0.00 | 0.000 |
| 165 | N166 | 717.780 | 63.354 | 0.00 | 0.000 |
| 166 | N167 | 717.780 | 63.385 | 0.00 | 0.000 |
| 167 | N168 | 717.780 | 63.473 | 0.00 | 0.000 |
| 168 | N169 | 717.780 | 63.980 | 0.00 | 0.000 |
| 169 | N170 | 717.779 | 63.617 | 0.00 | 0.000 |
| 170 | N171 | 717.779 | 63.678 | 0.00 | 0.000 |
| 171 | N172 | 717.779 | 63.997 | 0.00 | 0.000 |
| 172 | N173 | 717.779 | 63.730 | 0.00 | 0.000 |
| 173 | N174 | 717.779 | 63.303 | 0.00 | 0.000 |
| 174 | N175 | 717.783 | 62.857 | 0.00 | 0.000 |
| 175 | N176 | 717.786 | 62.707 | 0.00 | 0.000 |
| 176 | N177 | 717.789 | 62.263 | 0.00 | 0.000 |
| 177 | N178 | 717.793 | 61.579 | 0.00 | 0.000 |
| 178 | N179 | 717.796 | 61.410 | 0.00 | 0.000 |
| 179 | N180 | 717.799 | 60.596 | 0.00 | 0.000 |
| 180 | N181 | 717.803 | 60.365 | 0.00 | 0.000 |
| 181 | N182 | 717.807 | 59.556 | 0.00 | 0.000 |
| 182 | N183 | 717.810 | 59.145 | 0.00 | 0.000 |
| 183 | N184 | 717.814 | 59.421 | 0.00 | 0.000 |
| 184 | N185 | 717.817 | 59.225 | 0.00 | 0.000 |
| 185 | N186 | 717.820 | 59.187 | 0.00 | 0.000 |
| 186 | N187 | 717.824 | 59.040 | 0.00 | 0.000 |
| 187 | N188 | 717.827 | 58.806 | 0.00 | 0.000 |
| 188 | N189 | 717.832 | 58.281 | 0.00 | 0.000 |
| 189 | N190 | 717.836 | 58.383 | 0.00 | 0.000 |
| 190 | N191 | 717.839 | 58.738 | 0.00 | 0.000 |
| 191 | N192 | 718.073 | 51.823 | 0.00 | 0.000 |
| 192 | N193 | 718.101 | 51.768 | 0.00 | 0.000 |
| 193 | N194 | 718.149 | 50.619 | 0.00 | 0.000 |
| 194 | N195 | 718.191 | 49.600 | 0.00 | 0.000 |
| 195 | N196 | 718.240 | 48.248 | 0.00 | 0.000 |
| 196 | N197 | 718.266 | 47.086 | 0.00 | 0.000 |
| 197 | N198 | 718.292 | 46.875 | 0.00 | 0.000 |
| 198 | N199 | 718.311 | 46.723 | 0.00 | 0.000 |
| 199 | N200 | 718.339 | 46.495 | 0.00 | 0.000 |
| 200 | N201 | 718.362 | 46.273 | 0.00 | 0.000 |
| 201 | N202 | 718.384 | 46.395 | 0.00 | 0.000 |
| 202 | N203 | 718.243 | 48.285 | 0.00 | 0.000 |
| 203 | N204 | 718.245 | 48.043 | 0.00 | 0.000 |
| 204 | N205 | 718.248 | 47.826 | 0.00 | 0.000 |
| 205 | N206 | 718.251 | 48.160 | 0.00 | 0.000 |
| 206 | N207 | 718.100 | 51.577 | 0.00 | 0.000 |
| 207 | N208 | 718.100 | 50.937 | 0.00 | 0.000 |
| 208 | N209 | 718.255 | 45.200 | 0.25 | 0.000 |
| 209 | N210 | 718.260 | 46.444 | 0.00 | 0.000 |
| 210 | N211 | 718.263 | 46.627 | 0.00 | 0.000 |
| 211 | N212 | 717.809 | 63.044 | 0.00 | 0.000 |
| 212 | N213 | 717.810 | 62.802 | 0.00 | 0.000 |
| 213 | N214 | 717.812 | 62.268 | 0.00 | 0.000 |
| 214 | N215 | 717.814 | 60.909 | 0.00 | 0.000 |
| 215 | N216 | 717.815 | 59.918 | 0.00 | 0.000 |
| 216 | N217 | 717.816 | 59.359 | 0.00 | 0.000 |
| 217 | N218 | 717.821 | 60.954 | 0.00 | 0.000 |
| 218 | N219 | 717.823 | 60.454 | 0.00 | 0.000 |
| 219 | N220 | 717.824 | 60.150 | 0.00 | 0.000 |
| 220 | N221 | 717.841 | 58.016 | 0.10 | 0.000 |
| 221 | N222 | 717.842 | 58.653 | 0.00 | 0.000 |
| 222 | N223 | 717.842 | 59.252 | 0.00 | 0.000 |
| 223 | N224 | 717.917 | 56.234 | 0.00 | 0.000 |
| 224 | N225 | 717.917 | 55.754 | 0.00 | 0.000 |
| 225 | N226 | 717.917 | 55.104 | 0.00 | 0.000 |
| 226 | N227 | 717.917 | 53.781 | 0.25 | 0.000 |
| 227 | N228 | 717.937 | 53.605 | 0.00 | 0.000 |
| 228 | N229 | 717.954 | 52.974 | 0.00 | 0.000 |
| 229 | N230 | 717.971 | 52.370 | 0.10 | 0.000 |
| 230 | N231 | 718.009 | 52.023 | 0.00 | 0.000 |
| 231 | N232 | 717.963 | 51.787 | 0.00 | 0.000 |
| 232 | N233 | 717.953 | 51.079 | 0.00 | 0.000 |
| 233 | N234 | 717.944 | 50.280 | 0.25 | 0.000 |
| 234 | N235 | 717.942 | 48.864 | 0.00 | 0.000 |
| 235 | N236 | 717.940 | 46.995 | 0.00 | 0.000 |
| 236 | N237 | 717.938 | 45.467 | 0.00 | 0.000 |
| 237 | N238 | 717.936 | 42.930 | 0.00 | 0.000 |
| 238 | N239 | 717.933 | 41.042 | 0.00 | 0.000 |
| 239 | N240 | 717.931 | 38.246 | 0.25 | 0.000 |
| 240 | N241 | 717.909 | 53.721 | 0.00 | 0.000 |
| 241 | N242 | 717.901 | 52.947 | 0.00 | 0.000 |
| 242 | N243 | 717.898 | 53.167 | 0.00 | 0.000 |
| 243 | N244 | 717.895 | 53.553 | 0.00 | 0.000 |
| 244 | N245 | 717.892 | 54.721 | 0.25 | 0.000 |
| 245 | N246 | 717.892 | 56.173 | 0.00 | 0.000 |
| 246 | N247 | 717.892 | 56.768 | 0.00 | 0.000 |
| 247 | N248 | 717.892 | 56.859 | 0.00 | 0.000 |
| 248 | N249 | 717.892 | 57.029 | 0.00 | 0.000 |
| 249 | N250 | 717.897 | 50.755 | 0.00 | 0.000 |
| 250 | N251 | 717.894 | 48.197 | 0.25 | 0.000 |
| 251 | N252 | 718.097 | 51.018 | 0.00 | 0.000 |
| 252 | N253 | 718.094 | 49.614 | 0.00 | 0.000 |
| 253 | N254 | 718.092 | 50.004 | 0.00 | 0.000 |
| 254 | N255 | 718.089 | 49.290 | 0.00 | 0.000 |
| 255 | N256 | 718.086 | 47.859 | 0.00 | 0.000 |
| 256 | N257 | 718.082 | 45.240 | 0.25 | 0.000 |
| 257 | N258 | 718.198 | 49.154 | 0.00 | 0.000 |
| 258 | N259 | 718.196 | 48.804 | 0.00 | 0.000 |
| 259 | N260 | 718.193 | 48.383 | 0.00 | 0.000 |
| 260 | N261 | 718.191 | 47.719 | 0.00 | 0.000 |
| 261 | N262 | 718.188 | 45.165 | 0.00 | 0.000 |
| 262 | N263 | 718.184 | 43.355 | 0.00 | 0.000 |
| 263 | N264 | 718.183 | 40.476 | 0.25 | 0.000 |
| 264 | N265 | 718.319 | 46.859 | 0.00 | 0.000 |
| 265 | N266 | 718.315 | 45.382 | 0.00 | 0.000 |
| 266 | N267 | 718.311 | 43.466 | 0.00 | 0.000 |
| 267 | N268 | 718.308 | 41.804 | 0.00 | 0.000 |
| 268 | N269 | 718.305 | 38.296 | 0.25 | 0.000 |
| 269 | N270 | 717.773 | 63.884 | 0.00 | 0.000 |
| 270 | N271 | 717.769 | 64.144 | 0.00 | 0.000 |
| 271 | N272 | 717.764 | 64.424 | 0.00 | 0.000 |
| 272 | N273 | 717.760 | 64.689 | 0.00 | 0.000 |
| 273 | N274 | 717.755 | 65.192 | 0.00 | 0.000 |
| 274 | N275 | 717.750 | 65.679 | 0.00 | 0.000 |
| 275 | N276 | 717.744 | 66.089 | 0.00 | 0.000 |
| 276 | N277 | 717.739 | 66.053 | 0.00 | 0.000 |
| 277 | N278 | 717.731 | 66.115 | 0.15 | 0.000 |
| 278 | N279 | 717.730 | 66.222 | 0.00 | 0.000 |
| 279 | N280 | 717.729 | 66.054 | 0.00 | 0.000 |
| 280 | N281 | 717.729 | 65.808 | 0.00 | 0.000 |
| 281 | N282 | 717.728 | 65.446 | 0.00 | 0.000 |
| 282 | N283 | 717.727 | 65.291 | 0.00 | 0.000 |
| 283 | N284 | 717.727 | 65.237 | 0.00 | 0.000 |
| 284 | N285 | 717.726 | 64.402 | 0.00 | 0.000 |
| 285 | N286 | 717.725 | 63.284 | 0.00 | 0.000 |
| 286 | N287 | 717.725 | 63.074 | 0.00 | 0.000 |
| 287 | N288 | 717.724 | 61.278 | 0.00 | 0.000 |
| 288 | N289 | 717.724 | 60.036 | 0.00 | 0.000 |
| 289 | N290 | 717.723 | 58.636 | 0.00 | 0.000 |
| 290 | N291 | 717.722 | 57.959 | 0.00 | 0.000 |
| 291 | N292 | 717.721 | 56.147 | 0.20 | 0.000 |
| 292 | N293 | 717.730 | 66.114 | 0.00 | 0.000 |
| 293 | N294 | 717.729 | 65.578 | 0.00 | 0.000 |
| 294 | N295 | 717.728 | 64.880 | 0.00 | 0.000 |
| 295 | N296 | 717.727 | 64.125 | 0.00 | 0.000 |
| 296 | N297 | 717.726 | 63.348 | 0.00 | 0.000 |
| 297 | N298 | 717.725 | 62.154 | 0.00 | 0.000 |
| 298 | N299 | 717.724 | 60.349 | 0.00 | 0.000 |
| 299 | N300 | 717.723 | 59.679 | 0.00 | 0.000 |
| 300 | N301 | 717.722 | 59.317 | 0.00 | 0.000 |
| 301 | N302 | 717.721 | 59.451 | 0.00 | 0.000 |
| 302 | N303 | 717.720 | 59.980 | 0.00 | 0.000 |
| 303 | N304 | 717.719 | 60.111 | 0.00 | 0.000 |
| 304 | N305 | 717.718 | 59.632 | 0.15 | 0.000 |

## Pipes

| # | Name | Velocity (m/s) | Flow (L/s) | Losses (m/km) | Friction | Quality | Reaction rate (M/L/day) | Final status |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | P1 | 0.07 | -0.24 | 0.130 | 0.0401 | 0.000 | 0.0000 | Open |
| 2 | P2 | 0.07 | -0.24 | 0.123 | 0.0379 | 0.000 | 0.0000 | Open |
| 3 | P3 | 0.05 | -0.25 | 0.050 | 0.0343 | 0.000 | 0.0000 | Open |
| 4 | P4 | 0.05 | -0.27 | 0.062 | 0.0358 | 0.000 | 0.0000 | Open |
| 5 | P5 | 0.05 | -0.29 | 0.068 | 0.0361 | 0.000 | 0.0000 | Open |
| 6 | P6 | 0.05 | -0.29 | 0.073 | 0.0389 | 0.000 | 0.0000 | Open |
| 7 | P7 | 0.05 | -0.29 | 0.067 | 0.0359 | 0.000 | 0.0000 | Open |
| 8 | P8 | 0.05 | -0.29 | 0.071 | 0.0377 | 0.000 | 0.0000 | Open |
| 9 | P9 | 0.05 | -0.29 | 0.072 | 0.0384 | 0.000 | 0.0000 | Open |
| 10 | P10 | 0.05 | -0.29 | 0.070 | 0.0372 | 0.000 | 0.0000 | Open |
| 11 | P11 | 0.05 | -0.29 | 0.071 | 0.0378 | 0.000 | 0.0000 | Open |
| 12 | P12 | 0.05 | -0.29 | 0.072 | 0.0385 | 0.000 | 0.0000 | Open |
| 13 | P13 | 0.05 | -0.29 | 0.070 | 0.0374 | 0.000 | 0.0000 | Open |
| 14 | P14 | 0.05 | -0.29 | 0.070 | 0.0371 | 0.000 | 0.0000 | Open |
| 15 | P15 | 0.05 | -0.29 | 0.074 | 0.0392 | 0.000 | 0.0000 | Open |
| 16 | P16 | 0.05 | -0.29 | 0.071 | 0.0379 | 0.000 | 0.0000 | Open |
| 17 | P17 | 0.10 | -0.52 | 0.237 | 0.0374 | 0.000 | 0.0000 | Open |
| 18 | P18 | 0.14 | -0.75 | 0.449 | 0.0346 | 0.000 | 0.0000 | Open |
| 19 | P19 | 0.14 | -0.75 | 0.451 | 0.0347 | 0.000 | 0.0000 | Open |
| 20 | P20 | 0.14 | -0.75 | 0.449 | 0.0346 | 0.000 | 0.0000 | Open |
| 21 | P21 | 0.14 | -0.75 | 0.447 | 0.0344 | 0.000 | 0.0000 | Open |
| 22 | P22 | 0.14 | -0.75 | 0.452 | 0.0348 | 0.000 | 0.0000 | Open |
| 23 | P23 | 0.14 | -0.75 | 0.448 | 0.0345 | 0.000 | 0.0000 | Open |
| 24 | P24 | 0.14 | -0.75 | 0.449 | 0.0345 | 0.000 | 0.0000 | Open |
| 25 | P25 | 0.15 | -0.79 | 0.496 | 0.0341 | 0.000 | 0.0000 | Open |
| 26 | P26 | 0.15 | -0.79 | 0.495 | 0.0341 | 0.000 | 0.0000 | Open |
| 27 | P27 | 0.15 | -0.79 | 0.494 | 0.0340 | 0.000 | 0.0000 | Open |
| 28 | P28 | 0.11 | -0.56 | 0.267 | 0.0373 | 0.000 | 0.0000 | Open |
| 29 | P29 | 0.11 | -0.56 | 0.266 | 0.0372 | 0.000 | 0.0000 | Open |
| 30 | P30 | 0.11 | -0.56 | 0.263 | 0.0368 | 0.000 | 0.0000 | Open |
| 31 | P31 | 0.11 | -0.56 | 0.270 | 0.0378 | 0.000 | 0.0000 | Open |
| 32 | P32 | 0.15 | -0.79 | 0.496 | 0.0341 | 0.000 | 0.0000 | Open |
| 33 | P33 | 0.15 | -0.79 | 0.495 | 0.0341 | 0.000 | 0.0000 | Open |
| 34 | P34 | 0.26 | -1.35 | 1.283 | 0.0305 | 0.000 | 0.0000 | Open |
| 35 | P35 | 0.26 | -1.35 | 1.289 | 0.0306 | 0.000 | 0.0000 | Open |
| 36 | P36 | 0.26 | -1.34 | 1.271 | 0.0305 | 0.000 | 0.0000 | Open |
| 37 | P37 | 0.25 | -1.32 | 1.239 | 0.0306 | 0.000 | 0.0000 | Open |
| 38 | P38 | 0.25 | -1.32 | 1.240 | 0.0306 | 0.000 | 0.0000 | Open |
| 39 | P39 | 0.25 | -1.32 | 1.240 | 0.0306 | 0.000 | 0.0000 | Open |
| 40 | P40 | 0.25 | -1.32 | 1.242 | 0.0307 | 0.000 | 0.0000 | Open |
| 41 | P41 | 0.25 | -1.32 | 1.241 | 0.0307 | 0.000 | 0.0000 | Open |
| 42 | P42 | 0.25 | -1.32 | 1.239 | 0.0306 | 0.000 | 0.0000 | Open |
| 43 | P43 | 0.09 | -0.45 | 0.180 | 0.0389 | 0.000 | 0.0000 | Open |
| 44 | P44 | 0.35 | -1.82 | 2.223 | 0.0289 | 0.000 | 0.0000 | Open |
| 45 | P45 | 0.37 | -1.91 | 2.412 | 0.0287 | 0.000 | 0.0000 | Open |
| 46 | P46 | 0.37 | -1.91 | 2.410 | 0.0287 | 0.000 | 0.0000 | Open |
| 47 | P47 | 0.41 | -2.16 | 3.023 | 0.0281 | 0.000 | 0.0000 | Open |
| 48 | P48 | 0.47 | -2.45 | 3.813 | 0.0276 | 0.000 | 0.0000 | Open |
| 49 | P49 | 0.52 | -2.70 | 4.565 | 0.0272 | 0.000 | 0.0000 | Open |
| 50 | P50 | 0.71 | -3.70 | 8.253 | 0.0261 | 0.000 | 0.0000 | Open |
| 51 | P51 | 0.71 | -3.70 | 8.255 | 0.0261 | 0.000 | 0.0000 | Open |
| 52 | P52 | 0.71 | -3.70 | 8.257 | 0.0261 | 0.000 | 0.0000 | Open |
| 53 | P53 | 0.73 | -3.80 | 8.677 | 0.0260 | 0.000 | 0.0000 | Open |
| 54 | P54 | 0.73 | -3.80 | 8.679 | 0.0260 | 0.000 | 0.0000 | Open |
| 55 | P55 | 0.73 | -3.80 | 8.677 | 0.0260 | 0.000 | 0.0000 | Open |
| 56 | P56 | 0.73 | -3.80 | 8.678 | 0.0260 | 0.000 | 0.0000 | Open |
| 57 | P57 | 0.75 | -3.90 | 9.113 | 0.0259 | 0.000 | 0.0000 | Open |
| 58 | P58 | 0.75 | -3.90 | 9.113 | 0.0259 | 0.000 | 0.0000 | Open |
| 59 | P59 | 0.75 | -3.90 | 9.110 | 0.0259 | 0.000 | 0.0000 | Open |
| 60 | P60 | 0.75 | -3.90 | 9.115 | 0.0259 | 0.000 | 0.0000 | Open |
| 61 | P61 | 0.75 | -3.90 | 9.111 | 0.0259 | 0.000 | 0.0000 | Open |
| 62 | P62 | 0.75 | -3.90 | 9.116 | 0.0259 | 0.000 | 0.0000 | Open |
| 63 | P63 | 0.75 | -3.90 | 9.112 | 0.0259 | 0.000 | 0.0000 | Open |
| 64 | P64 | 0.77 | -4.00 | 9.558 | 0.0258 | 0.000 | 0.0000 | Open |
| 65 | P65 | 0.77 | -4.00 | 9.556 | 0.0258 | 0.000 | 0.0000 | Open |
| 66 | P66 | 0.77 | -4.00 | 9.559 | 0.0259 | 0.000 | 0.0000 | Open |
| 67 | P67 | 0.77 | -4.00 | 9.557 | 0.0258 | 0.000 | 0.0000 | Open |
| 68 | P68 | 0.77 | -4.00 | 9.557 | 0.0258 | 0.000 | 0.0000 | Open |
| 69 | P69 | 0.77 | -4.00 | 9.555 | 0.0258 | 0.000 | 0.0000 | Open |
| 70 | P70 | 0.77 | -4.00 | 9.560 | 0.0259 | 0.000 | 0.0000 | Open |
| 71 | P71 | 0.77 | -4.00 | 9.558 | 0.0258 | 0.000 | 0.0000 | Open |
| 72 | P72 | 0.77 | -4.00 | 9.555 | 0.0258 | 0.000 | 0.0000 | Open |
| 73 | P73 | 0.79 | -4.10 | 10.016 | 0.0258 | 0.000 | 0.0000 | Open |
| 74 | P74 | 0.79 | -4.10 | 10.012 | 0.0258 | 0.000 | 0.0000 | Open |
| 75 | P75 | 0.79 | -4.10 | 10.012 | 0.0258 | 0.000 | 0.0000 | Open |
| 76 | P76 | 0.79 | -4.10 | 10.011 | 0.0258 | 0.000 | 0.0000 | Open |
| 77 | P77 | 0.79 | -4.10 | 10.015 | 0.0258 | 0.000 | 0.0000 | Open |
| 78 | P78 | 0.81 | -4.20 | 10.475 | 0.0257 | 0.000 | 0.0000 | Open |
| 79 | P79 | 0.81 | -4.20 | 10.478 | 0.0257 | 0.000 | 0.0000 | Open |
| 80 | P80 | 0.81 | -4.20 | 10.477 | 0.0257 | 0.000 | 0.0000 | Open |
| 81 | P81 | 0.81 | -4.20 | 10.482 | 0.0257 | 0.000 | 0.0000 | Open |
| 82 | P82 | 0.81 | -4.20 | 10.475 | 0.0257 | 0.000 | 0.0000 | Open |
| 83 | P83 | 0.81 | -4.20 | 10.482 | 0.0257 | 0.000 | 0.0000 | Open |
| 84 | P84 | 0.81 | -4.20 | 10.476 | 0.0257 | 0.000 | 0.0000 | Open |
| 85 | P85 | 0.81 | -4.20 | 10.478 | 0.0257 | 0.000 | 0.0000 | Open |
| 86 | P86 | 0.81 | -4.20 | 10.478 | 0.0257 | 0.000 | 0.0000 | Open |
| 87 | P87 | 0.81 | -4.20 | 10.474 | 0.0257 | 0.000 | 0.0000 | Open |
| 88 | P88 | 0.81 | -4.20 | 10.480 | 0.0257 | 0.000 | 0.0000 | Open |
| 89 | P89 | 0.01 | 0.02 | 0.008 | 0.2462 | 0.000 | 0.0000 | Open |
| 90 | P90 | 0.01 | 0.02 | 0.007 | 0.2217 | 0.000 | 0.0000 | Open |
| 91 | P91 | 0.01 | 0.02 | 0.007 | 0.2306 | 0.000 | 0.0000 | Open |
| 92 | P92 | 0.01 | 0.02 | 0.006 | 0.1992 | 0.000 | 0.0000 | Open |
| 93 | P93 | 0.01 | 0.02 | 0.004 | 0.1342 | 0.000 | 0.0000 | Open |
| 94 | P94 | 0.01 | 0.02 | 0.008 | 0.2360 | 0.000 | 0.0000 | Open |
| 95 | P95 | 0.01 | 0.02 | 0.004 | 0.1280 | 0.000 | 0.0000 | Open |
| 96 | P96 | 0.01 | 0.02 | 0.008 | 0.2424 | 0.000 | 0.0000 | Open |
| 97 | P97 | 0.01 | 0.02 | 0.005 | 0.1538 | 0.000 | 0.0000 | Open |
| 98 | P98 | 0.06 | -0.23 | 0.106 | 0.0360 | 0.000 | 0.0000 | Open |
| 99 | P99 | 0.06 | -0.23 | 0.108 | 0.0366 | 0.000 | 0.0000 | Open |
| 100 | P100 | 0.06 | -0.23 | 0.106 | 0.0360 | 0.000 | 0.0000 | Open |
| 101 | P101 | 0.06 | -0.23 | 0.110 | 0.0372 | 0.000 | 0.0000 | Open |
| 102 | P102 | 0.06 | -0.23 | 0.105 | 0.0355 | 0.000 | 0.0000 | Open |
| 103 | P103 | 0.06 | -0.23 | 0.108 | 0.0364 | 0.000 | 0.0000 | Open |
| 104 | P104 | 0.06 | -0.23 | 0.110 | 0.0371 | 0.000 | 0.0000 | Open |
| 105 | P105 | 0.06 | -0.23 | 0.108 | 0.0366 | 0.000 | 0.0000 | Open |
| 106 | P106 | 0.06 | -0.23 | 0.105 | 0.0355 | 0.000 | 0.0000 | Open |
| 107 | P107 | 0.06 | -0.23 | 0.108 | 0.0365 | 0.000 | 0.0000 | Open |
| 108 | P108 | 0.00 | 0.01 | 0.004 | 0.5532 | 0.000 | 0.0000 | Open |
| 109 | P109 | 0.00 | 0.01 | 0.006 | 0.7526 | 0.000 | 0.0000 | Open |
| 110 | P110 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 111 | P111 | 0.00 | 0.01 | 0.004 | 0.4959 | 0.000 | 0.0000 | Open |
| 112 | P112 | 0.00 | 0.01 | 0.004 | 0.5601 | 0.000 | 0.0000 | Open |
| 113 | P113 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 114 | P114 | 0.00 | 0.01 | 0.004 | 0.5825 | 0.000 | 0.0000 | Open |
| 115 | P115 | 0.00 | 0.01 | 0.005 | 0.6382 | 0.000 | 0.0000 | Open |
| 116 | P116 | 0.00 | 0.01 | 0.004 | 0.5627 | 0.000 | 0.0000 | Open |
| 117 | P117 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 118 | P118 | 0.00 | 0.01 | 0.005 | 0.6712 | 0.000 | 0.0000 | Open |
| 119 | P119 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 120 | P120 | 0.00 | 0.01 | 0.006 | 0.8611 | 0.000 | 0.0000 | Open |
| 121 | P121 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 122 | P122 | 0.00 | 0.01 | 0.007 | 0.8944 | 0.000 | 0.0000 | Open |
| 123 | P123 | 0.00 | 0.01 | 0.004 | 0.5843 | 0.000 | 0.0000 | Open |
| 124 | P124 | 0.07 | -0.24 | 0.130 | 0.0395 | 0.000 | 0.0000 | Open |
| 125 | P125 | 0.07 | -0.24 | 0.125 | 0.0380 | 0.000 | 0.0000 | Open |
| 126 | P126 | 0.07 | -0.24 | 0.124 | 0.0378 | 0.000 | 0.0000 | Open |
| 127 | P127 | 0.07 | -0.24 | 0.130 | 0.0397 | 0.000 | 0.0000 | Open |
| 128 | P128 | 0.07 | -0.24 | 0.121 | 0.0368 | 0.000 | 0.0000 | Open |
| 129 | P129 | 0.07 | -0.24 | 0.130 | 0.0397 | 0.000 | 0.0000 | Open |
| 130 | P130 | 0.07 | -0.24 | 0.124 | 0.0377 | 0.000 | 0.0000 | Open |
| 131 | P131 | 0.07 | -0.24 | 0.126 | 0.0385 | 0.000 | 0.0000 | Open |
| 132 | P132 | 0.07 | -0.24 | 0.125 | 0.0381 | 0.000 | 0.0000 | Open |
| 133 | P133 | 0.07 | -0.24 | 0.128 | 0.0389 | 0.000 | 0.0000 | Open |
| 134 | P134 | 0.07 | -0.24 | 0.129 | 0.0393 | 0.000 | 0.0000 | Open |
| 135 | P135 | 0.07 | 0.25 | 0.143 | 0.0397 | 0.000 | 0.0000 | Open |
| 136 | P136 | 0.07 | 0.25 | 0.142 | 0.0393 | 0.000 | 0.0000 | Open |
| 137 | P137 | 0.07 | 0.25 | 0.148 | 0.0411 | 0.000 | 0.0000 | Open |
| 138 | P138 | 0.07 | 0.25 | 0.143 | 0.0397 | 0.000 | 0.0000 | Open |
| 139 | P139 | 0.07 | 0.25 | 0.145 | 0.0402 | 0.000 | 0.0000 | Open |
| 140 | P140 | 0.07 | 0.25 | 0.150 | 0.0416 | 0.000 | 0.0000 | Open |
| 141 | P141 | 0.07 | 0.25 | 0.142 | 0.0395 | 0.000 | 0.0000 | Open |
| 142 | P142 | 0.07 | 0.25 | 0.146 | 0.0405 | 0.000 | 0.0000 | Open |
| 143 | P143 | 0.07 | 0.25 | 0.147 | 0.0407 | 0.000 | 0.0000 | Open |
| 144 | P144 | 0.07 | 0.25 | 0.143 | 0.0397 | 0.000 | 0.0000 | Open |
| 145 | P145 | 0.07 | 0.25 | 0.144 | 0.0401 | 0.000 | 0.0000 | Open |
| 146 | P146 | 0.07 | 0.25 | 0.146 | 0.0405 | 0.000 | 0.0000 | Open |
| 147 | P147 | 0.07 | 0.25 | 0.145 | 0.0402 | 0.000 | 0.0000 | Open |
| 148 | P148 | 0.07 | 0.25 | 0.144 | 0.0401 | 0.000 | 0.0000 | Open |
| 149 | P149 | 0.07 | 0.25 | 0.146 | 0.0405 | 0.000 | 0.0000 | Open |
| 150 | P150 | 0.07 | 0.25 | 0.145 | 0.0402 | 0.000 | 0.0000 | Open |
| 151 | P151 | 0.07 | 0.25 | 0.143 | 0.0396 | 0.000 | 0.0000 | Open |
| 152 | P152 | 0.07 | 0.25 | 0.148 | 0.0411 | 0.000 | 0.0000 | Open |
| 153 | P153 | 0.07 | 0.25 | 0.145 | 0.0402 | 0.000 | 0.0000 | Open |
| 154 | P154 | 0.07 | 0.25 | 0.144 | 0.0398 | 0.000 | 0.0000 | Open |
| 155 | P155 | 0.01 | 0.04 | 0.014 | 0.1299 | 0.000 | 0.0000 | Open |
| 156 | P156 | 0.01 | 0.04 | 0.008 | 0.0791 | 0.000 | 0.0000 | Open |
| 157 | P157 | 0.01 | 0.04 | 0.014 | 0.1330 | 0.000 | 0.0000 | Open |
| 158 | P158 | 0.01 | 0.04 | 0.009 | 0.0902 | 0.000 | 0.0000 | Open |
| 159 | P159 | 0.01 | 0.04 | 0.009 | 0.0875 | 0.000 | 0.0000 | Open |
| 160 | P160 | 0.01 | 0.04 | 0.010 | 0.0958 | 0.000 | 0.0000 | Open |
| 161 | P161 | 0.01 | 0.04 | 0.013 | 0.1264 | 0.000 | 0.0000 | Open |
| 162 | P162 | 0.01 | 0.04 | 0.012 | 0.1106 | 0.000 | 0.0000 | Open |
| 163 | P163 | 0.01 | 0.04 | 0.008 | 0.0782 | 0.000 | 0.0000 | Open |
| 164 | P164 | 0.01 | 0.04 | 0.012 | 0.1150 | 0.000 | 0.0000 | Open |
| 165 | P165 | 0.01 | 0.04 | 0.010 | 0.0947 | 0.000 | 0.0000 | Open |
| 166 | P166 | 0.01 | 0.04 | 0.014 | 0.1317 | 0.000 | 0.0000 | Open |
| 167 | P167 | 0.01 | 0.04 | 0.009 | 0.0855 | 0.000 | 0.0000 | Open |
| 168 | P168 | 0.01 | 0.04 | 0.012 | 0.1107 | 0.000 | 0.0000 | Open |
| 169 | P169 | 0.01 | 0.04 | 0.009 | 0.0811 | 0.000 | 0.0000 | Open |
| 170 | P170 | 0.01 | 0.04 | 0.014 | 0.1327 | 0.000 | 0.0000 | Open |
| 171 | P171 | 0.01 | 0.04 | 0.010 | 0.0952 | 0.000 | 0.0000 | Open |
| 172 | P172 | 0.01 | 0.04 | 0.013 | 0.1224 | 0.000 | 0.0000 | Open |
| 173 | P173 | 0.01 | 0.04 | 0.009 | 0.0856 | 0.000 | 0.0000 | Open |
| 174 | P174 | 0.01 | 0.04 | 0.011 | 0.1078 | 0.000 | 0.0000 | Open |
| 175 | P175 | 0.09 | -0.46 | 0.189 | 0.0391 | 0.000 | 0.0000 | Open |
| 176 | P176 | 0.09 | -0.46 | 0.189 | 0.0392 | 0.000 | 0.0000 | Open |
| 177 | P177 | 0.09 | -0.46 | 0.188 | 0.0389 | 0.000 | 0.0000 | Open |
| 178 | P178 | 0.09 | -0.46 | 0.189 | 0.0392 | 0.000 | 0.0000 | Open |
| 179 | P179 | 0.09 | -0.46 | 0.193 | 0.0399 | 0.000 | 0.0000 | Open |
| 180 | P180 | 0.09 | -0.46 | 0.189 | 0.0391 | 0.000 | 0.0000 | Open |
| 181 | P181 | 0.09 | -0.46 | 0.188 | 0.0389 | 0.000 | 0.0000 | Open |
| 182 | P182 | 0.09 | -0.46 | 0.189 | 0.0390 | 0.000 | 0.0000 | Open |
| 183 | P183 | 0.09 | -0.46 | 0.189 | 0.0390 | 0.000 | 0.0000 | Open |
| 184 | P184 | 0.09 | -0.46 | 0.188 | 0.0390 | 0.000 | 0.0000 | Open |
| 185 | P185 | 0.09 | -0.46 | 0.190 | 0.0394 | 0.000 | 0.0000 | Open |
| 186 | P186 | 0.09 | -0.46 | 0.190 | 0.0394 | 0.000 | 0.0000 | Open |
| 187 | P187 | 0.09 | -0.46 | 0.190 | 0.0393 | 0.000 | 0.0000 | Open |
| 188 | P188 | 0.09 | -0.46 | 0.188 | 0.0389 | 0.000 | 0.0000 | Open |
| 189 | P189 | 0.09 | -0.46 | 0.190 | 0.0392 | 0.000 | 0.0000 | Open |
| 190 | P190 | 0.09 | -0.46 | 0.188 | 0.0388 | 0.000 | 0.0000 | Open |
| 191 | P191 | 0.09 | -0.46 | 0.191 | 0.0395 | 0.000 | 0.0000 | Open |
| 192 | P192 | 0.09 | -0.46 | 0.190 | 0.0392 | 0.000 | 0.0000 | Open |
| 193 | P193 | 0.24 | -0.88 | 1.443 | 0.0326 | 0.000 | 0.0000 | Open |
| 194 | P194 | 0.24 | -0.88 | 1.439 | 0.0325 | 0.000 | 0.0000 | Open |
| 195 | P195 | 0.29 | -1.04 | 1.981 | 0.0315 | 0.000 | 0.0000 | Open |
| 196 | P196 | 0.29 | -1.04 | 1.981 | 0.0315 | 0.000 | 0.0000 | Open |
| 197 | P197 | 0.29 | -1.04 | 1.979 | 0.0315 | 0.000 | 0.0000 | Open |
| 198 | P198 | 0.21 | -0.75 | 1.102 | 0.0336 | 0.000 | 0.0000 | Open |
| 199 | P199 | 0.28 | -1.00 | 1.848 | 0.0318 | 0.000 | 0.0000 | Open |
| 200 | P200 | 0.28 | -1.00 | 1.847 | 0.0317 | 0.000 | 0.0000 | Open |
| 201 | P201 | 0.28 | -1.00 | 1.846 | 0.0317 | 0.000 | 0.0000 | Open |
| 202 | P202 | 0.28 | -1.00 | 1.845 | 0.0317 | 0.000 | 0.0000 | Open |
| 203 | P203 | 0.28 | -1.00 | 1.845 | 0.0317 | 0.000 | 0.0000 | Open |
| 204 | P204 | 0.28 | -1.00 | 1.846 | 0.0317 | 0.000 | 0.0000 | Open |
| 205 | P205 | 0.08 | -0.29 | 0.205 | 0.0423 | 0.000 | 0.0000 | Open |
| 206 | P206 | 0.08 | -0.29 | 0.205 | 0.0424 | 0.000 | 0.0000 | Open |
| 207 | P207 | 0.08 | -0.29 | 0.206 | 0.0426 | 0.000 | 0.0000 | Open |
| 208 | P208 | 0.08 | -0.29 | 0.205 | 0.0423 | 0.000 | 0.0000 | Open |
| 209 | P209 | 0.08 | -0.29 | 0.211 | 0.0436 | 0.000 | 0.0000 | Open |
| 210 | P210 | 0.05 | 0.17 | 0.046 | 0.0284 | 0.000 | 0.0000 | Open |
| 211 | P211 | 0.05 | 0.17 | 0.046 | 0.0281 | 0.000 | 0.0000 | Open |
| 212 | P212 | 0.05 | 0.17 | 0.051 | 0.0313 | 0.000 | 0.0000 | Open |
| 213 | P213 | 0.07 | -0.25 | 0.146 | 0.0405 | 0.000 | 0.0000 | Open |
| 214 | P214 | 0.07 | -0.25 | 0.144 | 0.0400 | 0.000 | 0.0000 | Open |
| 215 | P215 | 0.07 | -0.25 | 0.146 | 0.0404 | 0.000 | 0.0000 | Open |
| 216 | P216 | 0.07 | -0.24 | 0.124 | 0.0385 | 0.000 | 0.0000 | Open |
| 217 | P217 | 0.07 | -0.24 | 0.129 | 0.0398 | 0.000 | 0.0000 | Open |
| 218 | P218 | 0.07 | -0.24 | 0.124 | 0.0384 | 0.000 | 0.0000 | Open |
| 219 | P219 | 0.07 | -0.24 | 0.125 | 0.0388 | 0.000 | 0.0000 | Open |
| 220 | P220 | 0.07 | -0.24 | 0.120 | 0.0372 | 0.000 | 0.0000 | Open |
| 221 | P221 | 0.07 | -0.24 | 0.122 | 0.0377 | 0.000 | 0.0000 | Open |
| 222 | P222 | 0.07 | -0.24 | 0.124 | 0.0384 | 0.000 | 0.0000 | Open |
| 223 | P223 | 0.07 | -0.24 | 0.124 | 0.0384 | 0.000 | 0.0000 | Open |
| 224 | P224 | 0.07 | -0.24 | 0.124 | 0.0385 | 0.000 | 0.0000 | Open |
| 225 | P225 | 0.07 | -0.24 | 0.121 | 0.0375 | 0.000 | 0.0000 | Open |
| 226 | P226 | 0.07 | -0.24 | 0.130 | 0.0404 | 0.000 | 0.0000 | Open |
| 227 | P227 | 0.03 | -0.10 | 0.026 | 0.0453 | 0.000 | 0.0000 | Open |
| 228 | P228 | 0.03 | -0.10 | 0.025 | 0.0440 | 0.000 | 0.0000 | Open |
| 229 | P229 | 0.03 | -0.10 | 0.028 | 0.0490 | 0.000 | 0.0000 | Open |
| 230 | P230 | 0.01 | -0.02 | 0.006 | 0.3228 | 0.000 | 0.0000 | Open |
| 231 | P231 | 0.01 | -0.02 | 0.005 | 0.2296 | 0.000 | 0.0000 | Open |
| 232 | P232 | 0.01 | -0.02 | 0.005 | 0.2377 | 0.000 | 0.0000 | Open |
| 233 | P233 | 0.01 | -0.02 | 0.004 | 0.1929 | 0.000 | 0.0000 | Open |
| 234 | P234 | 0.22 | -0.78 | 1.166 | 0.0335 | 0.000 | 0.0000 | Open |
| 235 | P235 | 0.22 | -0.78 | 1.158 | 0.0333 | 0.000 | 0.0000 | Open |
| 236 | P236 | 0.22 | -0.78 | 1.164 | 0.0335 | 0.000 | 0.0000 | Open |
| 237 | P237 | 0.38 | -1.38 | 3.276 | 0.0300 | 0.000 | 0.0000 | Open |
| 238 | P238 | 0.38 | -1.38 | 3.277 | 0.0300 | 0.000 | 0.0000 | Open |
| 239 | P239 | 0.14 | 0.50 | 0.532 | 0.0369 | 0.000 | 0.0000 | Open |
| 240 | P240 | 0.14 | 0.50 | 0.534 | 0.0370 | 0.000 | 0.0000 | Open |
| 241 | P241 | 0.14 | 0.50 | 0.530 | 0.0368 | 0.000 | 0.0000 | Open |
| 242 | P242 | 0.07 | 0.25 | 0.145 | 0.0401 | 0.000 | 0.0000 | Open |
| 243 | P243 | 0.07 | 0.25 | 0.145 | 0.0401 | 0.000 | 0.0000 | Open |
| 244 | P244 | 0.07 | 0.25 | 0.145 | 0.0401 | 0.000 | 0.0000 | Open |
| 245 | P245 | 0.07 | 0.25 | 0.145 | 0.0404 | 0.000 | 0.0000 | Open |
| 246 | P246 | 0.07 | 0.25 | 0.147 | 0.0407 | 0.000 | 0.0000 | Open |
| 247 | P247 | 0.07 | 0.25 | 0.141 | 0.0390 | 0.000 | 0.0000 | Open |
| 248 | P248 | 0.14 | 0.51 | 0.542 | 0.0365 | 0.000 | 0.0000 | Open |
| 249 | P249 | 0.14 | 0.51 | 0.549 | 0.0369 | 0.000 | 0.0000 | Open |
| 250 | P250 | 0.07 | 0.26 | 0.157 | 0.0410 | 0.000 | 0.0000 | Open |
| 251 | P251 | 0.07 | 0.26 | 0.160 | 0.0418 | 0.000 | 0.0000 | Open |
| 252 | P252 | 0.07 | 0.26 | 0.160 | 0.0417 | 0.000 | 0.0000 | Open |
| 253 | P253 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 254 | P254 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 255 | P255 | 0.00 | 0.01 | 0.004 | 1.0467 | 0.000 | 0.0000 | Open |
| 256 | P256 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 257 | P257 | 0.00 | 0.01 | 0.000 | 0.0000 | 0.000 | 0.0000 | Open |
| 258 | P258 | 0.07 | 0.25 | 0.142 | 0.0395 | 0.000 | 0.0000 | Open |
| 259 | P259 | 0.07 | 0.25 | 0.148 | 0.0410 | 0.000 | 0.0000 | Open |
| 260 | P260 | 0.07 | 0.25 | 0.144 | 0.0399 | 0.000 | 0.0000 | Open |
| 261 | P261 | 0.07 | 0.25 | 0.143 | 0.0396 | 0.000 | 0.0000 | Open |
| 262 | P262 | 0.07 | 0.25 | 0.145 | 0.0401 | 0.000 | 0.0000 | Open |
| 263 | P263 | 0.07 | 0.25 | 0.146 | 0.0406 | 0.000 | 0.0000 | Open |
| 264 | P264 | 0.07 | 0.25 | 0.144 | 0.0399 | 0.000 | 0.0000 | Open |
| 265 | P265 | 0.07 | 0.25 | 0.144 | 0.0401 | 0.000 | 0.0000 | Open |
| 266 | P266 | 0.07 | 0.25 | 0.147 | 0.0409 | 0.000 | 0.0000 | Open |
| 267 | P267 | 0.07 | 0.25 | 0.146 | 0.0404 | 0.000 | 0.0000 | Open |
| 268 | P268 | 0.07 | 0.25 | 0.143 | 0.0396 | 0.000 | 0.0000 | Open |
| 269 | P269 | 0.07 | 0.25 | 0.146 | 0.0404 | 0.000 | 0.0000 | Open |
| 270 | P270 | 0.07 | 0.25 | 0.147 | 0.0407 | 0.000 | 0.0000 | Open |
| 271 | P271 | 0.07 | 0.25 | 0.144 | 0.0400 | 0.000 | 0.0000 | Open |
| 272 | P272 | 0.07 | 0.25 | 0.145 | 0.0403 | 0.000 | 0.0000 | Open |
| 273 | P273 | 0.07 | 0.25 | 0.145 | 0.0403 | 0.000 | 0.0000 | Open |
| 274 | P274 | 0.07 | 0.25 | 0.145 | 0.0403 | 0.000 | 0.0000 | Open |
| 275 | P275 | 0.07 | 0.25 | 0.147 | 0.0407 | 0.000 | 0.0000 | Open |
| 276 | P276 | 0.07 | 0.25 | 0.143 | 0.0397 | 0.000 | 0.0000 | Open |
| 277 | P277 | 0.07 | 0.25 | 0.146 | 0.0404 | 0.000 | 0.0000 | Open |
| 278 | P278 | 0.10 | 0.50 | 0.221 | 0.0382 | 0.000 | 0.0000 | Open |
| 279 | P279 | 0.10 | 0.50 | 0.221 | 0.0382 | 0.000 | 0.0000 | Open |
| 280 | P280 | 0.10 | 0.50 | 0.221 | 0.0382 | 0.000 | 0.0000 | Open |
| 281 | P281 | 0.10 | 0.50 | 0.219 | 0.0380 | 0.000 | 0.0000 | Open |
| 282 | P282 | 0.10 | 0.50 | 0.220 | 0.0381 | 0.000 | 0.0000 | Open |
| 283 | P283 | 0.10 | 0.50 | 0.222 | 0.0384 | 0.000 | 0.0000 | Open |
| 284 | P284 | 0.10 | 0.50 | 0.221 | 0.0382 | 0.000 | 0.0000 | Open |
| 285 | P285 | 0.10 | 0.50 | 0.221 | 0.0383 | 0.000 | 0.0000 | Open |
| 286 | P286 | 0.10 | 0.50 | 0.220 | 0.0381 | 0.000 | 0.0000 | Open |
| 287 | P287 | 0.04 | 0.20 | 0.027 | 0.0287 | 0.000 | 0.0000 | Open |
| 288 | P288 | 0.04 | 0.20 | 0.026 | 0.0286 | 0.000 | 0.0000 | Open |
| 289 | P289 | 0.04 | 0.20 | 0.029 | 0.0314 | 0.000 | 0.0000 | Open |
| 290 | P290 | 0.04 | 0.20 | 0.026 | 0.0277 | 0.000 | 0.0000 | Open |
| 291 | P291 | 0.04 | 0.20 | 0.028 | 0.0299 | 0.000 | 0.0000 | Open |
| 292 | P292 | 0.04 | 0.20 | 0.028 | 0.0305 | 0.000 | 0.0000 | Open |
| 293 | P293 | 0.04 | 0.20 | 0.026 | 0.0279 | 0.000 | 0.0000 | Open |
| 294 | P294 | 0.04 | 0.20 | 0.027 | 0.0288 | 0.000 | 0.0000 | Open |
| 295 | P295 | 0.04 | 0.20 | 0.028 | 0.0302 | 0.000 | 0.0000 | Open |
| 296 | P296 | 0.04 | 0.20 | 0.028 | 0.0302 | 0.000 | 0.0000 | Open |
| 297 | P297 | 0.04 | 0.20 | 0.025 | 0.0276 | 0.000 | 0.0000 | Open |
| 298 | P298 | 0.04 | 0.20 | 0.027 | 0.0288 | 0.000 | 0.0000 | Open |
| 299 | P299 | 0.04 | 0.20 | 0.027 | 0.0289 | 0.000 | 0.0000 | Open |
| 300 | P300 | 0.04 | 0.20 | 0.028 | 0.0301 | 0.000 | 0.0000 | Open |
| 301 | P301 | 0.04 | 0.15 | 0.040 | 0.0305 | 0.000 | 0.0000 | Open |
| 302 | P302 | 0.04 | 0.15 | 0.038 | 0.0295 | 0.000 | 0.0000 | Open |
| 303 | P303 | 0.04 | 0.15 | 0.042 | 0.0327 | 0.000 | 0.0000 | Open |
| 304 | P304 | 0.04 | 0.15 | 0.038 | 0.0296 | 0.000 | 0.0000 | Open |
| 305 | P305 | 0.04 | 0.15 | 0.040 | 0.0311 | 0.000 | 0.0000 | Open |
| 306 | P306 | 0.04 | 0.15 | 0.039 | 0.0297 | 0.000 | 0.0000 | Open |
| 307 | P307 | 0.04 | 0.15 | 0.041 | 0.0314 | 0.000 | 0.0000 | Open |
| 308 | P308 | 0.04 | 0.15 | 0.040 | 0.0305 | 0.000 | 0.0000 | Open |
| 309 | P309 | 0.04 | 0.15 | 0.040 | 0.0311 | 0.000 | 0.0000 | Open |
| 310 | P310 | 0.04 | 0.15 | 0.041 | 0.0316 | 0.000 | 0.0000 | Open |
| 311 | P311 | 0.04 | 0.15 | 0.037 | 0.0286 | 0.000 | 0.0000 | Open |
| 312 | P312 | 0.04 | 0.15 | 0.042 | 0.0324 | 0.000 | 0.0000 | Open |
| 313 | P313 | 0.04 | 0.15 | 0.040 | 0.0305 | 0.000 | 0.0000 | Open |

## Reservoirs

| # | Name | Pressure elevation (m) | Pressure height (m) | Net Inflow (L/s) | Quality |
| --- | --- | --- | --- | --- | --- |
| 1 | N90 | 724.5 | 0 | -4.2 | 0 |